## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Proposal for SRMM General Requirements in Technical Guidance Document]
Date Submitted: [6 May, 2015]
Source: [Hidetoshi Yokota] Company [Landis&Gyr]
Address [1-2-9 Nishi Shimbashi Minato-ku, Tokyo 105-0003, Japan]
Voice:[+81 3-5532-7455], FAX: [+81 3-5532-7519], E-Mail:[hidetoshi.yokota@landisgyr.com]
Re: [“TG4s Technical Guidance Document”, IEEE 802.15-14-0555-04-004s]
Abstract: [This contribution proposes general requirements that should be considered in the Technical Guidance Document in order to apply Spectrum Resource Management in the field of AMI (Advanced Metering Infrastructure).]
Purpose: [Discussion and approval]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
Proposal for SRMM General Requirements in Technical Guidance Document
Authors:

## Slide 3: General requirements
Support of active and passive link measurements
  Link measurement request/report for instantaneous SRM (active)
  Cumulative SRMM information request/report for averaged SRM (passive)
  Equivalent functionality is supported in 802.11k RRM
Support of advance SRMM information retrieval
  SRM information IE in the beacon frame could help a device select optimal PAN
  Equivalent functionality is supported in 802.11k RRM

## Slide 4: General requirements (cont’d)
Support of multihop mesh topology
AP
STA
request
report
802.11 WLAN
802.15 WPAN
PAN
request
report
Target device
Relay device
(FFD)
STA
request
report
Requesting device
(PAN Coordinator)

## Slide 5: General requirements (cont’d)
Support of piggyback report
  Could reduce the number of request/report packets
  Could correlation of measurements on the path more easily
  Specific flag should be defined
N0
N3
request
Report (M3|M2|M1)
Target device
N2
N1
request
request
Report (M3| M2)
Report (M3)
measurement
measurement
measurement
M3
M2
M1

## Slide 6: Proposal for General descriptions (Section 4)
4 General descriptions
  4.2 General requirement of SRMM
    A device should be able to request another device to conduct spectrum resource measurements.
    A device should be able to conduct and report spectrum resource measurements at the time of receiving a request from another device, at a predefined interval or on a predefined condition.
    A device should be able to provide spectrum resource measurements information to another device before its joining (e.g., in the form of the beacon frame).
    Intermediate device(s) between the requesting and requested (target) devices should be able to relay the spectrum resource measurement request.
    Intermediate device(s) should be able to piggy back its own measurement information when relaying the report from the requested device to the requesting device.

## Slide 7: Proposal for General descriptions (cont’d)
4 General descriptions
  4.x Spectrum Resource Measurement Request Structure
    SRM request header should include the following:
      Requesting device ID, PAN ID
      Measurement type
      Measurement mode (e.g., autonomous, triggered)
      Measurement duration
      Relay mode (e.g., through, piggy back)