## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Proposal for SRMM Functional Requirements in Technical Guidance Document]
Date Submitted: [6 May, 2015]
Source: [Hidetoshi Yokota] Company [Landis&Gyr]
Address [1-2-9 Nishi Shimbashi Minato-ku, Tokyo 105-0003, Japan]
Voice:[+81 3-5532-7455], FAX: [+81 3-5532-7519], E-Mail:[hidetoshi.yokota@landisgyr.com]
Re: [“TG4s Technical Guidance Document”, IEEE 802.15-14-0555-04-004s]
Abstract: [This contribution investigates RMM defined in IEEE802.11 WLAN and proposes applicability to SRMM for IEEE802.15.4 WPAN as functional requirements in the Technical Guidance Document.]
Purpose: [Discussion and approval]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
Proposal for SRMM Functional Requirements in Technical Guidance Document
Authors:

## Slide 3: Outline
Investigation of IEEE802.11k (WLAN RRM)
  Measurement types and information
Applicability to IEEE802.15.4 (WPAN SRM)
Proposal for Functional requirements

## Slide 4: Measurement types supported in IEEE802.11k
Action frame
(management frame)
Public (4)
Radio Measurement (5)
Measurement pilot (7)
Radio Measurement Request (0)
Link Measurement Request (2)
Neighbor Report Request (4)
Radio Measurement Report (1)
Link Measurement Report (3)
Neighbor Report Response (5)
Beacon Request/Report (5)
Noise Histogram Request/Report (4)
STA Statistics Request/Request (7)
Chanel Load Request/Report (3)
Frame Request/Report (6)
Location Request/Report (8)
Transmit Stream/Category Request/Report (9)
“Category Code”
“Action Code”
“Measurement Type”
Measurement Pause Request (255)

## Slide 5: Measurement information handled in each type
Request/report measurements
  Channel Load: channel busy time in the measurement duration
  Noise Histogram: power histogram measurement of non-IEEE802.11 noise power
  Beacon: RCPI and RSNI of received Beacons or Probe Responses, etc.
  Frame: count of received frames, average RCPI, etc.
  STA Statistics: transmitted fragment counts, failed counts, retry counts, etc.
  Location Configuration Information (LCI): latitude, longitude and altitude, etc.
  Transmit Stream/Category: condition of an ongoing traffic stream link between QoS STAs

## Slide 6: Measurement information handled in each type (cont’d)
Request/report measurements (cont’d)
  Neighbor Report: list of APs and their information (security, capability, etc.)
  Link Measurement: instantaneous quality of a link (RCPI, RSNI)
Request only
  Measurement Pause: interval between individual measurements
Report only
  Measurement Pilot: periodically transmitted (more frequently than beacons)

## Slide 7: Applicability to IEEE802.15.4
Action | Measurement Type |  | Content | Applicability to 802.15* | Note
Resource Measurement | Channel load |  | channel unitization in measurement duration | Y | 
 | Noise histogram |  | noise power in idle mode | C | Definition needs to be changed
 | Beacon |  | Reported frame information (frame type) | C | Definition needs to be changed
 |  |  | RSNI | C | Definition needs to be changed
 |  |  | RCPI | C | Definition needs to be changed
 | Frame |  | MAC address | Y | 
 |  |  | Average RCPI | C | Definition needs to be changed
 |  |  | Last RSNI | C | Definition needs to be changed
 |  |  | Last RCPI | C | Definition needs to be changed
 |  |  | Frame count | Y | 
 | STA statistics | STA counter group | transmitted fragment counts | Y | 
 |  |  | group transmitted frame counts | Y | 
 |  |  | failed counts | Y | 
 |  |  | received fragment counts | Y | 
 |  |  | group received frame counts | Y | 
 |  |  | FCS error counts | Y | 
 |  |  | transmitted frame counts | Y | 
 |  | MAC Statistics group | retry counts | Y | 
 |  |  | multiple retry counts | Y | 
 |  |  | frame duplicate counts | Y | 
 |  |  | RTS success counts | N | RTS is not defined
 |  |  | RTS failure counts | N | RTS is not defined
 |  |  | ACK failure counts | Y | 
 |  | BSS Average Access Delay group | AP average access delay | C | Definition needs to be changed
 |  |  | AC average access delay | N | AC is not defined
 |  |  | Station count | N | STA count is not defined
 |  |  | channel utilization | C | Definition needs to be changed
 | Location configuration information |  | location of STA | U | irrelevant to SRM
 | Transmit Stream / Category measurement |  | condition of ongoing traffic stream between two STAs | N | TS/TC are not defined
 | Measurement pause |  | delay between two measurements (request only) | Y | 
Link measurement |  |  | Transmit Power used | Y | 
 |  |  | Max Transmit Power | Y | 
 |  |  | RCPI | C | Definition needs to be changed
 |  |  | RSNI | C | Definition needs to be changed
Neighbor report |  |  | known neighbor APs | N | AP is not defined
(*) Y: applicable, N: not applicable, C: conditionally applicable, U: unknown |  |  |  |  | 

## Slide 8: Proposal for Functional requirement (Section 5)
 |  | Items | Detailed Items | Metric ID (1 Octet） | Measurement | Report |  |  |  | 
 |  |  |  |  | Periodical/Request/Continues | Periodical/Request/Conditional |  | Memo |  | 
 | Measurement | Channel Load | ED (Passive) |  |  | Request |  | Detected energy each channel | 10.2.5 Receiver E | 8.2.11.1 MLME-SCAN.request
 |  |  | CCA (Passive) |  |  |  |  | 10.2.7 Clear channel assessment (CCA) |  | 
 |  |  | Active Scan |  |  |  |  |  |  | 
 |  |  | CCA value histogram |  |  |  |  |  |  | 
 |  |  | CA count |  |  |  |  |  |  | 
 |  |  | Noise? |  |  |  |  |  |  | 
 |  |  | Percentage of time of failed transmissions (No Ack) |  |  |  |  |  |  | 
 |  |  | Percentage of time of deferred transmissions (CCA) |  |  |  |  |  |  | 
 |  |  | channel utilization |  |  |  |  | should be redifned from "channel utilization" in 802.11k |  | 
 |  | Link Statistics | LQI value |  |  |  |  | 10.2.6 Link quality indicator (LQI) |  | 
 |  |  | Transmit power used |  |  |  |  | supported in 802.11k |  | 
 |  |  | Max transmit power |  |  |  |  | supported in 802.11k |  | 
 |  |  | Received Channle Rower Indicator (RCPI) |  |  |  |  | supported in 802.11k |  | 
 |  |  | Received Signal Noise Indicator (RSNI) |  |  |  |  | supported in 802.11k |  | 
 |  |  | Received signal level (RSSI) |  |  |  |  |  |  | 
 |  |  | Received signal quality indicator (RSQI) |  |  |  |  |  |  | 
 |  | Interference measurement | What is different from ED ? |  |  |  |  |  |  | 
 |  |  | Fluctuation of floor ? |  |  |  |  |  |  | 
 |  |  | Deviation to fluctuation of floor ? |  |  |  |  |  |  | 
 |  |  | Same as media sensing Histogram ? |  |  |  |  |  |  | 
 |  |  | noise histogram |  |  |  |  | noise power in idle mode defined in 802.11k |  | 
 |  | Node Statistics | Frame Error Count |  |  |  |  | equivalent to "failed counts" |  | 
 |  |  | Time out Occurrence Count |  |  |  |  |  |  | 
 |  |  | Retry Count |  |  |  |  |  |  | 
 |  |  | multiple retry counts |  |  |  |  | supported in 802.11k |  | 
 |  |  | frame duplicate coutns |  |  |  |  | supported in 802.11k |  | 
 |  |  | Number of packets transmitted |  |  |  |  | equivalent to "transmitted frame coutns" |  | 
 |  |  | Number of packets received |  |  |  |  |  |  | 
 |  |  | Number of failed transmission (No Ack) |  |  |  |  |  |  | 
 |  |  | Number of failed reception (CRC error) |  |  |  |  | equivalent to "FCS error counts" |  | 
 |  |  | Number of deferred transmission (CCA) |  |  |  |  |  |  | 
 |  |  | Average / Maximum Buffer Utilization |  |  |  |  |  |  | 
 |  |  | transmitted fragment counts |  |  |  |  | supported in 802.11k |  | 
 |  |  | received fragment counts |  |  |  |  | supported in 802.11k |  | 
 |  |  | multicast transmitted frame counts |  |  |  |  | supported in 802.11k |  | 
 |  |  | multicast received frame counts |  |  |  |  | supported in 802.11k |  | 
 |  |  | ACK failure counts |  |  |  |  | supported in 802.11k |  | 
 |  |  | average access delay |  |  |  |  | supported in 802.11k |  | 
 |  |  | channel utilization |  |  |  |  | should be redifined from "AP avearage access delay" in 802.11k |  | 
 |  | Channel Occupancy Statistics | Frame Air Time |  |  |  |  |  |  | 
 |  | Wakeup statistics | Average interval |  |  |  |  |  |  | 
 |  |  | Min./Max. interval |  |  |  |  |  |  | 
 |  |  | Aperiodic wakeup count |  |  |  |  |  |  | 
 |  |  | Average awake duration |  |  |  |  |  |  | 
 |  |  | Min./Max. awake duration |  |  |  |  |  |  | 
 |  | Time synch. Error | Corrected error value |  |  |  |  |  |  | 
 |  |  | Drift rate |  |  |  |  |  |  | 
 |  | Security | Link level MIC error counter |  |  |  |  |  |  | 
 |  |  | Network level MIC error counter |  |  |  |  |  |  | 
 |  |  | Network level failed join counter |  |  |  |  |  |  | 
 |  | Latency |  |  |  |  |  |  |  |