## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Measured channel examples and modeling
Date Submitted: 12 May, 2015
Source: Ken Hiraga, Andrew Estrada, Ichiro Seto, Itaru Maekawa
Company: NTT , Sony, Toshiba, JRC
Address: Hirarinooka 1-1, Yokosuka Japan
Voice:+81-46-859-3474, FAX: +81-46-855-1497, E-Mail: hiraga.ken@lab.ntt.co.jp
Re: []
Abstract: This contribution shows measured channel response examples.
Purpose: To propose the channel modeling for 15.3e.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Inter-device reflections
Inter-device reflections depends on transmission distance
Transmission route of “ 1 round trip”:
[Tx] → reflected on Rx→ Reflected on Tx→ [Rx], its length is around 3*D
excess delay, τ, is about 2*D/c. (c = 3*108 [m/sec])
Transmission distance, D

## Slide 3: Measured channel response examples
0.1 nec = 30 mm propagation
= round trip of 15 mm
Chart: τ [nsec]
LOS
1-round trip
dependent of transmission distance
Typical usage whose transmission distance is 30-90mm, 1 cluster is observed.
independent
Transmission distance, D
independent of transmission distance
Notes: resolution = 1/(67-50) nsec = 0.058nsec ~ 1/10 symbol

## Slide 4: Proposed model
having observed the channel response above, we propose 2 cluster model.
Excess delay, τ [samples]
|h| [dB]
0
1
2
…
Initial decay δ0
This cluster is Rayleigh distribution
τ1
γ intra-cluster decay rate
K
Γ inter-cluster decay rate

## Slide 5: Proposed model
Comprises 2 clusters
  cluster #1: LOS + intra-device reflections
  cluster #2: Inter-device reflections
    Tx -> [refl. @Rx] -> [refl. @Tx] -> Rx
    Arrival time for the inter-device cluster is deterministic by the transmission distance
    This includes inter-device reflection in the opposed device.