## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Proposed Resolution for Comments 96 and 97 from Charlie Perkins
Date Submitted: May 14, 2015
Source: Jaehwan Kim (ETRI), Soo-Young Chang (SYCA), Jaebeom Kim (Ajou Univ.), and Sangsung Choi (ETRI)
Company: ETRI, SYCA, Ajou Univ.
Address:
Voice: +82 42 850 5338, E-Mail: kimj@etri.re.kr
Re:
Abstract: Proposed comment resolution for comments suggested by Charlie Perkins in 15-15-0391-00 and 15-15-0399-00 on the draft of TG10 L2R routing
Purpose: To suggest a comment resolution for Letter Ballot #104
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Introduction
In this document, proposed resolutions for two comments from Charlie Perkins listed in 15-15-391-00 and 15-15-0399-00 are prepared.
  Comments 96 and 97 which are related to Clause 5.2.2.1

## Slide 3: Comment 96
Commentor
  Charlie Perkins
Related clause
  5.2.2.1 P 26 line 25
Comment
  How are the metric parameters known by all devices in PAN?
  For the Inactive Time Aware metric to work, these parameters must be known to all devices
Proposed Change
  Explain or modify

## Slide 4: Comment 97
Commentor
  Charlie Perkins
Related clause
  5.2.2.1 P 26 line 33
Comment
  Why use maximum frame size instead of average?
  Average frame size would provide a measurement more meaningful for the particular network
Proposed Change
  Explain or modify

## Slide 5: Proposed Resolution for Comment 96 (Accept in Principle)
Explanation
  Parameter information can be known by all PAN devices. These devices can get BO and SO values which are included in beacon messages received in the association procedure.
  Basically the devices also know other parameter values such as transmission rate.

## Slide 6: Proposed Resolution for Comment 97 (Accept in Principle)
Explanation
  The maximum frame size is pre-defined value.
  To use an average frame size, an additional definition using a mathematical expression is required. Moreover, the average frame size based link metric may invoke false positive route decision error in the case that this value varies in the broad range of values. Therefore the maximum is used in this draft

## Slide 7: Proposed Resolution for Comment 96 and 97 (Accept in Principle)
Proposed resolution
  Add after the first sentence in Page 26, Line 18
    BO and SO values are included in beacon message of the PAN coordinator. Maximum frame size is utilized for bt in this metric. Using the maximum frame size enables a simple representation across a broad range of link conditions and traffic conditions. This has advantages over other strategies such as using the average frame size, especially in very lossy environments.