## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [LLC Proposal for 802.15.4]
Date Submitted: [15 Sept 2015]
Source: [Pat Kinney] Company [Kinney Consulting]
Address [Chicago, IL]
Voice:[+1.847.960.3715], FAX: [], E-Mail:[pat.kinney@kinneyconsultingllc.com]
Re: [For consideration by IG LLC]
Abstract: [Description of an LLC proposal for 802.15.4]
Purpose: [For consideration of a new project within 802.15, i.e. 802.15.12]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: A new standards project focused on IEEE 802.15.4
Proposal of a new LLC specifically for IEEE 802.15.4

## Slide 3: IEEE 802.15.12 Logical Link Control (LLC)
A new IEEE 802.15 project is being conceived to:
  Make IEEE 802.15.4 easier to use, like IEEE 802.11 (WiFi) and IEEE 802.3 (Ethernet)
  Enable IEEE 802.15.4 to use many of the higher layer protocol stacks used by IEEE 802.11 and IEEE 802.3 without changes
  Allow IEEE 802.15.4 to address new applications yet maintain backward compatibility with existing devices and applications

## Slide 4: Target Applications for 802.15.12
Deterministic
  ISA100.11a
  IETF 6tisch
  Industrial Internet of Things (IIoT)
Non-Deterministic (best effort)
  Smart Grid (e.g. WiSUN™)
  Internet of Things (IoT)
  Long Range Infrastructure (e.g. LECIM, etc.)

## Slide 5: Table of Contents
Conceptual Overview
Background
Issues
General Benefits
  Set up behaviors
  Dynamic behaviors
Emulations of L2 protocols for standards based upon 802.15.4

## Slide 6: General Concept
Create a Data Link sublayer above the MAC that adapts and configures the 802.15.4 MAC for desired operation, and contains existing and soon to be released sub-layers for 802.15.4 such as 6LoWPAN, Key Management Protocol (KMP), Layer 2 Routing Mesh (L2R), 6top (IETF 6tisch)

## Slide 7: Protocol Layers
Transport Layer
Network Layer
Data Link Layer
Physical Layer
UDP, TCP, ICMP
IPv6 (IPv4 with adapter)
LLC (802.15.12)
MAC (802.15.4)
802.15.4 Modulations: O-QPSK,BFSK, FSK, OFDM
802.15.4 Frequency Bands: (433, 890, 915, 2450, et al)

## Slide 8: 802.15.12 LLC would contain:
KMP
6LoWPAN
IPv6 network adaption standard for 802.15.4 (RFC 6775)
6top
Part of IETF 6tisch standard for TSCH (deterministic behavior adapted from WHART and ISA100.11a)
L2R
Layer 2 Mesh routing standard (IEEE 802.15.10)
Key Management Protocol Layer 2 standard (IEEE 802.15.9)

## Slide 9: 802.15.12 would also include
802.15.4 MAC
PAN Configuration
Security Configuration
Channel Configuration
New features such as: - Duplicate frames detection - Priority operation
- EtherType (indicates protocol)
Information Element (IE) use
-Standardized L2 data handling
- Upper layer creation/use

## Slide 10: Background
IEEE 802.15.4’s culture is to keep the MAC simple and the PHY simpler.
Complex decisions determining MAC behaviors were passed to the next higher layer. For example:
  Should the node join a specific network?
  What short address should the coordinator allocate to a node?
  What data rates, modulations, et al should be used?
The above culture resulted in 802.15.4 not being as easily used as 802.11 and 802.3, since the 802.15.4 higher layers must do many additional operations (which may be poorly described).

## Slide 11: Issues
Although IEEE 802.15.4 is extremely popular with vendors and users, each user application needs a specific protocol stack
Older versions of 802.15.4 didn’t address many of the new application needs, hence user application stacks added their own enhancements
Security on older versions of 802.15.4 did not function correctly, hence user application stacks used their own security

## Slide 12: Issues (continued)
802.15.4 couldn’t optimally address application needs ranging from very small protocol code space to complicated protocol structures
Proprietary protocols such as LoRA™ and SigFox™ have arisen due to the complexity of 802.15.4 protocols, misunderstanding of how to use specific 802.15.4 modes and the performance gains they can give.

## Slide 13: 802.15.12 Benefits
802.15.12 will be able to configure the 802.15.4 MAC and PHY with security, network, and channel settings via defaults or settings received via an out-of-band means
802.15.12 will enable IC or stack vendors to provide consistent and standardized mechanisms to set up networks and links
802.15.12 will enable IEEE 802.15.4 to address new applications or to better address existing applications

## Slide 14: Network Discovery and Selection Support
Generic advertisement service (GAS) Functionality (borrowed from 802.11) enables nodes to discover the availability of information related to desired network services in a standardized fashion
  e.g., information about services such as provided in a WPAN, local access services, or other external networks

## Slide 15: Network Setup
PAN Coordinator default parameters
  Addressing
  PAN ID (or no PAN ID)
  Mode: Beacon-enabled or Nonbeacon-enabled
Topology
  Mesh or Star
Link set up
  channel(s), modulation parameters, data rate(s), transmit power(s), Low Energy mode(s), FCS size, CSMA settings
Channel Hopping Network
  changing frequencies periodically
Asymmetric Network
  devices are either high or low capability

## Slide 16: Security Set-up
Authentication and encryption
Policy settings (network keys only or link keys, security level by frame type, by IE type, etc.)
Key management protocol, such as 802.15.9
Authorization

## Slide 17: Management
Collection of network metrics
Neighbor tables
Information Elements
  Build IEs for transmission to other devices
  Decode IEs received from other devices
  Prepare IEs such as ESDUs intended for other device’s higher layers

## Slide 18: Regulatory Matters
Country of operation
Device class
  Duty cycle constraints
CCA settings (time, threshold, mode)

## Slide 19: Dynamic Behaviors
Dynamic behaviors allow a network/device to adapt to changing conditions and maintain performance. IEEE 802.15.12 proposed dynamic behaviors include:
Dynamic Data Rate Selection
  For those PHYs with multiple data rates, data rates could be better set by 802.15.12 on a link-by-link basis
Dynamic Transmit Power Selection
  For PHYs with defined multiple transmit power levels, 802.15.12 could set transmit power level on a link-by-link basis considering CSMA impact, PHY Preambles, PHY FEC, signal strength, failed packets
Dynamic Channel Selection
  For fixed frequency operation maintain current channel status such as coexistence issues and interferers and periodically search other channels for better link quality conditions and change to another channel if advantageous
Dynamic Preamble Selection
  For PHYs with multiple preamble, 802.15.12 will configure the MAC to verify the preamble’s effect on the link and then configure the MAC for the best preamble
Dynamic Modulation Selection
  For PHYs with multiple modulation options 802.15.12 will configure the MAC to test modulation effectiveness and then configure the MAC for the best modulation

## Slide 20: Emulation of standard’s L2 protocols based upon 802.15.4
802.15.12 could be enhanced with further ISA100.11a behaviors since TSCH and IETF 6top have already been developed
Others?

## Slide 21: Prioritized Functionality (first release)
Protocol differentiation (dispatch)
Align 802.15.9 and 802.15.10 with LLC
Architecture to provide extendibility
Regulatory configuration, e.g. PHY Configuration as per country of operation, Device class, Duty cycle constraints, CCA settings (time, threshold, mode)
L2 protocol extensions from other organizations, e.g. IETF 6tisch 6top, Thread™
  Priority