## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Proposed resolutions of DSME comments from Sponsor Ballot
Date Submitted: 16 July, 2015
Source: Wun-Cheol Jeong
Company: ETRI
Address: 161 Gajeong-dong, Yuseong-gu, Daejeon, KOREA
Voice: +82-42-860-5104, FAX: +82-42-860-4197, E-Mail: wjeong@etri.re.kr
Re:
Abstract: Proposed resolutions of DSME comments from SB.
Purpose: To propose resolutions of DSME comments from SB.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
Proposed Resolution of CID i-438
Insert the following table on page 262 in 8.2.21.1:
Table 109a-Elements of DSMESABSpecification
Name | Type | Valid range | Description
DSMESAB Sub-block Length | Integer | 0x00 – 0xff | The length of the DSMESAB sub-block in units in Figure 61 for channel adaptation mode or in Figure 63 for channel hopping mode.
DSMESAB Sub-block Index | Integer | 0x0000 – 0xffff | The beginning of the DSME SAB sub-block in the entire SAB as illustrated in Figure 61 for channel adaptation mode or in Figure 63 for channel hopping mode.
DSMESAB Sub-block | Bitmap | As defined in Figure 61 for channel adaption mode or in Figure 63 for channel hopping mode. | The sub-block of the DSME Slot Allocation Bitmap as described in Figure 61 for channel adaptation mode or in Figure 63 for channel hopping mode.
Notes: 2

## Slide 3
Proposed Resolution of CID i-438 (cont’d)
Change the Valid range of DSMESABSpecification in Table 109 on page 262 in 8.2.21.1 to “As defined in Table109a”.
Change the Valid range of DSMESABSpecification in Table 110 on page 264 in 8.2.21.2 to “As defined in Table109a”.
Change the Valid range of DSMESABSpecification in Table 111 on page 265 in 8.2.21.3 to “As defined in Table109a”.
Change the Valid range of DSMESABSpecification in Table 112 on page 266 in 8.2.21.4 to “As defined in Table109a”.
Notes: 3

## Slide 4
Proposed Resolution of CID i-439
The MAC commands for DSME-GTS allocations are sent in the CAP.
  Thus, to clarify it, change the first sentences in 7.5.14, 7.5.15, and 7.5.16
  “Only devices that have been … shall send this command.”
  to be
  “Only devices that have been … shall send this command in the CAP.”
The contents of macDsmeAct is updated at the destination device after the DSME-GTS notify command is received at the destination.
  Thus, remove the following sentence at 4 on page 90 in 6.11.5.1:
  “Also, the device shall update macDsmeAct … parameter value.”
  Then, add the following sentence after the last sentence at 36 on page 90 in 6.11.5.1:
  “Also, the device shall update macDsmeAct according to the value in the DSMESABSpecification field of the DSME GTS Notify command.”
Notes: 4

## Slide 5
Proposed Resolution of CID i-439
Add the following paragraph after the line 36 on page 90 to describe the behavior when a DSME GTS Notify command is not received at the destination device:
  “If no DSME GTS Notify command is received at the destination device within the expected time, the device shall notify the higher layer of the failure by the MLME-COMM-STATUS.indication primitive with a Status of TRANSACTION_EXPIRED.”
Replace Figure 65 on page 91 with the one in the next slide.
Notes: 5

## Slide 6
Sender
higher layer
Sender
MAC
Receiver
MAC
Receiver
higher MAC
MLME-DSME-GTS.request
DSME GTS Request command
MLME-DSME-GTS.indication
MLME-DSME-GTS.response
DSME GTS Response command
DSME GTS Notify command
MLME-COMM-STATUS.indication
MLME-DSME-GTS.confirm
Proposed Resolution of CID i-439 (cont’d)
Figure 65 – Message sequence chart for DSME GTS allocation and management
Notes: 6

## Slide 7
Proposed Resolution of CID i-439 (cont’d)
Discussions on the case when DSME-GTS commands are missed:
  When a DSME-GTS response command is not received at the source device:
    The MAC sublayer of the source device will notify the higher layer of the failure using MLME-DSME-GTS.confirm primitive as stated in the draft.
    The higher layer decides whether the DSME-GTS request shall be sent again or not. Since the behavioral description of the higher layer is beyond the scope of this standard, this procedure is not stated.
  When a DSME-GTS notify command is not received at the destination device:
    The MAC sublayer of the destination device will notify the higher layer of the failure DSME-GTS allocation using MLME-COMM-STATUS.indication primitive. The destination device will not allocate DSME-GTSs being negotiated.
    Since the source device does not know if the notify command is not received at the destination device, it will try to access the channel to exchange the MAC data frames on the allocated DSME-GTSs. However, the source device will not receive ACK for the MAC data frames. The higher layer of the source device will know the link is not stable after several trials to send data. Then, it may deallocate the DSME-GTSs.
Notes: 7

## Slide 8
Proposed Resolution of CID i-443
Allocation counter tables are required to manage DSME-GTSs. Using allocation counter tables, MAC sublayer schedules the DSME-GTSs in the next superframe to send or receive MAC data frames. Scheduling DSME-GTSs is performed in MAC sublayer, not in the next higher layer. So, the tables are required.
However, the description in the draft should be revised as follows:
  Change the description of macDsmeAct in the Table 140 on page 302 to be:
  Also, change the caption of Table 142 to “Elements of Allocation counter table”
Attribute | Type | Range | Description | Default
macDsmeAct | List of the allocation counter table, as defined in Table 142 | - | List of the allocation table of the DSME-GTS allocated to the devices | 0
Notes: 8