## Slide 1: Stack Ack Performance Estimation
Submission for TG3e
IEEE802.15.3e
Itaru Maekawa (JRC: Japan Radio Co.,Ltd.)

## Slide 2
Block ACK
  Effective way to save & share bandwidth among multiple devices, especially under high error or collision environments, however….This method has the following disadvantages:
    Higher complexity
    Larger buffer memory
    Larger potential latency
Stack ACK
  Practical way for HRCP, because …
    Bandwidth saving is not required, thanks to good BER environment
    Lower Complexity , simple hardware requirements
“Simple” Stack ACK
- Key Concept of HRCP MAC - #2 -
“Small” benefit versus cost (complexity)
for use cases of HRCP
“Stacked Coin”
FIFO Buffer

## Slide 3
Sub-F#N+4
Sub-F#N+3
Sub-F#N+2
Sub-F#N+1
ACK#M
Sub-F#M+4
Sub-F#M+3
Sub-F#M+2
Sub-F#M+1
ACK#N+4
Sub-F#N+8
Sub-F#N+7
Sub-F#N+6
Sub-F#N+5
ACK#M+4
Data Error
Or Buffer full
Sub-F#M+8
Sub-F#M+7
Sub-F#M+6
Sub-F#M+5
ACK#N+6
Sub-F#N+10
Sub-F#N+9
Sub-F#N+8
Sub-F#N+7
ACK#M+8
Time #1
ACK#M+8
ACK#N+6
Header Error
Time #2
Time #3
Time #4
ACK#N+6
ACK#N+12
ACK#M+10
Time #5
ACK#M+12
ACK#M+12
SIFS
SIFS
SIFS
IIFS
RIFS
IIFS
Sub-F#M+14
Sub-F#M+13
Sub-F#M+12
Sub-F#M+11
ACK#N+12
SIFS
Sync.lost
Dev.A
Dev.B
Dev.A
Dev.B
Dev.A
Dev.B
Dev.A
Dev.B
Dev.A
Dev.B
RIFS
SIFS
Sub-F#M+10
Sub-F#M+9
ACK#N+6
SIFS
SIFS
Sub-F#N+10
Sub-F#N+9
Sub-F#N+8
Sub-F#N+7
ACK#M+10
Sub-F#N+12
Sub-F#N+11
SIFS
SIFS
ACK#N+12
RIFS
ACK#M+12
IIFS
ACK#M+12
IIFS
Time Domain MAC Behavior

## Slide 4: Stack Ack: Performance Estimation Model
Time
Subframe#N+15
PHY Header
HCS
MAC Header
Subframe#N+1
Subframe#N
Subframe#N+31
PHY Header
HCS
MAC Header
Subframe#N+17
Subframe#N+16
SIFS
SIFS
SIFS
MPDU#N
FCS
Subframe#N
MAC
Subheader#N
HCS
PHY Header
HCS
MAC Header
PHY Header
HCS
MAC Header
Tperiod
 |  |  | unit
PHY Preamble | Tpr | 2 | usec
PHY-header+MAC-header +HCS | Lhd | 132 | bit
1760M BPSK, 1/2 ECC. | Rhead | 0.88 | Gbps
 | Thd | 2.15 | usec
16QAM wo pilot, 14/15 LDPC | Rphy | 6.57 | Gbps
 | Tsifs | 2 | usec
mpdu Length | Lmpd | 4 | kB
Sub-Header+HCS+FCS | Lsh | 11 | B
Aggregation Number | N | 16 | 
Tperiod | Tperiod | 86.44429 | usec
Parameters : Example
Simplified Estimation Model
When Frame Error is occurred with probability of FER, 50% of Sub-Frames (Average) are retransmitted.
MAC Throughput (MACtp) vs FER is calculated as below.
  FER=1-(1-BER)Lmpd・N
  :(BER:bit error rate)

## Slide 5: Block-Ack :Performance Estimation Model
Time
Subframe#N+15
PHY Header
HCS
MAC Header
Subframe#N+1
Subframe#N
PHY Header
HCS
MAC Header
Subframe#X
SIFS
SIFS
SIFS
MPDU#N
FCS
Subframe#N
MAC
Subheader#N
HCS
PHY Header
HCS
MAC Header
PHY Header
HCS
MAC Header
Tperiod
SIFS
Tretry
 |  |  | unit
PHY Preamble | Tpr | 2 | usec
PHY-header+MAC-header +HCS | Lhd | 132 | bit
1760M BPSK, 1/2 ECC. | Rhead | 0.88 | Gbps
 | Thd | 2.15 | usec
16QAM wo pilot, 14/15 LDPC | Rphy | 6.57 | Gbps
 | Tsifs | 2 | usec
mpdu Length | Lmpd | 4 | kB
Sub-Header+HCS+FCS | Lsh | 11 | B
Aggregation Number | N | 16 | 
Tperiod | Tperiod | 86.44429 | usec
Parameters : Example
Simplified Estimation Model
When Frame Error is occurred with probability of FER, “ONE” Sub-Frames are retransmitted.
MAC Throughput (MACtp) vs FER is calculated as below.
  FER=1-(1-BER)Lmpd・N
  :(BER:bit error rate)

## Slide 6: Stack ACK vs Block-Ack :Throughput Comparison
 |  |  | unit
PHY Preamble | Tpr | 2 | usec
PHY-header+MAC-header +HCS | Lhd | 132 | bit
1760M BPSK, 1/2 ECC. | Rhead | 0.88 | Gbps
 | Tsifs | 2 | usec
Sub-Header+HCS+FCS | Lsh | 11 | B
mpdu Length | Lmpd | 4 | kB
Common Parameters :
Chart: BER
| 1.0000000000000012E-10 | 1.0000000000000009E-9 | 1.000000000000001E-8 | 1.0000000000000011E-7
Stack ACK | 99.9974 | 99.9744 | 99.7447 | 97.5044
Block ACK | 99.9992 | 99.9922 | 99.9222 | 99.2452
Chart: BER
| 1.0000000000000012E-10 | 1.0000000000000009E-9 | 1.0000000000000008E-8
Stack ACK | 99.9795 | 99.7956 | 97.9934
Block ACK | 99.9992 | 99.9922 | 99.9222
FER ～ 5%
FER ～ 4%
PHY Rate :6.57Gbps (16QAM, LDPC 14/15 )
Number of Aggregation:16
PHY Rate :52.6Gbps (16QAM x8 MIMO, LDPC 14/15 )
Number of Aggregation:128
Conclusion
As long as FER is less than 10% order, throughput advantage of Block ACK is negligible .
(If FER exceed 10% level, Rate adaptation System should work.)