## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Proposal for IEEE802.15.3e – PHY MIMO]
Date Submitted: [10 September 2015]
Source: [Ken Hiraga(1), Jae Seung Lee, Itaru Maekawa, Makoto Noda, Ko Togashi, (representative contributors), all contributors are listed in “Contributors” slide]
Company: [ETRI, JRC, NTT1, Sony, Toshiba]
Address1: [Hirarinooka 1-1, Yokosuka Japan]
E-Mail1: [hiraga.ken@lab.ntt.co.jp (all contributors are listed in “Contributors” slide)]
Abstract: This document presents an overview of the full MAC/PHY proposal for HRCP.
Purpose: To propose a full set of specifications for TG 3e.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributors acknowledge and accept that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
Contributors
Name | Affiliation | Email
Jae Seung Lee | ETRI | jasonlee@etri.re.kr
Moon-Sik Lee | ETRI | moonsiklee@etri.re.kr
Itaru Maekawa | Japan Radio Corporation | maekawa.itaru@jrc.co.jp
Doohwan Lee | NTT Corporation | lee.doohwan@lab.ntt.co.jp
Ken Hiraga | NTT Corporation | hiraga.ken@lab.ntt.co.jp
Masashi Shimizu | NTT Corporation | masashi.shimizu@upr-net.co.jp
Keitarou Kondou | Sony Corporation | Keitarou.Kondou@jp.sony.com
Hiroyuki Matsumura | Sony Corporation | Hiroyuki.Matsumura@jp.sony.com
Makoto Noda | Sony Corporation | MakotoB.Noda at jp.sony.com
Masashi Shinagawa | Sony Corporation | Masashi.Shinagawa@jp.sony.com
Ko Togashi | Toshiba Corporation | ko.togashi@toshiba.co.jp
Kiyoshi Toshimitsu | Toshiba Corporation | kiyoshi.toshimitsu@toshiba.co.jp

## Slide 3
Proposal for IEEE802.15.3e
High-Rate Close Proximity System
September 15, 2015

## Slide 4
This part describes an outline of the key features for achieving high transmission rates using MIMO transmission.
Proposed draft is 15-15-0661 as a part of SC-PHY proposal (15-15-0665,” Proposal for IEEE802.15.3e - SC PHY Draft”)
Channel model parameters for PHY simulations are also shown. BER simulation results with random impulse response generation and fixed average response are compared. We found that there is few difference between them.
Abstract

## Slide 5
MIMO PHY proposal for 100 Gbit/s
HRCP Channel model
  Channel response measurements
  SISO model
  MIMO extension
Contents

## Slide 6: 1. MIMO PHY proposal for 100 Gbit/s
We propose the use of MIMO in line-of-sight (LOS) propagation environment for high rate towards 100Gbit/s.
Selecting antenna is allowed to be done by employing training using multiple of association requests.
For 100 Gbit/s transmission, channel aggregation or bonding will also be employed

## Slide 7: MCS
 |  | * Pilot word length/sub-block length = 8/64 |  |  |  |  |  |  |  |  | 
Modulation | Code Rate | PHY transmission rate, Gbit/s |  |  |  |  |  |  |  |  | 
 |  | x1 mode (Not MIMO) |  | x2 mode |  | x4 mode |  | x8 mode |  | x16 mode | 
 |  | without pilot word | with pilot word* | without pilot word | with pilot word* | without pilot word | with pilot word* | without pilot word | with pilot word* | without pilot word | with pilot word*
QPSK | 14/15 | 3.3 | 2.9 | 6.6 | 5.7 | 13.1 | 11.5 | 26.3 | 23.0 | 52.6 | 46.0
16QAM | 11/15 | 5.2 | 4.5 | 10.3 | 9.0 | 20.7 | 18.1 | 41.3 | 36.1 | 82.6 | 72.3
16QAM | 14/15 | 6.6 | 5.7 | 13.1 | 11.5 | 26.3 | 23.0 | 52.6 | 46.0 | 105.1 | 92.0
64QAM | 11/15 | 7.7 | 6.8 | 15.5 | 13.6 | 31.0 | 27.1 | 62.0 | 54.2 | 124.0 | 108.4
64QAM | 7/8 | 9.3 | 8.1 | 18.6 | 16.2 | 37.0 | 32.4 | 74.0 | 64.8 | 148.0 | 129.6
64QAM | 14/15 | 9.9 | 8.6 | 19.7 | 17.2 | 39.4 | 34.5 | 78.8 | 69.0 | 157.7 | 138.0
PHY Criteria 6 100 Gbit/s using Ch2 and Ch3, unlicense in US, EU, Korea, and Japan

## Slide 8: Channel aggregation
Channel # | Start frequency | Center frequency | Stop frequency
1 | 57.240 | 58.320 | 59.400
2 | 59.400 | 60.480 | 61.560
3 | 61.560 | 62.640 | 63.720
4 | 63.720 | 64.800 | 65.880
Frequency channels
Channel aggregation
1 & 3
2 & 4
1 & 4
Channel bonding should also be supported
PHY Criteria 2 in 60GHz band
Notes: The start and stop frequencies are nominal values. The frequency spectrum of the transmitted signal needs to conform to the transmit spectral mask as well as any regulatory requirement.

## Slide 9: PHY frame structures
Example of the number of branches, M = 4
72 symbol
8CP + 64symbol
Information for MIMO bitstream processing shall be included in header.
(Stream #)
M - streams data
Payload #4
Payload #1
Payload #3
Payload #2
for MIMO transmission channel estimation
SYNC
CES #4
CES #1
0 values, unmodulated
Tx#4
Tx#1
CES #3
Tx#3
CES #2
Tx#2
Same signal is transmitted from each antenna element
SFD
SYNC
SFD
SYNC
SFD
SYNC
SFD
Header #4
Header #1
Header #3
Header #2

## Slide 10: Selecting antenna
Array displacement occurred in touch by user
Kiosk automatically selects well-placed antennas.
In HRCP, the use of line-of-sight (LOS) MIMO that requires no multipath propagation effect will be assumed.
In LOS-MIMO transmission, the displacement of antenna arrays between transmitter and receiver will cause degradation in the channel capacity.
Idea of selecting antenna
Large-scale antenna array

## Slide 11: Selecting antenna
DEV2
DEV1
PPC
Uses these antenna elements which are located in front of terminal.
System Criteria 1 No accurate alignment
DEV1
PPC
DEV2
If array displacement occurred in touch by user..
Low capacity due to high spatial correlation between streams
High capacity with low spatial correlation

## Slide 12: Setup sequence for MIMO transmission
Comprises information below:
Value of M1
Value of Nar (The number of required Association request commands. It is equal or less than Marray )
MIMO mode
Beacon
The number of Association request packet is equal to Nar.
These are transmitted from antenna element #1 (TBD) to allow DEV1 to select antenna elements for following MIMO transmission.
While transmissions of Association requests the remaining number is counted down.
Switch to M-stream MIMO mode
SISO mode using the antenna element #1
SISO mode using the antenna element #1
Switch to M-stream MIMO mode
(Antenna elements used in transmission are already selected)
DEV2
(Portable terminal)
DEV1
(Kiosk)
The number of MIMO branches: M2
The number of antenna elements: Marray (1~ 256)
The number of MIMO branches: M1 ( 1~16)
Antenna Selection Procedure (in SISO)
DEV2 decides the number of branches, M, by determining “M=min(M1,M2)”. The value of M is notified within the following Association Request commands.
Association request #1
Comprises information below:
・Value of M
・Remaining time = (Nar – 1)
Reading the first Association Aequest, DEV1 knows the number of elements, M.
Association request #Nar
Association request #Nar − 1
…
Association request #2
(1) when M1>M，
DEV1 selects M antenna elements
(Example of procedure selecting antenna: Select using reception levels)
Association requests are transmitted M1 times, hence M1 antenna is switched on to receive these Association requests.
(2) when M1≦M
DEV1 does not have to select antenna element. (Just listens to association requests)
Example:
(6 us / Assoc Req. command) * 256 = 1536 us
Change the time interval of sending Association Request commands into a fixed value.
(e.g. 6 us.)
Association response

## Slide 13: BER simulations settings
RF impairments
  Phase noise
    PSD(0) = -100 dBc, fp = 1MHz, fz = 100 MHz;
  PA Nonlinearity
    p = 4.20
    Vsat = 1.413 V
    a = 8200000
    b = 0.326
    q1 = 10.6
    q2 = 8.0
    G = 3.30
    Output backoff = 10 dB
FEC: LDPC
  Code rate = 11/15, 7/8, 14/15

## Slide 14: 100Gbit/s Transmission performance 64QAM, MIMO with M=16
BER=5.6e-7
SNR = 36 dB
Chart: SNR[dB]
| 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45
LDPC14/15 | 0.4082 | 0.38516 | 0.36286 | 0.33535 | 0.31167 | 0.28455 | 0.25991 | 0.23518 | 0.21048 | 0.18683 | 0.16497 | 0.14386 | 0.12413 | 0.10566 | 0.088712 | 0.072581 | 0.057757 | 0.043727 | 0.030417 | 0.018274 | 0.0090918 | 0.0037278 | 0.0012199 | 0.00036917 | 0.00010404 | 2.4909e-05 | 6.6848e-07 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
LDPC7/8 | 0.40667 | 0.38495 | 0.36041 | 0.33538 | 0.30956 | 0.28484 | 0.259 | 0.2344 | 0.20976 | 0.18651 | 0.16434 | 0.1439 | 0.12472 | 0.10672 | 0.089644 | 0.072955 | 0.056408 | 0.03861 | 0.021604 | 0.0091092 | 0.0028653 | 0.00075805 | 0.0001824 | 2.6463e-05 | 2.9117e-06 | 1.7718e-07
LDPC3/4 | 0.40808 | 0.38476 | 0.3628 | 0.33716 | 0.3124 | 0.28806 | 0.26391 | 0.24001 | 0.21705 | 0.19476 | 0.17372 | 0.153 | 0.13326 | 0.11251 | 0.089926 | 0.061108 | 0.030299 | 0.009922 | 0.0023663 | 0.00038846 | 3.1674e-05
LDPC11/15 | 0.40631 | 0.38087 | 0.35786 | 0.33287 | 0.3094 | 0.28582 | 0.26106 | 0.23853 | 0.21507 | 0.19385 | 0.17158 | 0.14953 | 0.12767 | 0.10335 | 0.073885 | 0.042115 | 0.017545 | 0.0049047 | 0.0009339 | 7.342e-05 | 6.79e-07 | 0 | 0 | 0 | 0 | 0
LDPC1/2 | 0.41104 | 0.39091 | 0.36842 | 0.34656 | 0.32439 | 0.30327 | 0.27891 | 0.25596 | 0.23134 | 0.20488 | 0.17195 | 0.12472 | 0.068311 | 0.028193 | 0.0075838 | 0.0013586 | 9.9835e-05 | 1.7825e-06 | 0 | 0 | 0
No FEC | 0.40526 | 0.38508 | 0.36001 | 0.33498 | 0.30993 | 0.28327 | 0.25871 | 0.23323 | 0.20908 | 0.18603 | 0.16328 | 0.14274 | 0.12303 | 0.10493 | 0.087571 | 0.071207 | 0.056472 | 0.043215 | 0.031586 | 0.022211 | 0.014786 | 0.0095842 | 0.0058984 | 0.0035696 | 0.0021225 | 0.0012638 | 0.00080734 | 0.00050053 | 0.00033984 | 0.00024992 | 0.00018974

## Slide 15: Link budget margin
 | Part | Symbol | Value | Unit
Tx side |  |  |  | 
(a) | Average Tx power level | Pt | 5.0 | dBm
(b) | Tx_ANT gain | Gt | 4.0 | dBi
Implementation and propagation loss |  |  |  | 
(c) | Implementation loss | IL | 6.0 | dB
(d) | Center frequency | fc | 60.5 | GHz
 | Transmission distance | D | 40.0 | mm
(e) | Transmission loss | PL | 40.1 | dB
Rx side |  |  |  | 
(f) | Rx_ANT gain | Gr | 4.0 | dBi
(g) | Thermal noise | Nth | -173.8 | dBm/Hz
(h) | Rx NF | NF | 8.0 | dB
(i) | Signal Bandwidth | BW | 1.76 | GHz
(j) | Symbol rate | SymR | 92.5 | dBHz
(k) | Noise power level | NP | -73.3 | dBm
(l) | Required Es/No for FER=8% | EsNo | 35.7 | dB
(m) | System margin | SysM | 0.0 | dB
(n) | Required Rx level | ReqRx | -37.6 | dBm
Maximum transmission range |  |  |  | 
(o) | Allowable path loss | APL | 44.6 | dB
 | Link margin |  | 4.5 | dB
Tx power = 10 dBm (total)
Required Es/N0 = 35.7 dB
  Required SNR = 36.0 dB
  Requires Es/N0 = SNR * R = 36.0 dB * 14/15 = 35.7 dB
Antenna gain = 4 dBi
  Microstrip antenna including feeding loss
Transmission distance = 40mm,
Transmission power = 5 dBm total
fc=60.48 GHz (center frequency of Ch 2)

## Slide 16: 2. HRCP channel measurement
Kiosk side
Microstrip antenna
In order to extract the values of channel model,
channel impulse response was measured using a network analyzer.
Portable device
side
(with chassis)
Distance
40 mm
Distance
40 mm
10 mm
10 mm
Measurement area*
Portable device
Kiosk
Network Analyzer
Port 2
Port 1
x
y
z
System configuration
* The antenna in the portable device side is moved around within the square area and a number of impulse responses was measured. The responses are averaged along this area to get the power delay profile.
Presented at Hawaii meetings

## Slide 17: Channel measurement and parameter extraction procedure
Frequency domain measurement
10 mm
10 mm
Network Analyzer
Port 2
Port 1
Similar measurement to that described in the CMD.
Time domain
channel responses
at thousands of points in the measurement area
Averaging
Frequency domain
channel responses (S21) at thousands of points in the measurement area
IFFT
Power delay profile (PDP):
averaged through the measurement area in x-y plane
Channel
Measurement area
Presented at Hawaii meetings

## Slide 18: PDP and channel model in BER simulations
Channel model
PDP obtained from the measurement
Sample# (oversample=4) | Time [nsec] | Average Level [dB] | K-factor [dB] | Phase
1 | 0.000 | 0.0 | 24.0 | 0°
2 | 0.145 | -5.4 | 20.0 | random
3 | 0.290 | -16.0 | 15.5 | random
4 | 0.435 | -27.3 | 0.0 | random
5 | 0.580 | -36.2 | 8.5 | random
6 | 0.725 | -39.0 | 9.0 | random
7 | 0.870 | -39.6 | 14.5 | random
8 | 1.015 | -46.5 | 12.0 | random
9 | 1.160 | -53.2 | 0.0 | random
10 | 1.305 | -47.4 | 17.5 | random
11 | 1.450 | -55.5 | 0.0 | random
12 | 1.595 | -48.7 | 17.0 | random
13 | 1.740 | -51.1 | 11.0 | random
14 | 1.885 | -51.6 | 12.5 | random
15 | 2.030 | -55.6 | 10.3 | random
16 | 2.175 | -53.7 | 20.0 | random
17 | 2.320 | -56.1 | 18.0 | random
18 | 2.465 | -56.6 | 16.5 | random
19 | 2.610 | -57.2 | 20.0 | random
20 | 2.755 | -58.1 | 17.5 | random
Chart: τ [nsec]
| 0 | 0.14499999999999999 | 0.28999999999999998 | 0.435 | 0.57999999999999996 | 0.72499999999999998 | 0.87 | 1.0149999999999999 | 1.1599999999999999 | 1.3049999999999999 | 1.45 | 1.595 | 1.74 | 1.885 | 2.0299999999999998 | 2.1749999999999998 | 2.3199999999999998 | 2.4649999999999999 | 2.61 | 2.7549999999999999 | 2.9 | 3.0449999999999999 | 3.19 | 3.335 | 3.48 | 3.625 | 3.77 | 3.915 | 4.0599999999999996 | 4.2050000000000001 | 4.3499999999999996 | 4.4950000000000001 | 4.6399999999999997 | 4.7850000000000001 | 4.93 | 5.0750000000000002 | 5.22 | 5.3650000000000002 | 5.51 | 5.6550000000000002
 | 0 | -5.4 | -16 | -27.3 | -36.2 | -39 | -39.6 | -46.5 | -53.2 | -47.4 | -55.5 | -48.7 | -51.1 | -51.6 | -55.6 | -53.7 | -56.1 | -56.6 | -57.2 | -58.1 | -63.7984 | -61.3805 | -60.6863 | -59.2819 | -63.2943 | -60.4321 | -60.1449 | -62.672 | -60.4666 | -58.0135 | -64.9436 | -64.8412 | -63.2335 | -66.234 | -66.0491 | -66.1352 | -65.9743 | -66.26 | -65.2724 | -71.9515
Notes: some cluster is included
(fixed value)

## Slide 19: BER simulations settings
RF impairments
  Phase noise
    PSD(0) = -100 dBc, fp = 1MHz, fz = 100 MHz;
  PA Nonlinearity
    p = 4.20
    Vsat = 1.413 V
    a = 8200000
    b = 0.326
    q1 = 10.6
    q2 = 8.0
    G = 3.30
    Output backoff = 10 dB
No FEC: check BER = 10-3

## Slide 20: Transmission performance: 64QAM SISO BER
(2) Using generator with random
In BER simulator program, the
generated impulse response using measured PDP and statistical information is used as the channel impulse response.
(same as 15.3c performance simulations)
(1) Using fixed impulse response
In BER simulator program, the
measured static PDP is used as the channel impulse response.
Average 800 out of 1,000 results. (Top and lower 10% are removed)

## Slide 21: Performance comparison
Small difference between two BER results
(2) Using generator with random
(1) Using fixed level

## Slide 22: MIMO extension of channel model
A set of SISO responses
Rx#1
Rx#2
Tx#1
Tx#2
MIMO channel response is in a matrix
MIMO transmission channel
In this figure, the number of branches is M = 2.
Rx#1
Rx#2
Tx#1
Tx#2
D
d
MIMO propagation channel
h22
h11
h21
h12
hji
Each is a SISO impulse response model. The propagation distance is reflected in each model as the propagation loss and phase rotation in the first tap.
Presented at Hawaii meetings
Notes: Time diff. h21 and h11 = 5/4/c = 4 [psec]

## Slide 23: MIMO extension: how to make hji
τ [samples]
|hji| [dB]
0
1
2
…
First tap = LOS component:
rji is the geometrical distance between Tx#i and Rx#j
Phase: rji*(2π/λ)
Amplitude: (λ/4πrji)2
Each has LOS component as the first arrival wave (at the first tap).
Rx#i
Tx#i
Rx#j
Tx#j
r
Delayed taps:
Phase: random
Amplitude:(λ/4πr)2
hji
MIMO transmission in HRCP:
Propagation environment in which the LOS component is dominant
Presented at Hawaii meetings

## Slide 24: MIMO extension: Optimum element spacing
Chart: Transmission distance, D / λ0
M = 16
M = 8
M = 4
M = 2
M = 9
As mentioned in the CMD,
Element spacing is an important factor in the MIMO channel
Hence the element spacing will be optimized in the simulation
Presented at Hawaii meetings

## Slide 25
MIMO extension:
Array size
d
D
Tx array
Rx array
Microstrip antenna
Basically the propagation channel is LOS MIMO.
when the number of elements M = 16 and the transmission distance D = 20 mm, optimum element spacing will be d = 5.5 mm hence array is 20mm x 20 mm. (Reference: 3e CMD)
PHY Criteria 6 The antenna shall be small enough
Presented at Hawaii meetings

## Slide 26: Thank you