## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Proposal for IEEE802.15.3e – Single Carrier PHY]
Date Submitted: [10 September 2015]
Source: [Makoto Noda(1), Ken Hiraga, Jae Seung Lee, Itaru Maekawa, Ko Togashi, (representative contributors), all contributors are listed in “Contributors” slide]
Company: [Sony1, ETRI, JRC, NTT, Toshiba]
Address1: [1-7-1 Konan, Minato-ku, Tokyo 108-0075]
E-Mail1: [MakotoB.Noda at jp.sony.com (all contributors are listed in “Contributors” slide)]
Abstract: This document presents a Single-Carrier PHY of the full MAC/PHY proposal for HRCP.
Purpose: To propose a full set of specifications for TG 3e.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributors acknowledge and accept that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Contributors
Name | Affiliation | Email
Jae Seung Lee | ETRI | jasonlee@etri.re.kr
Moon-Sik Lee | ETRI | moonsiklee@etri.re.kr
Itaru Maekawa | Japan Radio Corporation | maekawa.itaru@jrc.co.jp
Lee Doohwan | NTT Corporation | lee.doohwan@lab.ntt.co.jp
Ken Hiraga | NTT Corporation | hiraga.ken@lab.ntt.co.jp
Masashi Shimizu | NTT Corporation | masashi.shimizu@upr-net.co.jp
Keitarou Kondou | Sony Corporation | Keitarou.Kondou at jp.sony.com
Hiroyuki Matsumura | Sony Corporation | Hiroyuki.Matsumura at jp.sony.com
Makoto Noda | Sony Corporation | MakotoB.Noda at jp.sony.com
Masashi Shinagawa | Sony Corporation | Masashi.Shinagawa at jp.sony.com
Ko Togashi | Toshiba Corporation | ko.togashi@toshiba.co.jp
Kiyoshi Toshimitsu | Toshiba Corporation | kiyoshi.toshimitsu@toshiba.co.jp

## Slide 3: Proposal for IEEE802.15.3e High-Rate Close Proximity System
September 10, 2015

## Slide 4: Single Carrier (SC) PHY
Extremely high PHY-SAP payload-bit rates outperforming those of 15.3c
Min. 2 Gb/s and Max. 13 Gb/s, using a single channel with 2.16 GHz bandwidth
Reusing the best error-correction code respecting 15.3c
Reusing the rate-14/15 low-density parity-check (LDPC) code
Introducing a new rate-11/15 LDPC code whose decoder compatible with that for the rate-14/15 LDPC code to obtain moderate bit rates
New preamble, comparing 15.3c:
Decrease the length
Double the zero-auto correlation zone of the channel-estimation sequence
MIMO in SC PHY for 100 Gb/s is described in other material (15-0661/r1).
SC PHY proposal is also described in a draft version (15-0665/r1).

## Slide 5: Index for HRCP-SC PHY
Channelization of HRCP-SC PHY
Modulation and coding
Frame format
Preamble
MCS Evaluation

## Slide 6: Index for HRCP-SC PHY
Channelization of HRCP-SC PHY
Modulation and coding
Frame format
Preamble
MCS Evaluation

## Slide 7: Channel assignments for a single channel
a The start and stop frequencies are nominal values. The frequency spectrum of the transmitted signal needs to conform to the transmit spectral mask as well as any regulatory requirement.
CHNL_ID | Start frequencya | Center frequency | Stop frequencya
1 | 57.240 | 58.320 | 59.400
2 | 59.400 | 60.480 | 61.560
3 | 61.560 | 62.640 | 63.720
4 | 63.720 | 64.800 | 65.880

## Slide 8: Transmit spectral mask for a single channel
0
1
2
3
–1
–2
–3
(f – fc) (GHz)
0
–10
–20
–30
(same as that in 802.11ad)
(0.94, 0)
(1.2, –17)
(2.7, –22)
(3.06, –30)
(–0.94, 0)
(–1.2, –17)
(–2.7, –22)
(–3.06, –30)
Power (dB)

## Slide 9: Index for HRCP-SC PHY
Channelization of HRCP-SC PHY
Modulation and coding
Frame format
Preamble
MCS Evaluation

## Slide 10: Modulation and coding scheme (MCS)
PW: pilot word
PW length/sub-block length = 0.125
MCS identifier | single-carrier modulation | FEC Rate | PHY-SAP payload-bit rate (Gb/s) | 
 |  |  | w/o PW | w/ PW
0 | π/2 QPSK | 11/15 | 2.5813 | 2.2587
1 | π/2 QPSK | 14/15 | 3.2853 | 2.8747
2 | 16QAM | 11/15 | 5.1627 | 4.5173
3 | 16QAM | 14/15 | 6.5707 | 5.7493
4 | 64QAM | 11/15 | 7.7440 | 6.7760
5 | 64QAM | 14/15 | 9.8560 | 8.6240
6 | 256QAM | 14/15 | 13.1413 | 11.4987
Minimum 2 Gb/s and Maximum 13 Gb/s MCSs using a single channel

## Slide 11: Forward Error Correction
Gap between SNRr* obtained by floating point simulation and the Shannon limit in binary AWGN channel for codes employed in standards.
RS(240,224) on GF(28) T J 0.933 9.77 6.51 –3.26
LDPC(1440,1344) 15.3c 0.933 8.46 6.51 –1.96
LDPC(672,588) 15.3c 0.875 7.55 5.27 –2.28
LDPC(672,546) 11ad 0.813 6.96 4.26 –2.70
LDPC(672,504) 11ad 0.750 5.91 3.39 –2.53
LDPC(1440,1056) New 0.733 5.36 3.17 –2.20
SNRr*: signal-to-noise ratio required for a bit-error rate of 10–6
Reuse the 14/15 LDPC code and a new 11/15 LDPC code with the best code efficiencies.
code standard rate SNRr
(dB)
(dB)
(dB)
Shannon
limit
gap
rate
14/15
rate
11/15

## Slide 12: Proposed Overlaid-rate-compatible (ORC) LDPC Codes
A low-rate parity-check matrix, as a simplified example of an 11/15 LDPC code
A high-rate parity-check matrix, as a simplified example of a 14/15 LDPC code
1 0 0 0 0 0 0
0 1 0 0 0 0 0
0 0 1 0 0 0 0
0 0 0 1 0 0 0
0 0 0 0 1 0 0
0 0 0 0 0 1 0
0 0 0 0 0 0 1
0 0 0 0 1 0 0
0 0 0 0 0 1 0
0 0 0 0 0 0 1
1 0 0 0 0 0 0
0 1 0 0 0 0 0
0 0 1 0 0 0 0
0 0 0 1 0 0 0
0 0 0 0 0 0 1
1 0 0 0 0 0 0
0 1 0 0 0 0 0
0 0 1 0 0 0 0
0 0 0 1 0 0 0
0 0 0 0 1 0 0
0 0 0 0 0 1 0
0 0 0 0 0 1 0
0 0 0 0 0 0 1
1 0 0 0 0 0 0
0 1 0 0 0 0 0
0 0 1 0 0 0 0
0 0 0 1 0 0 0
0 0 0 0 1 0 0
0 0 0 0 0 0 1
1 0 0 0 0 0 0
0 1 0 0 0 0 0
0 0 1 0 0 0 0
0 0 0 1 0 0 0
0 0 0 0 1 0 0
0 0 0 0 0 1 0
1 0 0 0 0 0 0
0 1 0 0 0 0 0
0 0 1 0 0 0 0
0 0 0 1 0 0 0
0 0 0 0 1 0 0
0 0 0 0 0 1 0
0 0 0 0 0 0 1
0 0 0 0 1 0 0
0 0 0 0 0 1 0
0 0 0 0 0 0 1
1 0 0 0 0 0 0
0 1 0 0 0 0 0
0 0 1 0 0 0 0
0 0 0 1 0 0 0
0 1 0 0 0 0 0
0 0 1 0 0 0 0
0 0 0 1 0 0 0
0 0 0 0 1 0 0
0 0 0 0 0 1 0
0 0 0 0 0 0 1
1 0 0 0 0 0 0
1 0 0 0 0 0 1
1 1 0 0 0 0 0
0 1 1 0 0 0 0
0 0 1 1 0 0 0
0 0 0 1 1 0 0
0 0 0 0 1 1 0
0 0 0 0 0 1 1
1 0 0 0 1 0 0
0 1 0 0 0 1 0
0 0 1 0 0 0 1
1 0 0 1 0 0 0
0 1 0 0 1 0 0
0 0 1 0 0 1 0
0 0 0 1 0 0 1
0 0 0 0 1 0 1
1 0 0 0 0 1 0
0 1 0 0 0 0 1
1 0 1 0 0 0 0
0 1 0 1 0 0 0
0 0 1 0 1 0 0
0 0 0 1 0 1 0
0 1 0 0 0 1 0
0 0 1 0 0 0 1
1 0 0 1 0 0 0
0 1 0 0 1 0 0
0 0 1 0 0 1 0
0 0 0 1 0 0 1
1 0 0 0 1 0 0
A check matrix of a high-rate code composed of overlay of sub-matrices in a check matrix of a low-rate code. This structure enables to share a belief-propagation decoder for the high-rate and low-rate LDPC codes.

## Slide 13: A Simple LDPC encoder
A systematic (n, k) quasi-cyclic code, such that every cyclic shift of a codeword by p symbols yields another codeword, can be encoded by using p generator polynomials and an (v = n–k+p–1)-stage shift register*.
D
Select a generator polynomial g(n– i–1)modp*xp–1–{(n–i–1)modp} at time i, where i = 0 is defined as the time that the first v information bits are stored in the v-stage shift registers; v = 96+15–1 = 110 for a rate-14/15 LDPC code and v = 96*4+15–1 = 398 for a rate-11/15 LDPC code.
+
D
+
…
D
+
information bits
parity bits
information bits
…
(for x0)
(for x1)
(for xv– 1)
0
(Zero is selected after k information bits are received)
* H. Yamagishi and M. Noda, Proc. IEEE, pp.78-83, Sep. 2008

## Slide 14: Performance comparison of LDPC decoders
[1] K. Okada, et al., IEEE J. Solid State Circuits, vol. 48, no.1, pp. 46-65, Jan. 2013
[2] S-Y. Hung, et al., Proc. IEEE (ASSCC), Nov. 2010.
[3] J.L. Coz, et al., ISSCC Dig, pp.336-337, Feb. 2011
none
CMOS process
core area (mm2)
6.45
SOI 65nm LP
max. user rate (Gb/s)
codeword length (bits)
1440
power at BER = 10–6 (mW)
error floor at BER = 10–11
energy efficiency (pJ/bit)
Okada,
2013 [1]
Coz,
2011 [3]
1944
672
Hung,
2010 [2]
IEEE802 standard
15.3c
15.3c
11n
5.79
0.693
65nm LP
40nm LP
2
1.56
0.46
288
361
76
not confirmed
supply voltage (V)
1.1
operation frequency (MHz)
288
360
all BB
chip configuration
LDPC only
LDPC only
not confirmed
1.0
197
1.2
62.4
416
11.8
1/5
1/35
A quasi-cyclic LDPC code with a regular structure simplifies the decoder

## Slide 15: Index for HRCP-SC PHY
Channelization of HRCP-SC PHY
Modulation and coding
Frame format
Preamble
MCS Evaluation

## Slide 16: Frame header construction process
PHY
header
MAC
header
HCS
PHY header
MAC header
Append and scramble
HCS
caluculation
scrambled
Extended Hamming
encode
Spreader
π/2-shift BPSK
mapper
Subblock
builder
PHY
header
MAC
header
HCS
scrambled
coded
scramble
Scrambled
stuff
bits
Stuff bits

## Slide 17: PHY header format
Field Name | Number of bits | Start bit | Description
MCS | 3 | 0 | Index into the Modulation and Coding Scheme table
Pilot word | 1 | 3 | Shall be set to 1 if the pilot word is used
Scrambler seed ID | 4 | 4 | The initial state for payload scrambling
Reserved | 4 | 8 | Set to 0, ignored by the receiver
Frame length | 20 | 13 | Number of data octets in the PSDU

## Slide 18: 16-bit Header CRC for HCS
Bit-error Rate, bER
Undetected Error Probability
generator polynomial: 1A12B (TG3e, dmin = 6), 11021 (ITU-T, dmin = 4)
1-error event/10 years
for 1 G packets/day
CRC: cyclic-redundancy-check code
dmin: minimum Hamming distance
code-word length = 128 bits

## Slide 19: Header FEC: (8, 4) Extended Hamming (EH) Code
source bits |  |  |  | parity bits |  |  | 
i0 | i1 | i2 | i3 | p0 | p1 | p2 | p3
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1 | 1 | 1 | 0
0 | 0 | 1 | 0 | 1 | 0 | 1 | 1
0 | 0 | 1 | 1 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 1 | 1 | 0 | 0 | 1
0 | 1 | 1 | 0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 0 | 0 | 1 | 0
1 | 0 | 0 | 0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | 0 | 1 | 1 | 0
1 | 0 | 1 | 1 | 1 | 0 | 0 | 0
1 | 1 | 0 | 0 | 1 | 0 | 1 | 0
1 | 1 | 0 | 1 | 0 | 1 | 0 | 0
1 | 1 | 1 | 0 | 0 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Table for encoding
source data
coded data
4-bit source word
4-bit parities
Schematic view for header encoding
Why EH Code ?
a code with a short codeword length
reasonable minimum Hamming distance of four
Easy to soft decode by using:
complete maximum likelihood decoding or
simplified version such as Chase algorithm*
-> approx. 3 dB gain compared with spreading
* D. Chase, IEEE Trans. Info. Theory, vol. 18, no. 1, pp. 170-182, Jan. 1972.

## Slide 20: Simple receiver: advantage of short coded header
DL
MUX
Demod
header/payload mod
Sync &
Header
Dec
header/payload timing
D: delay operator
received signal
received data
Payload
Dec
A block diagram of a receiver
This block can be removed.
(a) conventional
Preamble
MCS
Length etc.
Payload
(b) improved
Timing diagram of header/payload mod
received signal
L
L
L: demod delay

## Slide 21: Index for HRCP-SC PHY
Channelization of HRCP-SC PHY
Modulation and coding
Frame format
Preamble
MCS Evaluation

## Slide 22: Proposed preamble structure
Frame format
TG3e
Preamble
Header
Payload
–a
b
a
b
a
–b
a
b
–a
b
a
a
a
a
b
first transmitted
last transmitted
transmission order
reference:
IEEE 802.15.3c SC, HR
a
a
a
–a
–a
a
b
a
–b
a
b
a
–b
a
b
a
SYNC
14 GCSs
SFD
4 GCSs
CES
9 GCSs
128*27 = 3456 chips: 1.96 µs
SYNC
14 GCSs
SFD
1 GCS
CES
11 GCSs
128*26 = 3328 chips: 1.89 µs
GCS: Golay complementary sequence, a or b, here 128-bit length
SYNC: synchronization sequence
SFD: start frame delimiter
CES: channel-estimation sequence

## Slide 23: Proposed Golay Complementary Sequences (GCSs)
a128 | b128
+1 –1 +1 –1 –1 +1 –1 +1 –1 +1 –1 +1 –1 +1 –1 +1 –1 +1 +1 –1 –1 +1 +1 –1 +1 –1 –1 +1 –1 +1 +1 –1 +1 +1 –1 –1 –1 –1 +1 +1 –1 –1 +1 +1 –1 –1 +1 +1 –1 –1 –1 –1 –1 –1 –1 –1 +1 +1 +1 +1 –1 –1 –1 –1 –1 –1 –1 –1 +1 +1 +1 +1 +1 +1 +1 +1 +1 +1 +1 +1 +1 +1 –1 –1 +1 +1 –1 –1 –1 –1 +1 +1 +1 +1 –1 –1 –1 +1 +1 –1 +1 –1 –1 +1 +1 –1 –1 +1 +1 –1 –1 +1 +1 –1 +1 –1 +1 –1 +1 –1 –1 +1 –1 +1 +1 –1 +1 –1 | +1 –1 +1 –1 –1 +1 –1 +1 –1 +1 –1 +1 –1 +1 –1 +1 –1 +1 +1 –1 –1 +1 +1 –1 +1 –1 –1 +1 –1 +1 +1 –1 +1 +1 –1 –1 –1 –1 +1 +1 –1 –1 +1 +1 –1 –1 +1 +1 –1 –1 –1 –1 –1 –1 –1 –1 +1 +1 +1 +1 –1 –1 –1 –1 +1 +1 +1 +1 –1 –1 –1 –1 –1 –1 –1 –1 –1 –1 –1 –1 –1 –1 +1 +1 –1 –1 +1 +1 +1 +1 –1 –1 –1 –1 +1 +1 +1 –1 –1 +1 –1 +1 +1 –1 –1 +1 +1 –1 –1 +1 +1 –1 –1 +1 –1 +1 –1 +1 –1 +1 +1 –1 +1 –1 –1 +1 –1 +1
Two complementary form of the GCSs a128 and b128 with a length of 128
The GCSs are transmitted from left to right, up to down
Hexadecimal form of the GCSs a128 and b128 with a length of 128
The GCSs are transmitted from left to right where the left-most bit is transmitted first in time.
a128 | b128
A5556696C33300F00FFFCC3C6999AA5A | A5556696C33300F0F00033C3966655A5

## Slide 24: Side-lobe comparison of SFD
(a) 15.3c
Time Slot
(b) TG3e
Time Slot
r: a noiseless received sequences
R: a reference sequence= [a128 –a128]
Cross Correlation of
r and R
SYNC
CES
SFD
+256
+14
–16
Cross Correlation of
r and R
+22
+256
–26
SYNC
CES
SFD
The last 3 GCS of SFD in 15.3c are used for detection of the header rate, either medium rate (MR) or high rate (HR).
–38 %
–36 %
The new Golay sequence reduces the side-lobe level of SFD by 36%

## Slide 25: Performance of SFD and header FEC
CNR dependence of FER
Frame-error Rate, FER
Carrier to Noise Ratio, CNR (dB)
0.9 dB gain
Pmd: calculated missed detection probability (failure at the correct position)
Pfa: calculated false alarm probability (failure at the incorrect position)
a threshold for SFD detection: 80
payload: MCS0 10 octets

## Slide 26: Performance comparison of channel estimation
Time Slot
a128
–a128
a128
b128
a128
–b128
a128
b128
–a128
b128
a128
a128
CES
SYNC
a512
b512
a256
b128
SFD
a128
b128
–b256
–a128
a128
b128
a128
–b128
a128
b128
a128
–b128
a128
a128
CES
SYNC
a256
–a128
a128
b128
a128
SFD
b256
a256
b256
b128
dual peak with 512
128-symbol ZCC
Cross Correlation
single peak with 1024
256-symbol ZCC
Cross Correlation
Time Slot
(b) TG3e
(a) 15.3c
The new CES doubles the zero-cross correlation (ZCC) zone

## Slide 27: Index for HRCP-SC PHY
Channelization of HRCP-SC PHY
Modulation and coding
Frame format
Preamble
MCS Evaluation

## Slide 28: Channel model used in PHY evaluation*
Channel model
Power delay profile obtained from the measurement1
Sample# (oversample=4) | Time [nsec] | Average Level [dB] | K-factor [dB] | Phase
1 | 0.000 | 0.0 | 24.0 | 0°
2 | 0.145 | -5.4 | 20.0 | random
3 | 0.290 | -16.0 | 15.5 | random
4 | 0.435 | -27.3 | 0.0 | random
5 | 0.580 | -36.2 | 8.5 | random
6 | 0.725 | -39.0 | 9.0 | random
7 | 0.870 | -39.6 | 14.5 | random
8 | 1.015 | -46.5 | 12.0 | random
9 | 1.160 | -53.2 | 0.0 | random
10 | 1.305 | -47.4 | 17.5 | random
11 | 1.450 | -55.5 | 0.0 | random
12 | 1.595 | -48.7 | 17.0 | random
13 | 1.740 | -51.1 | 11.0 | random
14 | 1.885 | -51.6 | 12.5 | random
15 | 2.030 | -55.6 | 10.3 | random
16 | 2.175 | -53.7 | 20.0 | random
17 | 2.320 | -56.1 | 18.0 | random
18 | 2.465 | -56.6 | 16.5 | random
19 | 2.610 | -57.2 | 20.0 | random
20 | 2.755 | -58.1 | 17.5 | random
Chart: τ [nsec]
| 0 | 0.14499999999999999 | 0.28999999999999998 | 0.435 | 0.57999999999999996 | 0.72499999999999998 | 0.87 | 1.0149999999999999 | 1.1599999999999999 | 1.3049999999999999 | 1.45 | 1.595 | 1.74 | 1.885 | 2.0299999999999998 | 2.1749999999999998 | 2.3199999999999998 | 2.4649999999999999 | 2.61 | 2.7549999999999999 | 2.9 | 3.0449999999999999 | 3.19 | 3.335 | 3.48 | 3.625 | 3.77 | 3.915 | 4.0599999999999996 | 4.2050000000000001 | 4.3499999999999996 | 4.4950000000000001 | 4.6399999999999997 | 4.7850000000000001 | 4.93 | 5.0750000000000002 | 5.22 | 5.3650000000000002 | 5.51 | 5.6550000000000002
 | 0 | -5.4 | -16 | -27.3 | -36.2 | -39 | -39.6 | -46.5 | -53.2 | -47.4 | -55.5 | -48.7 | -51.1 | -51.6 | -55.6 | -53.7 | -56.1 | -56.6 | -57.2 | -58.1 | -63.7984 | -61.3805 | -60.6863 | -59.2819 | -63.2943 | -60.4321 | -60.1449 | -62.672 | -60.4666 | -58.0135 | -64.9436 | -64.8412 | -63.2335 | -66.234 | -66.0491 | -66.1352 | -65.9743 | -66.26 | -65.2724 | -71.9515
*K. Hiraga, 15-0656/r00

## Slide 29: Parameters used for power-amplifier and phase-noise models
Power Amplifier
Phase Noise
AM-AM:
AM-PM:
parameter | value
G | 3.3
p | 4.2
Vsat | 1.413 V (13 dBm)
α | 8.2 x 105
β | 0.326
q1 | 10.6
q2 | 8.0
Output Back off from Vsat | 15 dB
parameter | value | 
Modulation | QPSK, 16QAM, 64QAM | 256QAM
PSD(0) | −90 dBc/Hz | 
fz | 8.1 × 107 Hz | 5.18 × 107 Hz
fp | 5.79 × 105 Hz | 2.60 × 105 Hz
PSD(1MHz) | −96 dBc/Hz* | −102 dBc/Hz
PSD( Infinity). | −133 dBc/Hz | −136 dBc/Hz
*Musa, et al., IEEE ASSC, 2010

## Slide 30: AM-PM/AM-AM 2-tone measurement setup
AWG
12 GS/s
60GHz RF Tx
Spectrum Analyzer
20Hz – 67GHz
5mm
Ich
Qch
Horn Ant.
24dBi
Agilent
M8190A
Rohde & Schwarz
FSU67
Baseband Signal
RF Signal
AM-AM distortion is derived by sets of baseband and RF signal power
AM-PM distortion  in degree can be calculated as*:
Baseband Signal
RF Signal
*C. F. Campbell and S. A. Brown, IEEE Symp. on Emerging Tech., 2001.
An example combination of base band signal and resulting RF signal in AM-PM measurement
ATT

## Slide 31: AM-AM/AM-PM measurement results for a direct-conversion 60 GHz CMOS RF transceiver*
Chart: Input Power [dBm]
| 5.1053143969999999 | 4.6187130390000002 | 4.1721868410000003 | 3.6518139490000001 | 3.1270750569999999 | 2.6006223579999999 | 2.1187180950000002 | 1.5876104520000001 | 1.0701305459999999 | 0.54068158799999999 | 5.4209610999999998E-2 | -0.45162224000000001 | -0.92033708299999994 | -1.4382233680000001 | -1.9350749730000001 | -2.4327356880000002 | -2.7931602280000001 | -3.3066006360000002 | -3.7977604650000001 | -4.3322347130000001 | -4.8671583040000002 | -5.3863214079999997 | -5.8583791449999998 | -6.3588068010000001 | -6.8092969759999997 | -7.3379716119999996 | -7.8354697590000004 | -8.3611147839999997 | -8.8683561359999992 | -9.3623819469999994 | -9.8002186400000006 | -10.29706764 | -10.755778019999999 | -11.286671910000001 | -11.76871832 | -12.29847004 | -12.85166939 | -13.37077021 | -13.84605638 | -14.365256390000001
AM-AM meas. | 13.022 | 12.8776 | 12.7922 | 12.6611 | 12.4751 | 12.2633 | 12.0235 | 11.694 | 11.3574 | 10.9481 | 10.5585 | 10.0817 | 9.5969 | 9.0476 | 8.5591 | 8.015 | 7.586 | 7.039 | 6.5263 | 5.9633 | 5.4017 | 4.8377 | 4.3336 | 3.7921 | 3.2242 | 2.7041 | 2.1842 | 1.6279 | 1.1002 | 0.52292 | 0.063364 | -0.48488 | -1.0259 | -1.5715 | -2.056 | -2.6078 | -3.1359 | -3.6743 | -4.1365 | -4.6434
Rappmodel AM-AM | 13.0021 | 13.0017 | 13.0009 | 12.9997 | 12.9976 | 12.9944 | 12.9891 | 12.9807 | 12.9671 | 12.9455 | 12.9115 | 12.8586 | 12.7783 | 12.6601 | 12.4934 | 12.2698 | 11.9865 | 11.6471 | 11.2603 | 10.8369 | 10.3871 | 9.9194 | 9.4399 | 8.9527 | 8.4607 | 7.9657 | 7.4688 | 6.9707 | 6.4719 | 5.9726 | 5.473 | 4.9733 | 4.4735 | 3.9736 | 3.4736 | 2.9737 | 2.4737 | 1.9737 | 1.4737 | 0.97375 | 0.47375 | -0.026248
AM-PM meas. | 18.2665 | 15.6397 | 13.4207 | 10.9499 | 8.7384 | 6.8165 | 5.3062 | 3.8409 | 2.7437 | 1.7921 | 1.1522 | 0.63109 | 0.2813 | 0.03451 | 0.010514 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Modified Rappmodel AM-PM | 104.5922 | 90.0465 | 77.5203 | 66.732 | 57.4388 | 49.4312 | 42.5282 | 36.5734 | 31.4307 | 26.9819 | 23.1233 | 19.7634 | 16.8212 | 14.2246 | 11.9106 | 9.8268 | 7.9357 | 6.2207 | 4.6902 | 3.3737 | 2.3038 | 1.4938 | 0.92439 | 0.5505 | 0.31839 | 0.18032 | 0.10066 | 0.05565 | 0.030574 | 0.016728 | 0.009129 | 0.0049736 | 0.0027068 | 0.0014722 | 0.00080034 | 0.00043498 | 0.00023637 | 0.00012843 | 6.978e-05 | 3.7911e-05
*S. Kawai, et al., RFIC Symp., pp. 137-140, June 2013.

## Slide 32: Block diagram of simulator
MOD
Tx
Filter
FDE
DEM
Ch. Model
ECC DEC
ECC
ENC
CES/Pw
Ins.
PLL
Ch. Estimate
user data
received user data
coded data
payload symbols
frame
symbols
baseband signal
Tx signal
Rx signal
received
baseband signal
received
payload
symbols
Rx filter
received
frame
recovered
frame
received
coded data
Tx phase noise
PA non-linearity
Rx phase noise
AWGN

## Slide 33: MCS performance, FER v.s. Eb/N0 with RF impairments and channel model
frame length = 214 B
Eb/N0 (dB)
Frame-error Rate, FER (dB)
FER = 0.08
Chart: 
| -1.074857 | -0.874857 | -0.67485700000000004 | -0.47485699999999997 | -0.27485700000000002 | -7.4857000000000007E-2 | 0.125143 | 0.32514300000000002 | 0.52514300000000003 | 0.72514299999999998 | 0.92514300000000005 | 1.125143 | 1.325143 | 1.5251429999999999 | 1.7251430000000001 | 1.925143 | 2.125143 | 2.3251430000000002 | 2.5251429999999999 | 2.7251430000000001 | 2.9251429999999998 | 3.125143 | 3.3251430000000002 | 3.5251429999999999 | 3.7251430000000001 | 3.9251429999999998 | 4.1251429999999996 | 4.3251429999999997 | 4.5251429999999999
QPSK 11/15 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0.93333 | 0.48182 | 0.17414 | 0.048095
QPSK 14/15 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0.95833 | 0.7 | 0.34 | 0.11444 | 0.033893
16QAM 11/15 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0.80714 | 0.35333 | 0.12024 | 0.035714
16QAM 14/15 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0.925 | 0.63125 | 0.255 | 0.1 | 0.031646
64QAM 11/15 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0.94167 | 0.75714 | 0.5 | 0.26579 | 0.14286 | 0.052632
64QAM 14/15 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0.98333 | 0.82143 | 0.55556 | 0.2381 | 0.11744 | 0.04065
256QAM 14/15 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0.96667 | 0.86667 | 0.585 | 0.4 | 0.22083 | 0.098077 | 0.052083
 | 0.08 | 0.08

## Slide 34: MCS performance, FER v.s. Eb/N0 in AWGN
frame length = 214 B
Chart: 
| -1.6554070000000001 | -1.4554069999999999 | -1.2554069999999999 | -1.055407 | -0.85540700000000003 | -0.65540699999999996 | -0.45540700000000001 | -0.255407 | -5.5406999999999998E-2 | 0.144593 | 0.34459299999999998 | 0.54459299999999999 | 0.74459299999999995 | 0.94459300000000002 | 1.144593 | 1.3445929999999999 | 1.5445930000000001 | 1.7445930000000001 | 1.944593 | 2.144593 | 2.3445930000000001 | 2.5445929999999999 | 2.7445930000000001 | 2.9445929999999998 | 3.144593 | 3.3445930000000001 | 3.5445929999999999 | 3.7445930000000001 | 3.9445929999999998
QPSK 11/15 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0.98684 | 0.64871 | 0.23813 | 0.063025 | 0.016171 | 0.004386
QPSK 14/15 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0.96474 | 0.72837 | 0.34954 | 0.12215 | 0.04162 | 0.011886 | 0.0030834
16QAM 11/15 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0.99671 | 0.90179 | 0.56716 | 0.2027 | 0.062604 | 0.016741 | 0.0048898
64QAM 11/15 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0.98397 | 0.73077 | 0.35164 | 0.12885 | 0.043005 | 0.012802 | 0.0032903
64QAM 14/15 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0.96795 | 0.78906 | 0.44265 | 0.17857 | 0.062708 | 0.023049 | 0.0077018
256QAM 14/15 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0.98684 | 0.90179 | 0.61089 | 0.30793 | 0.13298 | 0.051796 | 0.018012 | 0.0061881
 | 0.08 | 0.08
Eb/N0 (dB)
Frame-error Rate, FER (dB)
FER = 0.08

## Slide 35: Link budget of SC PHY using a single channel
*incorporating RF impairments and channel model
MCS |  | MCS0 | MCS1 | MCS2 | MCS3 | MCS4 | MCS5 | MCS6
Tx | frequency for CH4 (GHz) | 64.8 | 64.8 | 64.8 | 64.8 | 64.8 | 64.8 | 64.8
 | PHY-SAP bit rate (Gb/s) | 2.5813 | 3.2853 | 5.1627 | 6.5707 | 7.7440 | 9.8560 | 13.1413
 | Tx power (dBm) | -23.72 | -20.57 | -16.98 | -13.69 | -10.92 | -7.4 | -1.62
 | Tx antenna gain (dBi) | 6 | 6 | 6 | 6 | 6 | 6 | 6
channel | distance(m) | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1 | 0.1
 | 1m loss (dB) | 68.67 | 68.67 | 68.67 | 68.67 | 68.67 | 68.67 | 68.67
 | path Loss (dB) | -20.00 | -20.00 | -20.00 | -20.00 | -20.00 | -20.00 | -20.00
 | propagation loss index | 2 | 2 | 2 | 2 | 2 | 2 | 2
 | Rx input level (dBm) | -66.39 | -63.24 | -59.65 | -56.36 | -53.59 | -50.07 | -44.29
 | average noise power per bit (dBm) | -79.88 | -78.83 | -76.87 | -75.82 | -75.11 | -74.06 | -72.81
Rx | Rx antenna gain (dBi) | 6 | 6 | 6 | 6 | 6 | 6 | 6
 | noise figure (dB) | 8 | 8 | 8 | 8 | 8 | 8 | 8
 | implementation loss (dB) | 6 | 6 | 6 | 6 | 6 | 6 | 6
 | shadowing margin (dB) | 1 | 1 | 1 | 1 | 1 | 1 | 1
 | receiving Eb/N0 (dB) | 4.49 | 6.59 | 8.22 | 10.46 | 12.52 | 14.99 | 19.52
required Eb/N0* |  | 4.49 | 6.59 | 8.22 | 10.46 | 12.52 | 14.99 | 19.52
margin |  | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00

## Slide 36: END