## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Proposal for SRM specific MAC PIB in Technical Guidance Document]
Date Submitted: [xx September, 2015]
Source: [Hidetoshi Yokota and Ruben Salazar] Company [Landis&Gyr]
Address: [1-2-9 Nishi Shimbashi Minato-ku, Tokyo 105-0003, Japan,
30000 Mill Creek Av., Alpharetta, GA 30022, USA ]
Voice: [+81 3-5532-7455, +1 678 258 3165], E-Mail:[hidetoshi.yokota@landisgyr.com, ruben.salazar@landisgyr.com]
Re: [“TG4s Technical Guidance Document”, IEEE 802.15-14-0555-06-004s]
Abstract: [This contribution proposes SRM MAC specific PIB attributes that should be considered in the Technical Guidance Document for measuring spectrum resources in WPAN.]
Purpose: [Discussion and approval]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
Proposal for SRM specific MAC PIB in Technical Guidance Document
Authors:

## Slide 3: Outline of the proposal
Propose SRM specific MAC PIB
  Required metrics in Table 1 in Section 5
Discussion
  Handling of ambiguous definitions
  Addition or removal of metrics
References [1] IEEE802.15.4-REVc-D00
[2] IEEE802.15.4-0555-06-004s (TGD)

## Slide 4: ED (Energy Detection) [Sec.10.2.5]
The average of the received signal power over 8 symbol periods
The minimum and maximum values of ED are 0x00 and 0xff
The received power in units of dB is linearly mapped between these values
[Channel load]

## Slide 5: Percentage of time of failed transmissions (No Ack)
macFailTxTime
=
linearly distributed in 0x00-0xff
[Channel load]
fail tx time [1]
Measurement time
NoAck
1+ macMaxFrameRetries
fail tx time [2]
NoAck
1+ macMaxFrameRetries

## Slide 6: Percentage of time of deferred transmissions (CCA)
macDeferredTxTime =
linearly distributed in 0x00-0xff
[Channel load]
back off period
busy
Measurement time
ACK
back off period
busy
ACK

## Slide 7: Channel Utilization
Total channel used time for Tx and Rx and occupied time for the other devices over the measurement duration, linearly scaled with 255 representing100%
Channel Busy Time:
  Total time of Tx and Rx of all Frames and ACKs
  If CCA mechanism reported a busy medium, time period from the beginning of the current transmission attempt to the next transmission attempt is also added
    In the case of TSCH, this time period is from the beginning of the initial transmission attempt until the beginning of the next assigned transmit timeslot
“Channel load” is defined in Sec.10.11.9.3 IEEE802.11-2012 for reference
[Channel load]

## Slide 8: LQI (Link Quality Indicator) [Sec.10.2.6]
A characterization of the strength and/or quality of a received packet
The minimum and maximum LQI values (0x00 and 0xff) should be associated with the lowest and highest quality compliant signals detectable by the receiver, and LQI values in between should be uniformly distributed between these two limits
[Link Statistics]

## Slide 9: Transmit Power Used
The actual power used as measured at the output of the antenna connector, in units of dBm (defined in 8.4.1.20 IEEE802.11-2012)
The minimum and maximum values are 0x00 and 0xff and the values in between should be uniformly distributed
[Link Statistics]

## Slide 10: Max Transmit Power
The upper limit, in units of dBm, on the transmit power as measured at the output of the antenna connector to be used by the device on the current channel (defined in 8.4.1.19 IEEE802.11-2012)
The minimum and maximum values are 0x00 and 0xff and the values in between should be uniformly distributed
[Link Statistics]

## Slide 11: Received Channel Power Indicator (RCPI)
The total channel power (signal, noise, and interference) of the entire received frame measured on the channel and at the antenna connector used to receive the frame (defined in 20.3.2.16 IEEE802.11-2012)
RCPI shall be a monotonically increasing, logarithmic function of the received power level defined in dBm. The allowed values shall be an 8 bit value in the range from 0 to 220
[Link Statistics]
0
-110
-109.5
-109
-0.5
0
220
219
1
2

## Slide 12: Received Signal Noise Indicator (RSNI)
The signal to noise plus interference ratio of a received frame, which is defined by the ratio of the received signal power (RCPI-ANPI) to the noise plus interference power (ANPI) as measured on the channel and at the antenna connector used to receive the frame (defined 10.11.9.2 in IEEE802.11-2012)
Averaged IPI Density can be used for ANPI
[Link Statistics]

## Slide 13: Received Signal Noise Indicator (RSNI) cont’d
IPI Density in the specified channel as a function of time over the measurement duration where the channel is idle (CCA indicates idle and no Tx or Rx) (10.11.9.4 in IEEE802.11.2012)
[Link Statistics]
0
9
10
8
IPI level
8
9
10
8
9
DIPI=10

## Slide 14: Received Signal Strength Indicator (RSSI) [Table 129]
The RF power level at the input of the transceiver measured during the PHR and is valid after the SFD is detected
The minimum and maximum values are 0x00 and 0xff and the values in between should be uniformly distributed
[Link Statistics]

## Slide 15: Noise Histogram
A power histogram measurement of non-IEEE 802.15 noise power by sampling the channel when CCA indicates idle and the device is neither transmitting nor receiving a frame
Defined in 4.3.8.7 and 10.11.9.4 in IEE802.11
[Interference measurement]

## Slide 16: Average Access Delay
The average medium access delay for transmitted frames measured from the time the MPDU is ready for transmission until the actual frame transmission start time
  In the case of TSCH, macTsTxOffset can be used calculate Access Delay time
Defined in Sec.10.11.16 in IEE802.11
[Node statistics]

## Slide 17: SRM Requirement [Table 1]

## Slide 18: Discussion
Node statistics attributes
  Most of the existing performance metrics are supported, but not all
  What about the rest?

## Slide 19: Discussion (cont’d)
Link statistics attributes
  Link quality: LQI, RSQI
  Signal strength: RCPI (frame), RSSI (PHR)
  Signal to Noise: RSNI
Definitions are all different
All needed or selection?