## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Proposed Resolution on some Rouge comments of LB 110
Date Submitted: Oct., 2015
Source: Jaehwan Kim, Sangjae Lee (ETRI), Jaebeom Kim, Jina Han, Youngbae Ko (Ajou Univ.), Soo-Young Chang (SYCA), and Sangsung Choi (ETRI)
Company: ETRI, Ajou Univ., SYCA
Address:
Voice: +82 42 850 5338, E-Mail: kimj@etri.re.kr
Re:
Abstract:
Purpose: To suggest a comment resolution for Letter Ballot #110
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Comment CID R1087
Commentor
  Charlie Perkins
Related clause
  5.2.1 P 23 line 38
Comment
  "SHR preamble code for UWB PHY [##]"
Proposed Change
  Citation needed, along with an escape code for non-UWB PHY

## Slide 3: Proposed resolution for CID R1087
Accept in Principle:
  Modify citation: "SHR preamble code when the L2R mesh is used on a UWB PHY [IEEE 802.15.4-2011]“ in Table 17, in 6.2.4.1.

## Slide 4: Comment CID R1112
Commentor
  Charlie Perkins
Related clause
  5.2.4.3 P 29 line 26
Comment
  Does "described in 4.3." refer to clause 4.3 in this document?
Proposed Change
  Check and correct if necessary.

## Slide 5: Proposed resolution for CID R1112
Accept: related reference is changed to 5.4.1.3
The details of multi-channel route establishment procedure is described in 5.4.1.3 and figure 23.
Rewrite of the Subclause is found in doc. #15-0788-00

## Slide 6: Comment CID R1132
Commentor
  Charlie Perkins
Related clause
  5.4.1.3 P 37 line 47
Comment
  "a CAP, a CFP and a BOP." looks very mysterious
Proposed Change
  Citation needed along with a short explanation.

## Slide 7: Proposed resolution for CID R1132
Accept in Principle:
Inserted full name in 3.2 Acronyms and abbreviations section
CAP : Contention Access Period
CFP : Contention Free Period
BOP : Beacon Only Period

## Slide 8: Comment CID R1140
Commentor
  Charlie Perkins
Related clause
  5.4.1.3 P 38 line 36
Comment
  "device 5-1 (t0)" refers to undefined device and time value
Proposed Change
  Explain what device 5-1 and t0 mean. Could use a subscript for t0.

## Slide 9: Proposed resolution for CID R1140
Accept in Principle: related sentences and figure are modified.
“The detail of data forwarding in MCO environment is as below. If PAN coordinator 1 wants to send a frame to Device 5-1 at t0, it forwards the frame to PAN coordinator 4 while they are operating on channel 1.”

## Slide 10: Comment CID R1142
Commentor
  Charlie Perkins
Related clause
  5.4.1.3 P 38 line 38
Comment
  "PAN ID 5 (t1)" refers to undefined time value t1
Proposed Change
  Explain what t1 means. Could use a subscript for t1.

## Slide 11: Proposed resolution for CID R1142
Accept in Principle: related sentences and figure are modified.
“PAN coordinator 4 waits for the next CAP or CFP in channel 4 and forwards the frame to PAN coordinator 5 at t1”

## Slide 12: Comment CID R1143
Commentor
  Charlie Perkins
Related clause
  5.4.1.3 P 38 line 39
Comment
  "wait next periods" seems wrong
Proposed Change
  Clarify wording.

## Slide 13: Proposed resolution for CID R1143
Accept in Principle: related sentences and figure are modified.
“PAN coordinator 5 finally transmits the frame to Device 5-1 during the CAP or the CFP of channel 5 at t2.”

## Slide 14: Comment CID R1144
Commentor
  Charlie Perkins
Related clause
  5.4.1.3 P 38 line 39
Comment
  "device 5-1 (t2)" refers to undefined device and time value
Proposed Change
  Similar to comment on row 144

## Slide 15: Proposed resolution for CID R1144
Accept: related sentences and figure are modified.
“PAN coordinator 5 finally transmits the frame to Device 5-1 during the CAP or the CFP of channel 5 at t2.”

## Slide 16: Comment CID R1145
Commentor
  Charlie Perkins
Related clause
  5.4.1.3 P 39 line 1
Comment
  Figure 23 is not referenced in the text, and is hard to understand.
Proposed Change
  Provide additional explanation for the figure

## Slide 17: Proposed resolution for CID R1145
Accept in Principle: related figure is referenced in the text
“Figure 23 shows an example of the multichannel routing in TMCTP topology (the details related to superframe scheduling and multichannel topology construction is described in IEEE std. 802.15.4m-2014) as presented in Figure 22.”