## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Proposal for IEEE802.15.3e - PHY MIMO supporting material]
Date Submitted: [9 November 2015]
Source: [Ken Hiraga(1), Jae Seung Lee, Itaru Maekawa, Makoto Noda, Ko Togashi, (representative contributors), all contributors are listed in “Contributors” slide]
Company: [ETRI, JRC, NTT1, Sony, Toshiba]
Address1: [Hirarinooka 1-1, Yokosuka Japan]
E-Mail1: [hiraga.ken@lab.ntt.co.jp (all contributors are listed in “Contributors” slide)]
Abstract: This document is a supporting document for MIMO design in PHY draft proposal for HRCP.
Purpose: To propose a full set of specifications for TG 3e.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributors acknowledge and accept that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
Contributors
Name | Affiliation | Email
Jae Seung Lee | ETRI | jasonlee@etri.re.kr
Moon-Sik Lee | ETRI | moonsiklee@etri.re.kr
Itaru Maekawa | Japan Radio Co., Ltd. | maekawa.itaru@jrc.co.jp
Doohwan Lee | NTT Corporation | lee.doohwan@lab.ntt.co.jp
Ken Hiraga | NTT Corporation | hiraga.ken@lab.ntt.co.jp
Hideki Toshinaga | NTT Corporation | toshinaga.hideki@lab.ntt.co.jp
Masashi Shimizu | NTT Corporation | masashi.shimizu@upr-net.co.jp
Keitarou Kondou | Sony Corporation | Keitarou.Kondou@jp.sony.com
Hiroyuki Matsumura | Sony Corporation | Hiroyuki.Matsumura@jp.sony.com
Makoto Noda | Sony Corporation | MakotoB.Noda at jp.sony.com
Masashi Shinagawa | Sony Corporation | Masashi.Shinagawa@jp.sony.com
Ko Togashi | Toshiba Corporation | ko.togashi@toshiba.co.jp
Kiyoshi Toshimitsu | Toshiba Corporation | kiyoshi.toshimitsu@toshiba.co.jp

## Slide 3: 1. 7/8 adds complexity and is not needed because rates are very close to 14/15.
Modulation | Code Rate | PHY transmission rate, Gbit/s |  |  |  |  |  |  |  |  | 
 |  | SISO |  | 2 x 2 |  | 4 x 4 |  | 9 x 9 |  | 16 x 16 | 
 |  | without pilot word | with pilot word* | without pilot word | with pilot word* | without pilot word | with pilot word* | without pilot word | with pilot word* | without pilot word | with pilot word*
QPSK | 14/15 | 3.3 | 2.9 | 6.6 | 5.7 | 13.1 | 11.5 | 29.6 | 25.9 | 52.6 | 46.0
16QAM | 11/15 | 5.2 | 4.5 | 10.3 | 9.0 | 20.7 | 18.1 | 46.5 | 40.7 | 82.6 | 72.3
16QAM | 14/15 | 6.6 | 5.7 | 13.1 | 11.5 | 26.3 | 23.0 | 59.1 | 51.7 | 105.1 | 92.0
64QAM | 11/15 | 7.7 | 6.8 | 15.5 | 13.6 | 31.0 | 27.1 | 69.7 | 61.0 | 123.9 | 108.4
64QAM | 14/15 | 9.9 | 8.6 | 19.7 | 17.2 | 39.4 | 34.5 | 88.7 | 77.6 | 157.7 | 138.0
MCS table was revised:
7/8 MCS were removed.
M = 9 is used instead of M = 8
  M = 9 modes have better BER than M = 8.

## Slide 4: Proposal to use M=9 instead of M=8
Chart: SNR[dB]
| 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35
LDPC7/8 | 0.38409 | 0.36566 | 0.34558 | 0.32299 | 0.30103 | 0.27864 | 0.25432 | 0.23077 | 0.20819 | 0.18573 | 0.16531 | 0.14535 | 0.1268 | 0.10947 | 0.092688 | 0.07577 | 0.058784 | 0.043804 | 0.030684 | 0.020189 | 0.013278 | 0.0089 | 0.0056491 | 0.0036665 | 0.0024784 | 0.0017738
LDPC3/4
LDPC1/2
No FEC
Chart: SNR[dB]
LDPC11/15
LDPC7/8
LDPC3/4
LDPC1/2
No FEC | 0.3444 | 0.32136 | 0.2969 | 0.27273 | 0.2483 | 0.22448 | 0.20068 | 0.1778 | 0.15601 | 0.13533 | 0.11586 | 0.097589 | 0.080631 | 0.064301 | 0.049803 | 0.036878 | 0.026259 | 0.017509 | 0.011094 | 0.0067834 | 0.00386 | 0.0021438 | 0.0011558 | 0.00062272 | 0.00034592 | 0.0002097 | 0.00012254 | 9.0526e-05 | 6.5758e-05 | 5.2685e-05 | 4.5177e-05
M=9
M=8
When M=9, (channel capacity / M) is higher than M=8.
-> correlation is low
When M=9, BER performance is better than M=8.
Chart: Transmission distance [mm]

## Slide 5: Channel aggregation and bonding
Channel # | Start frequency | Center frequency | Stop frequency
1 | 57.240 | 58.320 | 59.400
2 | 59.400 | 60.480 | 61.560
3 | 61.560 | 62.640 | 63.720
4 | 63.720 | 64.800 | 65.880
Frequency channels (same as 15.3c)
Channel aggregation
  2 channels: Ch1+Ch2， Ch1+Ch3， Ch1+Ch4， Ch2+Ch3， Ch2+Ch4， Ch3+Ch4
  3 channels:Ch1+Ch2+Ch3，Ch1+Ch2+Ch4，Ch1+Ch3+Ch4，Ch2+Ch3 + Ch4
  4 channels:Ch1+Ch2+Ch3+Ch4
Channel bonding
  2 channels: Ch2+Ch3
  3 channels: Ch1+Ch2+Ch3
  4 channels: Ch1+Ch2+Ch3+Ch4

## Slide 6: 2. Parallel preamble and SFD for all branches? Should we add cyclic shift delay?
SYNC and SFD have to have cyclic shift delay in order to avoid the deep reception level depression due to canceling effect caused by the interelement spacing.
DEV
PPC
If the same waveform is transmitted from all antennas…
Cancel each other when these path length difference is around half wavelength and causes deep depression in the reception level:

## Slide 7: 2. Parallel preamble and SFD for all branches? Should we add cyclic shift delay?
M - streams data
Payload #4
Payload #1
Payload #3
Payload #2
SYNC
CES
Tx#4
Tx#1
Tx#3
Tx#2
SFD
SYNC
SFD
SYNC
SFD
SYNC
SFD
Header #4
Header #1
Header #3
Header #2
CES
CES
CES
The value of cyclic shift for i th transmitter
TCSsync_i = 60 * ( i – 1 ) [ns].
The value of cyclic shift for i th transmitter
TCSsfd_i = 4 * ( i – 1 ) [ns].

## Slide 8: CES structure
Payload #4
Payload #1
Payload #3
Payload #2
SYNC
CES#1
Tx#4
Tx#1
Tx#3
Tx#2
SFD
SYNC
SFD
SYNC
SFD
SYNC
SFD
Header #4
Header #1
Header #3
Header #2
Payload #4
Payload #1
Payload #3
Payload #2
for MIMO transmission channel estimation
SYNC
CES #4
CES #1
0 values, unmodulated
Tx#4
Tx#1
CES #3
Tx#3
CES #2
Tx#2
same in each antenna element
SFD
SYNC
SFD
SYNC
SFD
SYNC
SFD
Header #4
Header #1
Header #3
Header #2
CES#2
CES#3
CES#4
Presented in Sep. meetings
Proposal
Golay sequences with cyclic shifts

## Slide 9: CES structure
8 chips CP inserted
Payload #i
CES# i
Tx#i
SYNC# i
SFD# i
Header # i
Ga64 = [-1 -1 +1 -1 +1 -1 -1 -1 +1 +1 -1 +1 +1 -1 -1 -1 -1 -1 +1 -1 +1 -1 -1 -1 -1 -1 +1 -1 -1 +1 +1 +1 -1 -1 +1 -1 +1 -1 -1 -1 +1 +1 -1 +1 +1 -1 -1 -1 +1 +1 -1 +1 -1 +1 +1 +1 +1 +1 -1 +1 +1 -1 -1 -1 ]
Frequency domain
Time domain waveform
TCSces_i = 4.5* ( i – 1 ) [ns]
M = 2, 4
72*8
= 576 chips
= 327 ns
64
8
72 chips
Ga64
8 repetitions
72
Cyclic shift
72
72
72
72
IFFT
…
72 * 8 repetitions

## Slide 10: CES structure
64
8
72 chips
Ga64
8 chips CP inserted
Payload #i
CES# i
Tx#i (i = 9 ~ 16)
SYNC# i
SFD# i
Header # i
Ga64 = [-1 -1 +1 -1 +1 -1 -1 -1 +1 +1 -1 +1 +1 -1 -1 -1 -1 -1 +1 -1 +1 -1 -1 -1 -1 -1 +1 -1 -1 +1 +1 +1 -1 -1 +1 -1 +1 -1 -1 -1 +1 +1 -1 +1 +1 -1 -1 -1 +1 +1 -1 +1 -1 +1 +1 +1 +1 +1 -1 +1 +1 -1 -1 -1 ]
Frequency domain
Time domain waveform
4 repetitions
72*4
= 288 chips
=164 ns
TCSces_i = 4.5* ( mod(i, 8) – 1 ) [ns]
72
Cyclic shift
72
M = 9, 16
164 ns
Payload #i
CES# i
SYNC# i
SFD# i
Header # i
Tx#i (i = 1 ~ 8)
72
72
72
IFFT

## Slide 11: 3. When is stable position assumed? How to know when device is stable?
DEV should start sending Array Training commands after DEV recognizes it is not moving around on the array surface of the PPC.
The method for the recognition is up to implementation, for example
  Use of NFC signal detection
  Use of optical camera imaging
  Use of timer, assuming the user stabilizes the positions of DEV within a certain time (e.g. 2 sec).
In draft, above is reflected in the description on the setup sequence.

## Slide 12: 4. What is the time interval of Association Request Commands? What is the duration of each Association Request Command?
MIMO setup sequence is revised as shown in the next slide.

## Slide 13
Comprises information below:
MIMO capability (M1)
Value of Nar (No. of Array training commands. Nar = 0 ~ 511, Nar ≤ Marray )
Value of Tar (Period of Array training commands, 10, 20, 40, or 80 )
Channel Agg. capability
Channel bond. capability
MIMO and ch agg./bond. mode
Beacon
・The number of Antenna training commands sent here is equal to Nar.
・These are transmitted from antenna element #1 to allow PPC to select antenna elements for following MIMO transmission.
・While transmissions of these commands the remaining number is counted down.
・Array training commands #1 ~ #Nar − 1 shall be No-ACK policy.
Only the last Array training command shall be Stack-ACK policy.
Switch to M-stream MIMO mode
with channel aggregation. or bonding.
SISO mode on Ch2
using the antenna element #1
SISO mode on Ch2
using the antenna element #1
Switch to M-stream MIMO mode (Antenna elements to be used are already selected) with channel aggrgation. or bonding.
DEV(Portable terminal)
PPC (Kiosk)
The number of MIMO branches: M2
The number of antenna elements: Marray (1~ 511)
The number of MIMO branches: M1 ( 1~16)
Antenna Selecting Procedure (in SISO on ch2)
・decides the number of branches, M,
(e.g. by determining “M=min(M1,M2)”. )
・Channel bonding or aggregation is decided as well.
Decision method is on implementations
Association request
Comprises information below:
・Value of M as MIMO capability field
・A channel Agg. or bond. as capability field
knows the number of MIMO branches to be used, M.
and channel aggregation/bonding.
Array training #Nar
Array training #Nar − 1
…
Array training #1
・Remaining time = (Nar – 1)
(1) when M < Marray
PPC selects M antennas
(Example of procedure selecting antenna: Select using reception levels)
Array training commands are sent Nar times, hence Nar antennas are switched on to receive these commands.
(2) when M = Marray
PPC does not have to select antenna element.
Ack
Association (in SISO on ch2)
Association response
Switch to antenna selecting mode
Switch to antenna selecting mode
Ready to listen the Array training commands.
Detect that DEV is stable position or timeout (e.g. 2 sec)
PHY frames with MIMO channel agg./bond.
The last Array training command received
If ACK for Array training #Nar is not received by DEV, Array training #Nar shall be retransmitted. The reception antenna shall be changed into another one, and after retransmissions the reception antenna is set to an element that successfully received Array training command before #Nar.
For example, start receiving Array Training using antenna element which has sent Association response.
Array training #2

## Slide 14: 5. Total 5 dBm tx power for 16 antennas
Reflected in the link budget table.

## Slide 15: 6. Link budget for all MIMO combinations, including channel aggregation.
6.1. Supporting material, specify all link budget
This table shows the link budget per all combinations for frequency channel.
Total transmission power should be multiplied by No. of channels.

## Slide 16: 6. Link budget for all MIMO combinations, including channel aggregation.
Transmitter specification: Same as SISO mode as shown in 12a.2.4
  Because each SISO signal stream is transmitted via each antenna.
Min receive level: added on 12a.2.8.10 (next slide)
6.2. Draft material, EVM, min receive level

## Slide 17: Min receive level
MIMO No. of branches | MCS | Receiver sensitivity dBm
2 | QPSK, 14/15 | -54
2 | 16QAM, 11/15 | -55
2 | 16QAM, 14/15 | -50
2 | 64QAM, 11/15 | -49
2 | 64QAM, 14/15 | -43
4 | QPSK, 14/15 | -54
4 | 16QAM, 11/15 | -52
4 | 16QAM, 14/15 | -49
4 | 64QAM, 11/15 | -47
4 | 64QAM, 14/15 | -43
9 | QPSK, 14/15 | -52
9 | 16QAM, 11/15 | -40
9 | 16QAM, 14/15 | -47
9 | 64QAM, 11/15 | -45
9 | 64QAM, 14/15 | -40
16 | QPSK, 14/15 | -50
16 | 16QAM, 11/15 | -49
16 | 16QAM, 14/15 | -44
16 | 64QAM, 11/15 | -42
16 | 64QAM, 14/15 | -36

## Slide 18: 7. Remove 20%?
It should be “remove 10% worst error results”.
  To remove abnormal values, we use 10 % trim averaging in BER calculation using channel model.
  This is the same procedure as 15.3c criteria (15-05-0493r27).
Notes: http://www2.vmas.kitasato-u.ac.jp/lecture0/statistics/smilnoff.pdf

## Slide 19: 8. Specify data throughput from MAC to PHY across PHY SAP for MIMO
8.1. Supporting material
MCS |  |  | M, (MIMO) | Payload size (Octets) |  | Period [nsec] |  |  |  |  |  |  |  |  |  |  |  | PHY-SAP bitrate [Gbps] No-ACK mode | PHY-SAP bitrate [Gbps] Imm-ACK mode
 | Modulation bit/symbol | Code rate |  |  |  | T_PA_INITIAL | T_PA_CONT | T_PHYHDR | T_MACHDR | T_HCS | T_PAYLOAD | T_FCS | T_MIFS | T_SIFS | N (No. of frames) | T_PACKET | T_OVHD |  | 
QPSK,14/15 | 2 | 0.9 | 2 | 16384 |  | 1854.5 | 1418.2 | 86.4 | 90 | 20 | 39896 | 9.1 | 50 | 2500 | 1 | 40102 | 4560 | 5.9 | 5.3
QPSK,14/15 | 2 | 0.9 | 4 | 16384 |  | 1854.5 | 1418.2 | 86.4 | 90 | 20 | 39896 | 9.1 | 50 | 2500 | 1 | 40102 | 4560 | 11.8 | 10.7
QPSK,14/15 | 2 | 0.9 | 9 | 16384 |  | 1854.5 | 1418.2 | 86.4 | 90 | 20 | 39896 | 9.1 | 50 | 2500 | 1 | 40102 | 4560 | 26.5 | 24.1
QPSK,14/15 | 2 | 0.9 | 16 | 16384 |  | 1854.5 | 1418.2 | 86.4 | 90 | 20 | 39896 | 9.1 | 50 | 2500 | 1 | 40102 | 4560 | 47.2 | 42.8
16QAM,11/15 | 4 | 0.7 | 2 | 16384 |  | 1854.5 | 1418.2 | 86.4 | 90 | 20 | 25388 | 4.5 | 50 | 2500 | 1 | 25589 | 4555.5 | 8.8 | 7.6
16QAM,11/15 | 4 | 0.7 | 4 | 16384 |  | 1854.5 | 1418.2 | 86.4 | 90 | 20 | 25388 | 4.5 | 50 | 2500 | 1 | 25589 | 4555.5 | 17.5 | 15.2
16QAM,11/15 | 4 | 0.7 | 9 | 16384 |  | 1854.5 | 1418.2 | 86.4 | 90 | 20 | 25388 | 4.5 | 50 | 2500 | 1 | 25589 | 4555.5 | 39.4 | 34.2
16QAM,11/15 | 4 | 0.7 | 16 | 16384 |  | 1854.5 | 1418.2 | 86.4 | 90 | 20 | 25388 | 4.5 | 50 | 2500 | 1 | 25589 | 4555.5 | 70.0 | 60.8
16QAM,14/15 | 4 | 0.9 | 2 | 16384 |  | 1854.5 | 1418.2 | 86.4 | 90 | 20 | 19948 | 4.5 | 50 | 2500 | 1 | 20149 | 4555.5 | 10.7 | 9.0
16QAM,14/15 | 4 | 0.9 | 4 | 16384 |  | 1854.5 | 1418.2 | 86.4 | 90 | 20 | 19948 | 4.5 | 50 | 2500 | 1 | 20149 | 4555.5 | 21.4 | 18.0
16QAM,14/15 | 4 | 0.9 | 9 | 16384 |  | 1854.5 | 1418.2 | 86.4 | 90 | 20 | 19948 | 4.5 | 50 | 2500 | 1 | 20149 | 4555.5 | 48.1 | 40.6
16QAM,14/15 | 4 | 0.9 | 16 | 16384 |  | 1854.5 | 1418.2 | 86.4 | 90 | 20 | 19948 | 4.5 | 50 | 2500 | 1 | 20149 | 4555.5 | 85.6 | 72.2
64QAM,11/15 | 6 | 0.7 | 2 | 16384 |  | 1854.5 | 1418.2 | 86.4 | 90 | 20 | 16926 | 3.0 | 50 | 2500 | 1 | 17125 | 4553.9 | 12.2 | 10.1
64QAM,11/15 | 6 | 0.7 | 4 | 16384 |  | 1854.5 | 1418.2 | 86.4 | 90 | 20 | 16926 | 3.0 | 50 | 2500 | 1 | 17125 | 4553.9 | 24.4 | 20.1
64QAM,11/15 | 6 | 0.7 | 9 | 16384 |  | 1854.5 | 1418.2 | 86.4 | 90 | 20 | 16926 | 3.0 | 50 | 2500 | 1 | 17125 | 4553.9 | 54.9 | 45.3
64QAM,11/15 | 6 | 0.7 | 16 | 16384 |  | 1854.5 | 1418.2 | 86.4 | 90 | 20 | 16926 | 3.0 | 50 | 2500 | 1 | 17125 | 4553.9 | 97.6 | 80.6
64QAM,14/15 | 6 | 0.9 | 2 | 16384 |  | 1854.5 | 1418.2 | 86.4 | 90 | 20 | 13299 | 3.0 | 50 | 2500 | 1 | 13498 | 4553.9 | 14.7 | 11.7
64QAM,14/15 | 6 | 0.9 | 4 | 16384 |  | 1854.5 | 1418.2 | 86.4 | 90 | 20 | 13299 | 3.0 | 50 | 2500 | 1 | 13498 | 4553.9 | 29.4 | 23.4
64QAM,14/15 | 6 | 0.9 | 9 | 16384 |  | 1854.5 | 1418.2 | 86.4 | 90 | 20 | 13299 | 3.0 | 50 | 2500 | 1 | 13498 | 4553.9 | 66.1 | 52.6
64QAM,14/15 | 6 | 0.9 | 16 | 16384 |  | 1854.5 | 1418.2 | 86.4 | 90 | 20 | 13299 | 3.0 | 50 | 2500 | 1 | 13498 | 4553.9 | 117.5 | 93.6

## Slide 20: 8. Specify data throughput from MAC to PHY across PHY SAP for MIMO
Chart: PHY-SAP Throughput for Imm-ACK mode (64QAM)
| 256 | 512 | 1024 | 2048 | 4096 | 8192 | 16384 | 32768 | 65536 | 131072 | 262144 | 524288 | 1048576
2 | 0.43969 | 0.86019 | 1.6484 | 3.0425 | 5.2713 | 8.3182 | 11.6994 | 14.6838 | 16.8304 | 18.1576 | 18.9029 | 19.299 | 19.5033
4 | 0.87938 | 1.7204 | 3.2969 | 6.0849 | 10.5426 | 16.6364 | 23.3988 | 29.3675 | 33.6607 | 36.3151 | 37.8057 | 38.5979 | 39.0066
9 | 1.9786 | 3.8709 | 7.418 | 13.6911 | 23.721 | 37.432 | 52.6474 | 66.0769 | 75.7366 | 81.709 | 85.0629 | 86.8453 | 87.7648
16 | 3.5175 | 6.8815 | 13.1876 | 24.3397 | 42.1706 | 66.5457 | 93.5954 | 117.4701 | 134.6428 | 145.2604 | 151.223 | 154.3917 | 156.0263

## Slide 21: Thank you