## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: General Architecture of Kookmin University PHY and MAC multiple-proposal for Image Sensor Communication
Date Submitted: January 2016
Source: Yeong Min Jang, Trang Nguyen, Nam Tuan Le, Md. Shareef Ifthekhar, Mohammad Arif Hossain, Hong Chang Hyun, Amirul Islam [Kookmin University]
Contact: +82-2-910-5068 E-Mail: yjang@kookmin.ac.kr
Re:
Abstract: This is a general architecture of Kookmin University ISC PHY and MAC Multiple-Proposal
Purpose: Call for Proposal Response
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
doc.: IEEE 802.15-16- 0011 -01-007a
Submission

## Slide 2
Submission
Content
PHY Layer Introduction
  Definitions
  PHY design principles and considerations
  Compatibility features
PHY layer specification
  PHY modes
  PHY frame format – class I
  PHY frame format – class II
Error correction
MAC Layer specification
  MAC considerations
  General MAC frame format
  Broadcast/Beacon MAC frame format
  Data transfer MAC frame format
  Command MAC frame format
doc.: IEEE 802.15-16- 0011 -01-007a

## Slide 3
Submission
PHY Layer Introduction
doc.: IEEE 802.15-16- 0011 -01-007a

## Slide 4
Submission
optical clock rate: The frequency at which the data is clocked out to the optical source.
symbol rate: The number of different symbols across the transmission medium per time. It shows how fast the data symbol is clocked out (e.g. 10 symbol/sec). Note that a symbol definition is up to the modulation scheme.
modulation rate: This term is used only for LED use case to show how fast LED is modulated.
clock information (of a data packet/symbol): The information represents the state of a symbol clocked out. The clock information is transmitted along with a symbol to help a receiver identifying an arrival state of new symbol under presence of frame rate variation.
frame rate variation: This term is applied for a typical camera when a fixed frame rate video mode is not supported or an auto-frame rate mode is selected by a software application. The frame rate variation is limited by the range of frame rate (frame rate range)
frame rate range: The range observed of frame rate in a selected video mode which is lower limited by the minimum practical frame rate and upper limited by the maximum practical frame rate during the recording time.
varying shutter speed: Shutter speed stands for the length of time a camera shutter is open to expose light into the image sensor. Auto-exposure in video mode causes the variation in shutter speed, hence the available bandwidth is varying.
sampling rate: The number of rows are sequentially obtained per time in a rolling shutter image sensor (also known as row-scanning rate). However, in a global shutter image sensor, the frame rate is equal to the sampling rate.
rolling sampling rate: the practical sampling rate observed from the selected resolution mode of an output image. By using a output image to extract data, the practical sampling rate is less than the sampling rate in an image sensor because the output image resolution is reduced.
spatial scheme: The communications scheme to solve the problem of frame-rate variation in the receiver by transmitting data along with its clock information spatially. A spatial-MIMO transmitter is used in this scheme.
Spatial M-PSK (SM-PSK): A communications scheme in which a group of LEDs consists of multiple LEDs which are modulated at different phases together transmit a phase spatially. At a time, the camera captures multiple states of those LEDs (a group of LEDs) and uses those states to decode a transmitted phase, outputting a data symbol.
dimmable spatial M-PSK (DSM-PSK): A specific form of SM-PSK in which dimming is supported in steps of 1/M.
reference LEDs: In the spatial scheme, the reference-LEDs do not transmit any data but a reference signal (a specific form of clock information) to help a varying frame-rate receiver decoding data.
data LEDs: The LEDs which transmit data in the spatial scheme.
Definitions
doc.: IEEE 802.15-16- 0011 -01-007a

## Slide 5
Submission
temporal scheme: The communications scheme to solve the problem of frame-rate variation in the receiver by transmitting data along with its clock information together as one packet.
asynchronous bit/symbol: a form of clock information in the temporal scheme to solve frame rate variation problem.
interrupted Lighthouse-to-Ship: Lighthouse rotation causes to the cyclical interruption in transmission from lighthouse to ship. The period of repetition is about 9s for example.
frequency-domain scheme: The communications scheme to solve the problem of frame-rate variation in the receiver. A data along with its clock information together are transmitted as one symbol. But before transmission, the packet is encoded in frequency domain.
Compatible Multiple-Frequency Shift Keying (CM-FSK): The modified M-FSK scheme to be compatible to a varying frame-rate camera receiver by transforming a data packet along with its clock information together into a frequency symbol. Additionally, CM-FSK also supports compatibility in different sampling rates at different rolling shutter receivers.
Compatible On-Off-Keying (C-OOK): The modified OOK scheme to be compatible to a varying frame-rate camera receiver by transmitting data along with its clock information together as one packet. Additionally, C-OOK also supports compatibility in different sampling rates at different rolling shutter receivers.
Compatible Color-Shift-Keying (C-CSK): a modification of CSK scheme to be compatible to a varying frame-rate camera receiver.
rolling effect: This happens in a rolling shutter camera receiver in which camera exposes sequentially to light. Different LEDs may be captured at different time instances on an image due to the rolling effect.
majority symbol voting: When the frame rate of a camera receiver is much less than the symbol rate of a transmitter, a symbol which is transmitted multiple times will be re-captured multiple times. The clock information of a symbol shows that the symbol is repeated or first time transmitted. The majority voting scheme which is applied to vote all captured symbols on a same clock to output a data symbol can enhance error rate.
available bandwidth: the bandwidth limited by the upper physical limit of camera; typically by the shutter speed. The lower limit for the available bandwidth is defined by eye cut-off frequency, e.g. 200Hz, for flicker-free application.
global exposure time (or capturing time): This term is used specifically in rolling shutter camera to differentiate with the exposure time (the time a row of pixel in an image sensor exposes to light). It is the time from the moment the first-row shutter opens to the moment the last-row shutter close.
Rolling -shutter –Packet period to Frame interval Ratio (RPFR): This term is applied in C-OOK scheme in which a processed rolling image outputs a data packet. The ratio of the period of the data packet decoded from an rolling image to the frame interval shows how efficiency the transmission is.
doc.: IEEE 802.15-16- 0011 -01-007a

## Slide 6
Submission
PHY Design principles and Considerations:
Compatibility Support for Commercial Cameras
  Compatible to varying frame-rates
  Compatible to sampling rates/shutter speeds
  Compatible to both global shutter and rolling shutter receivers.
  Compatible to different resolutions
Performance (e.g. link rate, distance) is considered when the available bandwidth is narrow. Low overhead transmission mode will be supported.
Dimming Support (the step of dimming depends on a specific application)
Localization
Identification of multiple transmitters
doc.: IEEE 802.15-16- 0011 -01-007a

## Slide 7
Submission
Compatibility to varying-frame-rates
Assume that:
A camera has a varying frame-rate within a variation range that is different from the other cameras’.
The variation in frame rate is irregular, but for communications let assume it is always above a specific value (e.g. 10fps). (If anytime the frame rate drops to below the condition, e.g. 10fps, the FEC is required to correct error lately)
Three solutions are proposed:
Temporal Scheme (Compatible-OOK) | Data along with its clock information are transmitted as one packet.
Spatial Scheme (Spatial M-PSK/ Dimmable Spatial M-PSK) | Clock information is also encoded spatially with data. We call those LEDs which transmit reference signal (clock information of a data symbol) are reference-LEDs. The other LEDs which transmit data are called data-LEDs.
Frequency Domain Scheme (Compatible M-FSK) | Data along with its clock information are transmitted as one symbol. But before transmission, the packet is encoded in frequency domain.
doc.: IEEE 802.15-16- 0011 -01-007a

## Slide 8
Submission
Compatibility to varying-frame-rates
doc.: IEEE 802.15-16- 0011 -01-007a

## Slide 9
Submission
Compatibility to different sampling-rates/shutter speeds
Different sampling rates problem
In Image Sensor Communications system using M-FSK modulation scheme and a rolling shutter camera receiver, a rolling shutter camera has a different sampling rate and a different shutter speed from the other rolling shutter cameras’.
Solution:
Compatibility Support for different sampling-rates/shutter speeds by using Data Frame Structure with a specific frame (a training frame)
Compatibility-support frame
(training frame)
Data frame
Data frame
…
The roles of a compatibility-support frame
  Training: Helps a receiver previewing and self-identifying the sampling rate (kHz). The value of sampling rate (a constant in an image sensor) will be restored and used for decoding of the following data packets.
doc.: IEEE 802.15-16- 0011 -01-007a

## Slide 10
Submission
Compatibility to global shutter and rolling shutter
DSM-PSK
(Dimmable Spatial M-PSK)
CM-FSK
(Compatible M-FSK)
Performance
(Link rate)
Spatial 2-PSK 1
1 Our spatial 2-PSK (a subset of SM-PSK) is proposed to be compatible to both global and rolling shutter types, and compatible to varying frame-rate cameras.
2 Our CM-FSK scheme which is designed mainly for rolling shutter types can support for a varying frame-rate and be compatible to different sampling rates/shutter speeds. If the number of frequency, M>2, global shutter is not supported. 2-FSK can support for both types of shutter.
Our hybrid M-PSK/CM-FSK is proposed to give best performance in rolling shutter type with supports for a varying frame-rate and different sampling rates/shutter speeds. Dimming is also supported by performing PWM in FSK.
2-FSK 2
(for only global shutter in case of M >2)
(for only rolling shutter in case of M >2)
Compatible to both types of shutter
Both Shutters Support
Lowest
Highest
No
(M >2)
YES
(M =2)
doc.: IEEE 802.15-16- 0011 -01-007a
Hybrid M-PSK.M-FSK
For rolling shutter

## Slide 11
Submission
Compatibility to global shutters and rolling shutters
Color Transmission (C-CSK)
OOK Scheme (C-OOK)
This scheme is compatible to both global shutter and rolling shutter types because the symbol rate of transmission is less than the minimum frame rate of a camera.
The rolling effect is also considered and mitigated in our C-CSK scheme on a rolling shutter receiver.
(Rolling effect causes the problem that different LEDs may be captured at different time instances)
This scheme is not designed to be compatible to global shutter type. Only rolling shutter type is considered as a receiver.
(optical clock rate is about several kHz to target high performance of rolling shutter receiver which has sampling rate up to tens of kHz)
(The C-OOK mainly supports compatibility in frame rate variation and different sampling rates.)
doc.: IEEE 802.15-16- 0011 -01-007a

## Slide 12
Submission
Compatibility to resolutions
Problem
The high resolution causes to the long readout time and post-processing time, reducing the frame rate of a camera receiver. A camera has a different capacity of resolution and frame rate limit from the other’s. The resolution should be small enough to target high frame rate range, e.g. above 20fps (to avoid missing data when dropping frame rate to below the symbol rate of transmission).
The sampling rate on an rolling image sensor is constant. However, by reducing resolution in read-out process, the downsampled image causes reducing the rolling sampling rate practically.
Solution:
A camera receiver operates a preview mode before getting data in order to select the proper resolution mode in which the frame rate range is suitable for communications (i.e. above the symbol rate, 20fps for example). Higher frame rate range is better for error correction in using majority symbol voting.
Especially in the rolling shutter receiver, the selected resolution should provide a rolling sampling rate high enough for the reliable communications.
doc.: IEEE 802.15-16- 0011 -01-007a

## Slide 13
Submission
PHY modes
The IEEE 802.15.7 specification classified PHY types into PHY I, PHY II and PHY III upon the data rate. Our proposed PHY modes for Image Sensor Communications belong to PHY I.
doc.: IEEE 802.15-16- 0011 -01-007a

## Slide 14
Submission
PHY modes (TBD)
Low-rate PHY I modes (Flicker-free)
  Modulation : CM-FSK or hybrid CM-FSK/ M-PSK
  Line Coding : None
  Symbol rate : 5/10/15 (symbol/sec)
  Data rate : 20 bps – 120 bps
  Compatibility features support: varying frame-rates (YES); shutter speeds/sampling rates (YES); rolling shutter type (YES); global shutter type (YES if 2-FSK).
Medium-rate PHY I modes (Flicker-free)
  Modulation : C-OOK
  Line Coding : Manchester/4B6B/8B10B
  Optical clock rate : 2 kHz/ 4 kHz Symbol rate : 5/10/15 (symbol/sec)
  Data rate : 500 bps – 3.2 kbps
  Compatibility features support: varying frame-rates (YES); shutter speeds/sampling rates (YES); rolling shutter type (YES); global shutter type (NO).
High-rate PHY I modes (Spatial MIMO)
doc.: IEEE 802.15-16- 0011 -01-007a

## Slide 15
Submission
Color Transmission (Flicker) | Spatial-MIMO LEDs (Flicker-free)
Modulation : C-CSK Symbol rate : 5/10/15 (symbol/sec) Data rate : kbps – Mbps Compatibility features: varying frame-rates (YES); rolling shutter type (YES); global shutter type (YES). | Modulation : SM-PSK/ DSM-PSK Symbol rate : 5/ 10/ 15 (symbol/sec) Data rate : kbps – Mbps Compatibility features: varying frame-rates (YES); global shutter type (YES); rolling shutter type (NO).
PHY modes (TBD) continue
High-rate PHY I modes (Spatial MIMO)
doc.: IEEE 802.15-16- 0011 -01-007a

## Slide 16
Submission
Low-rate PHY I modes (Flicker-free)
 |  |  |  |  | Data rate | Compatibility Support |  | 
 |  | Modulation |  | Symbol Rate (symbol/sec) | (e.g. 10 sym/sec) | Varying frame rates | Shutter speeds/ Sampling rates | Shutter type
1 | Low rate PHY I | S2-PSK * |  | 5/ 10/ 15 | 10 bps | Y | Y | Both
2 |  | 32-FSK |  | 5/ 10/ 15 | 50 bps | Y | Y | Rolling
3 |  | hybrid 32-FSK/ | 2-PSK | 5/ 10/ 15 | 60 bps | Y | Y | Rolling
4 |  | hybrid 64-FSK/ | 2-PSK | 5/ 10/ 15 | 70 bps | Y | Y | Rolling
5 |  | hybrid 64-FSK/ | 4-PSK | 5/ 10/ 15 | 80 bps | Y | Y | Rolling
  Other supports:
  In a hybrid M-FSK and M-PSK scheme, dimming is supported in FSK by performing PWM.
  The maximum number of frequencies is limited by the available bandwidth (B) divided by frequency separation (∆f ):
    Number_of_frequency = (B/ ∆f)
*S2-PSK scheme (Spatial 2-PSK) uses a couple of LEDs to transmit data. The inverse relation in phases of two LEDs blinks bit 0; otherwise the similarity in phases blinks bit 1.
doc.: IEEE 802.15-16- 0011 -01-007a

## Slide 17
Submission
Medium-rate PHY I modes (Flicker-free)
 |  |  |  |  |  |  | Data rate | Compatibility Support |  | 
 |  | Modulation | Coding | Optical Clock rate | Symbol rate | RPFR | (e.g. 10 sym/s) | Varying frame rates | Shutter speeds/ Sampling rates | shutter type
6 | Medium PHY I (kbps) | C-OOK | Manchester | 2 kHz | 5/ 10/ 15 | 25% | 84 bps | Y | Y | Rolling
7 |  | C-OOK | Manchester | 2 kHz | 5/ 10/ 15 | 50% | 0.17 kbps | Y | Y | Rolling
8 |  | C-OOK | 4B6B | 2 kHz | 5/ 10/ 15 | 50% | 0.22 kbps | Y | Y | Rolling
9 |  | C-OOK | 4B6B | 4 kHz | 5/ 10/ 15 | 50% | 0.44 kbps | Y | Y | Rolling
10 |  | C-OOK | 8B10B | 4 kHz | 5/ 10/ 15 | 50% | 0.53 kbps | Y | Y | Rolling
Data rate = (optical clock rate) x (RPFR) x (symbol rate)
  Other supports:
  Dimming is supported in OOK by performing dimmed-OOK.
  In rolling shutter receiver, the maximum optical clock rate is limited by the observed sampling rate (about tens of kS/s) and the shutter speed (about 8 kHz for typical smartphone cameras).
  A rolling shutter camera has an global exposure time which is different from the other rolling shutter camera’s. The value of global exposure time is a limitation to the data packet length.
doc.: IEEE 802.15-16- 0011 -01-007a

## Slide 18
Submission
High-rate PHY I modes (Flicker and Flicker-free)
 |  |  |  |  |  | Data rate | Compatibility Support |  | 
 | High PHY I modes | Modulation |  | Symbol Rate (/sec) |  | (e.g. 10 symbol/s) | Varying frame rates | Shutter speeds | shutter type
11 | Flicker (16 x 16) | C-2CSK (OOK) |  | 5/ 10/ 15 |  | 2.5 kbps | Y | n/a | Both
12 |  | C-4CSK (4 Color) |  | 5/ 10/ 15 |  | 5 kbps | Y | n/a | Both
13 |  | C-8CSK (8 Color) |  | 5/ 10/ 15 |  | 7.5 kbps | Y | n/a | Both
14 | Flicker (64 x 64) | C-2CSK (OOK) |  | 5/ 10/ 15 |  | 40 kbps | Y | n/a | Both
15 |  | C-4CSK (4 Color) |  | 5/ 10/ 15 |  | 80 kbps | Y | n/a | Both
16 | Flicker-free (16 x 16) | S2-PSK |  | 5/ 10/ 15 |  | 2.5 kbps | Y | Y | Global
17 |  | S8-PSK |  | 5/ 10/ 15 |  | 1.92 kbps | Y | Y | Global
18 |  | Dimmable S8-PSK |  | 5/ 10/ 15 |  | 0.96 kbps | Y | Y | Global
19 | Flicker-free (64 x 64) | S2-PSK |  | 5/ 10/ 15 |  | 40 kbps | Y | Y | Global
20 |  | S8-PSK |  | 5/ 10/ 15 |  | 30.7 kbps | Y | Y | Global
21 |  | Dimmable S8-PSK |  | 5/ 10/ 15 |  | 15.3 kbps | Y | Y | Global
  Other supports:
  dimming is not proposed in color transmission.
  In dimmable spatial-MIMO M-PSK scheme (DSM-PSK), dimming is supported in steps of 1/M.
doc.: IEEE 802.15-16- 0011 -01-007a

## Slide 19
Submission
PHY I Frame Format –class I
for temporal and/or frequency-domain scheme
Preamble and training | PHY header | HCS | PSDU
SHR | PHR |  | PHY payload
PHY I Frame Format – class II
for spatial MIMO scheme
Preamble | PHY header | HCS | PSDU
SHR | PHR |  | PHY payload
doc.: IEEE 802.15-16- 0011 -01-007a

## Slide 20
Submission
PHY I Frame Format –class I
for temporal (C-OOK) and/or frequency-domain(CM-FSK) scheme
doc.: IEEE 802.15-16- 0011 -01-007a

## Slide 21
Submission
SHR symbol 1
HCS
MCS ID
PSDU length
Reserved
PSDU
SHR symbol 2
fSF
CM-FSK scheme (on the best-compatible-band)
CM-FSK/ C-OOK (extended band)
f’SF
SHR
PHR
Best Compatible Band
Extended band
Camera
Physical
limit
Camera
Physical
limit
SHR and PHR design:
This part should have compatibility to most of rolling shutter cameras
  CM-FSK is chosen because of its error rate advantages compared to C-OOK:
    Hence CM-FSK is more reliable in detection and synchronization
    The frequency band for encoding SHR and PHR is the low band. This is to ensure the accuracy and compatibility to any rolling shutter camera.
  The PSDU can keep CM-FSK scheme or switch to C-OOK scheme, and is performed on extended band to achieve higher link rate in specific situations.
doc.: IEEE 802.15-16- 0011 -01-007a

## Slide 22
Submission
fSF
f'SF
best compatible band
. . .
32 frequency
. . .
extended band
Camera
limit
Data frequency: fi = fSF + i.∆f (i=1; 2;…; 32)
Preamble frequency: f’SF = fSF + 33.∆f
~8 kHz
Preamble design:
On the lowest-band among the CM-FSK PHY modes to ensure compatibility with low sampling-rate cameras.
Relationship between fSF and f’SF is for training
  fSF is chosen as lowest frequency on the available bandwidth, e.g. 200Hz, to be easily detected.
  f’SF = fSF + 33x ∆f to train different cameras which have different sampling rates.
doc.: IEEE 802.15-16- 0011 -01-007a

## Slide 23
Submission
PHY header design:
  All frequencies used for PHY header are on low- band of the available bandwidth (e.g. 200Hz – 2kHz). This is to be compatible to low sampling rate cameras.
  SHR and PHR are allocated in a common band (low-band)
  The length for each frequency symbol is constant throughout the frame between preamble, header, and payload
  PSDU can be allocated on the extended band.
 | MCS indication | PHY modes | Data rate | Unit
1 | 0000 0000 | I.1 | 10 | bps
2 | 0000 0001 | I.2 | 50 | 
3 | 0000 0010 | I.3 | 60 | 
4 | 0000 0011 | I.4 | 70 | 
5 | 0000 0100 | I.5 | 80 | 
6 | 0000 0101 | I.6 | 84 | 
7 | 0000 0110 | I.7 | 0.17 | kbps
8 | 0000 0111 | I.8 | 0.22 | 
9 | 0000 1000 | I.9 | 0.44 | 
10 | 0000 1001 | I.10 | 0.53 | 
32-FSK ==> (5 bit/symbol)
MCS ID: 2 symbols (8 bit ID)
1 freq. symbol ==> 1 (asynchronous bit) and 4 (ID bits)
doc.: IEEE 802.15-16- 0011 -01-007a

## Slide 24
Submission
PHY Frame Format – type II
for spatial-MIMO scheme
doc.: IEEE 802.15-16- 0011 -01-007a

## Slide 25
Submission
symbol 1
HCS
MCS ID
PSDU length
Reserved
PSDU
symbol 2
s
Spatial-MIMO
(resolution mode 1)
spatial-MIMO
(resolution mode 2)
SHR
PHR
SHR and PHR design:
On a low resolution to ensure compatibility to different resolutions versus distance.
doc.: IEEE 802.15-16- 0011 -01-007a

## Slide 26
Submission
Preamble design:
Symbol its inverse form (s and ) are to help receiver in identifying LEDs.
Preamble symbols are at low spatial-resolution among spatial-MIMO PHY modes.
symbol s
Preamble
HCS
MCS ID
PSDU length
Reserved
PSDU
constant symbol rate
resolution mode 1
resolution mode 2
Although the resolution can be increased at PSDU, the symbol rate does not change throughout the frames between preamble, header, and payload. Any symbol rate should be pre-noticed
doc.: IEEE 802.15-16- 0011 -01-007a

## Slide 27
Submission
PHY header design:
SHR and PHR are at the same resolution (lowest among spatial-MIMO PHY modes).
Although the resolution can be increased at PSDU, the symbol rate does not change throughout the frame between preamble, header, and payload. Any symbol rate should be pre-noticed
 | MCS indication | PHY modes | Data rate | Unit | Note | 
11 | 0000 1011 | I.18 | 0.96 | kbps | Flicker-free(16 x 16) | DS8-PSK
12 | 0000 1100 | I.17 | 1.92 |  |  | S8-PSK
13 | 0000 1101 | I. 16 | 2.5 |  |  | S2-PSK
14 | 0000 1110 | I.11 | 2.5 |  | Flicker (16 x 16) | C-2CSK
15 | 0000 1111 | I.12 | 5 |  |  | C-4CSK
16 | 0001 0000 | I.13 | 7.5 |  |  | C-8CSK
17 | 0001 0001 | I.21 | 15.3 |  | Flicker-free(64 x 64) | DS8-PSK
18 | 0001 0010 | I.20 | 30.7 |  |  | S8-PSK
19 | 0001 0011 | I.19 | 40 |  |  | S2-PSK
20 | 0001 0100 | I.14 | 40 |  | Flicker (64 x 64) | C-2CSK
21 | 0001 0101 | I.15 | 80 |  |  | C-4CSK
22 - 256 |  | reserved |  |  |  | 
doc.: IEEE 802.15-16- 0011 -01-007a

## Slide 28
Submission
PHY error correction:
SHR | PHR | PHY symbol 1 | PHY symbol 1 | PHY symbol 1 | PHY symbol 2 | PHY symbol 2 | … | FCS
Clock information
repetition
PHY structure
Camera sampling
Majority Voting
symbol 1 voting
symbol 2 voting
Note:
For a simple error correction, a repetition of transmission and majority voting scheme are together applied. The camera sampling rate is faster than the symbol rate at any condition. The clock information becomes indispensable for the voting, especially under presence of frame rate variation.
Two types of voting: a symbol (a group of bits) majority voting/ every single bit majority voting
doc.: IEEE 802.15-16- 0011 -01-007a

## Slide 29
Submission
PHY Summary
20 PHY modes were proposed up on modulation schemes
Two PHY frame format Types:
  An common PHY frame format for Temporal/Frequency-Domain scheme
    CM-FSK and hybrid CM-FSK/M-PSK(<100 bps)
    C-OOK (100bps - 1kbps)
  An identical PHY frame format for both Spatial-MIMO schemes
    Flicker mode: Color transmission C-CSK (2.5kbps - 80kbps)
    Flicker-free mode: CM-PSK/DCM-PSK (100bps – 3kbps)
The symbol rate does not change throughout the frames between preamble, header, and payload. Any symbol rate should be pre-noticed
Compatibility support in SHR and PHR design is highly considered. The lowest data mode among available PHY modes is used for both SHR and PHR.
  Low-band CM-FSK is used as common PHY for Temporal/Frequency-Domain scheme
  Low-resolution is used for SHR and PHR frames in spatial scheme.
The DPSU can use the same PHY mode or upgrade to another PHY mode (higher data rate) among available PHY modes. The notice of DPSU PHY mode is MCS ID frame.
The error is corrected by repeating transmission along with a majority voting. The clock information transmission is helpful (and indispensable) for the voting under presence of frame rate variation.
doc.: IEEE 802.15-16- 0011 -01-007a

## Slide 30
Submission
MAC Layer
doc.: IEEE 802.15-16- 0011 -01-007a

## Slide 31
Submission
Kookmin MAC supports 4 modes based on applications/usages:
Beacon broadcast (Low overhead beacon broadcast) mode
Information Broadcast (IB) mode
Bidirectional communication mode
Device-to-Device (D2D) mode
Four MAC Types
Sources
Tag
…
Unidirectional broadcast of beacon/information
Connected
Coordinators
Tag
Tag
Tag
…
Bidirectional star topology
Device 1
Device 2
Bidirectional unicast
1) Low-overhead beacon mode/
2) IB Mode
3) Bidirectional Communications
4) D2D Mode
Tag
Tag
doc.: IEEE 802.15-16- 0011 -01-007a

## Slide 32
Submission
Low complexity and low overhead.
This is critical because of low data rate in ISC
Flexibility
a common MAC frame format for
  Beacon broadcast mode: The most basic and lowest overhead with localization supported
  IB mode: Unidirectional information broadcast
  Bidirectional data transfer mode
  D2D mode
MAC design principles
doc.: IEEE 802.15-16- 0011 -01-007a

## Slide 33
Submission
PHR
SHR
PSDU
Low-overhead beacon mode
IB Mode
D2D Mode
Bidirectional multiple access Mode
All slots are data transfer
Beacon, shorten beacons, beacon, shorten beacons
Beacon, low-overhead downlink, beacon, low-overhead downlink
Beacon, contention, uplink, downlink
MAC Overview
doc.: IEEE 802.15-16- 0011 -01-007a

## Slide 34
Submission
6/16/10 | 0/x | 0/16 | 0/x | variable | 0/x
Frame control | Sequence number | Addressing fields | Security Field | PSDU | FCS
MHR |  |  |  | MSDU | MFR
Bits: 3 | 0/2 | 0/1 | 0/2 | 0/2 | 3/13/0
Frame type | Frame version | Security Enabled | Dest Addressing mode | Source Addressing mode | Optional fields
Beacon | 000
Data | 001
Acknowledgement | 010
MAC command | 011
Reserved | 
(all left options are for low overhead beacon)
Frame Types (3 bits)
3 bits | 0/10 bits
Beacon type | Company ID
General MAC frame format
doc.: IEEE 802.15-16- 0011 -01-007a

## Slide 35
Submission
Broadcast MAC frame formats
Full beacon
prefix
Full beacon
Content
Shorten prefix
Shorten Content
2 bytes
6 bits
Full beacon
shorten beacon
Shorten prefix
Shorten Content
shorten beacon
Full beacon
prefix
Full beacon
Content
long-beacon interval
. . .
. . .
3 bits
Beacon type
000
(frame type)
10 bits
Optional fields
Frame Types (3 bits)
Beacon | 000
Data | 001
Acknowledgement | 010
MAC command | 011
Reserved | 
Beacon types (3 bits)
(3 fields) LED-ID beacon | 000
(4 fields) LED-ID beacon and Advertisement Data | 001
Shorten beacon | 010
Reserved | 
doc.: IEEE 802.15-16- 0011 -01-007a

## Slide 36
Submission
ID-SN
Company ID
Beacon type
Zone-ID field
1-2 bytes
FCS
x bytes
Full Beacon
Beacon prefix
2 bytes
Sub-Zone ID field 1
1-2 bytes
3 bit
10 bit
000
(frame type)
3 bit
ID-SN (ID sequence number):
to match an ID frame to the correct ID field when there are multi ID fields.
Sub-Zone ID field 2
1-2 bytes
ID data
5-13 bit
3 bit
Adv. field
1-2 bytes
010
(ID-SN)
010
(shorten beacon)
Shorten Beacon
Beacon prefix
6 bíts
Sub-Zone ID field 2
1-2 bytes
3 bit
000
(frame type)
3 bit
ID data
5-13 bit
3 bit
Frame Types (3 bits)
Beacon | 000
Data | 001
Acknowledgement | 010
MAC command | 011
Reserved | 
Beacon types (3 bits)
(3 fields) LED-ID beacon | 000
(4 fields) LED-ID beacon and Advertisement Data | 001
Shorten beacon | 010
Reserved | 
ID-SN (3 bits)
Zone-ID | 000
Sub-Zone-1 ID (floor) | 001
Sub-Zone-2 ID (LED #) | 010
Advertisement data | 011
Reserved | 
Broadcast MAC frame formats
doc.: IEEE 802.15-16- 0011 -01-007a

## Slide 37
Submission
D2D mode: Data frame format
10 | x | 16 | x | variable | x
Frame control | Sequence number | Addressing fields | Security Field | PSDU | FCS
MHR |  |  |  | MSDU | MFR
Bits: 3 | 2 | 1 | 2 | 2
Frame type | Frame version | Security Enabled | Dest Addressing mode | Source Addressing mode
Beacon | 000
Data | 001
Acknowledgement | 010
MAC command | 011
Reserved | 
doc.: IEEE 802.15-16- 0011 -01-007a

## Slide 38
Submission
MAC command frame format
Bits: 10 | x | 16 | x | 8 | variable | x
Frame control | Sequence number | Addressing fields | Security Field | Command ID | Command payload | FCS
MHR |  |  |  | MSDU |  | MFR
Command ID | Command name | Purpose | Tx | Rx
0x15 | Symbol rate change request | To adapt Tx symbol rate versus Rx frame rate variation when Rx has the minimum frame rate below the symbol rate. | X | X
0x16 | Bandwidth change request | To adapt Tx frequency band versus Rx sampling rate when Rx has a low sampling rate that cannot get data in PSDU frames. | X | X
0x17 | Resolution change request | To adapt the number of Tx LEDs spatially (resolution) versus Rx image resolution mode. | X | X
0x18 - 0xff | Reserved |  |  | 
doc.: IEEE 802.15-16- 0011 -01-007a

## Slide 39
Submission
MAC Summary
Four MAC types
  3 bits frame type used to identify a MAC frame
  Without an acknowledgement
Low overhead broadcast mode MAC frame format
  Low overhead Beacon: a full and a shorten beacon frame
  IB mode: low overhead downlink MAC frame
Low complexity
  D2D mode requires security (sometimes) then the security frame is considered.
MAC frame command: Add 3 command-IDs to support compatibility
  Symbol rate change request
  Bandwidth change request
  Resolution change request
doc.: IEEE 802.15-16- 0011 -01-007a

## Slide 40
Submission
Appendix
doc.: IEEE 802.15-16- 0011 -01-007a

## Slide 41
Submission
Related Sub-Proposals (Kookmin University)
  1; 2 Compatibility features supported include: Compatible to different varying-frame-rates; Compatible to different sampling rates/shutter speeds; Compatible to global shutter and rolling shutter types (optional); and Compatible to different resolutions.
1 | Color transmission PHY sub-proposal for ISC | Flicker
2 | Asynchronous temporal-Scheme PHY sub-proposal for ISC (C-OOK) | Flicker-free
3 | Asynchronous Frequency-Scheme PHY sub-proposal (CM-FSK with Compatibility features support1) for ISC | Flicker-free
4 | Dimmable Spatial-MIMO PHY sub-proposal (SM-PSK/DSM-PSK with Compatibility features support2) for ISC | Flicker-free
doc.: IEEE 802.15-16- 0011 -01-007a