## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Proposal of SRM MAC Commands for Technical Guidance Document]
Date Submitted: [15 January, 2016]
Source: [Hidetoshi Yokota, Ruben Salazar, Chris Calvert and Steve Chasko] Company [Landis&Gyr]
Address: [1-2-9 Nishi Shimbashi Minato-ku, Tokyo 105-0003, Japan,
30000 Mill Creek Av., Alpharetta, GA 30022, USA ]
Voice: [+81 3-5532-7455, +1 678 258 3165, +1 678 258 1516, +1 678 258 1538], E-Mail: [hidetoshi.yokota@landisgyr.com, ruben.salazar@landisgyr.com, chris.calvert@landisgyr.com, stephen.chasko@landisgyr.com]
Re: [“TG4s Technical Guidance Document”, IEEE 802.15-14-0555-10-004s]
Abstract: [This contribution proposes MAC commands that should be considered in the Technical Guidance Document for measuring spectrum resources in WPAN.]
Purpose: [Discussion and approval]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
Proposal of SRM MAC Commands for Technical Guidance Document
Authors:

## Slide 3: Outline of this contribution
Introduction
Usage scenarios of SRM signaling
Proposal
  SRM MAC Functional Description
  SRM MAC Command Frame Format
Discussion
  Possible extension for SRM MAC Management Service Primitives
References [1] IEEE802.15.4-REVc-D00

## Slide 4: Introduction
All PIB attributes identified to meet SRM requirements so far have been defined
These attributes are not only used within each device, but also exchanged between devices in the PAN
This contribution proposes MAC commands to push, pull and set these PIB attributes

## Slide 5: Usage scenarios of SRM signaling
Router
PNC#1
(Concentrator)
Leaf
Router
Router
Router
Layer 1
Layer 2
Layer 0
[SRM Request]
Timing: On demand
Usage:
- information retrieval: PIB attributes
- control (TPC)
[SRM Response]
Timing: in response to SRM request
Usage:
- send PIB attributes
- send command result
[SRM Information/ Extended Beacon]
Timing: On demand or periodical
- Extended Beacon: before MAC join
- SRM Information: after MAC join
Usage: control (TPC)
Source: “IEEE 802.15-15-0177-00-004s-use-case-for-tgd”, March 2015
[SRM Report]
Timing: periodical or event-driven
Usage: send latest PIB attributes

## Slide 6: Proposal of SRM functional description
Device
MAC
Device
higher layer
MLME-SRM.request
SRM Request
SRM Response
MLME-SRM.indication
MLME-SRM.response
MLME-SRM.confirm
Device
MAC
Device
higher layer
MLME-GET.request
MAC PIB
MLME-GET.confirm
Example procedure
SRM Request/Response (Section 6.17)
Acknowledgment
Acknowledgment

## Slide 7: Proposal of SRM functional description (cont’d)
Device
MAC
Device
higher layer
MLME-SRM.request (TPC)
SRM Request (TPC)
SRM Response
MLME-SRM.confirm
Device
MAC
Device
higher layer
Device
PHY
MLME-SET.request
MLME-SET.confirm
TPC process
SRM Request/Response (cont’d)
Example procedure
(*) Depending on the application or use case, it is also possible that the MAC layer of the recipient of SRM Request notifies the higher layer of its reception by MLME-SRM.indication and the higher layer triggers MLME-SET to control the lower layer.
(*)

## Slide 8: Proposal of SRM functional description (cont’d)
Device
MAC
Device
higher layer
MLME-SRM-REPORT.request
SRM Report Notification
Acknowledgment
MLME-SRM-REPORT.indication
MLME-SRM-REPORT.confirm
(OPTIONAL)
Device
MAC
Device
higher layer
SRM Report

## Slide 9: Proposal of SRM functional description (cont’d)
Device
MAC
Device
higher layer
MLME-SRM-INFORMATION.request
SRM Information Notification
Acknowledgment (*)
MLME-SRM-INFORMATION.indication
Device
MAC
Device
higher layer
MLME-SRM-INFORMATION.confirm
(OPTIONAL)
MLME-SET.request
MAC PIB
MLME-SET.confirm
SRM Information
(*) Acknowledgment is required only for unicast SRM Information Notification

## Slide 10: Current MAC Command frame format [1]
MAC Command frame format (7.3.4)

## Slide 11: Proposal of SRM MAC Command
0x23-0x2f | Reserved |  |  | 
0x30 | SRM Request command |  |  | 7.5.25
0x31 | SRM Response command |  |  | 7.5.26
0x32 | SRM Report Notification command |  |  | 7.5.27
0x33 | SRM Information Notification command |  |  | 7.5.28
0x32 or 0x33
SRM Command (7.5.1)

## Slide 12: Proposal of SRM MAC Command (cont’d)
SRM Request Command (7.5.25)
  Command ID=0x30
  Content:
Octet:1 | Bit: 0-5 | 6-7 | Octent:1 | Octet:2
Length | SRM Metric ID | Scope | SRM Token | Command Information
bits:0 | 1 | 2 | 3 | 4 | 5 | 6-15
Start Time Present | SRM Duration Present | Channel Page Present | Channel Number Present | Address Mode Present | Device Address Present | Reserved
Command Information
Octets:8
Start Time
Start Time Content Field
Octets: 2
SRM Duration
SRM Duration Content Field
The rest of content fields are already defined.

## Slide 13: Proposal of SRM MAC Command (cont’d)
SRM Response command (7.5.26)
  Command ID=0x31
  Content
Octet:1 | Bit: 0-5 | 6-7 | Octet:1 | 1 | 4
Length | SRM Metric ID | Scope | SRM Token | Status | Attribute Value
Status value | Description
0 | Success
1 | Not supported
2 | Rejected
3-255 | Reserved

## Slide 14: Proposal of SRM MAC Command (cont’d)
SRM Report Notification command (7.5.27)
  Command ID=0x32
  Content
Octet:1 | Bit: 0-5 | 6-7 | Octet:1 | 1 | 4
Length | SRM Metric ID | Scope | SRM Token | Command Information | Attribute Value

## Slide 15: Proposal of SRM MAC Command (cont’d)
SRM Information Notification command (7.5.28)
  Command ID=0x33
  Content
Octet:1 | Bit: 0-5 | 6-7 | Octet:1 | 1 | 4
Length | SRM Metric ID | Scope | SRM Token | Command Information | Attribute Value

## Slide 16: Discussion
Service primitives should also be extended for coordinating with SRM MAC commands
  Place: Section 8.2 [1]
    MLME-SRM.{request, notification, response, confirmation}
    MLME-SRM-REPORT.{request, notification, confirmation}
    MLME-SRM-INFORMATION.{request, notification, confirmation}