## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Proposed resolution for CID 2131
Date Submitted: Jan., 2016
Source: Jaehwan Kim, Sangsung Choi (ETRI), Jaebeom Kim, Youngbae Ko (Ajou Univ.), Soo-Young Chang (SYCA), and Cheolho Shin (ETRI)
Company: ETRI, Ajou Univ., SYCA
Address:
Voice: +82 42 850 5338, E-Mail: kimj@etri.re.kr
Re:
Abstract:
Purpose: To suggest a comment resolution for Letter Ballot #113
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: CID 2131
Commentor
  Jussi Haapola
Related clause
  5.2.2.3 P 30 line 38
Comment
  Wrong: 'In non-beacon enabled PANs, the BO and SO are set to 1 in order to ignore inactive/active time weight.' in nonbeacon-enables PANs, BO = 15 and SO is ignored if BO = 15.
Proposed Change
  Change text to reflect this and also correct the formula below to take undefined SOs into account.

## Slide 3: CID 2131
Proposed Resolution
  Revise
  Replace “In non-beacon enabled PANs, the BO and SO are set to 1 in order to ignore inactive/active time weight” with “In non-beacon enabled PANs, inactive/active time weight need to be ignored, because superframe does not exist, the BO is set to 15, and the SO is ignored upon reception."