## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [A method for generating realistic wireless traffic through analysis of smartphone operation logs]
Date Submitted: [16 Feb, 2016]
Source: [Yuko Hirabe, Yutaka Arakawa, Keiichi Yasumoto] Company [Nara Institute of Science and Technology (NAIST)]
Address [Takayama-cho 8916-5, Ikoma, Nara 630–0192, Japan ]
Voice:[+81-743-72-5392], FAX: [+81-743-72-5976], E-Mail:[hirabe.yuko.ho2@is.naist.jp, ara@is.naist.jp, yasumoto@is.naist.jp]
Re: []
Abstract: [For development of a realistic performance eveluation model of IEEE 802.15, this document introduces an investigated result of the influence that IEEE 802.11 interference gives to IEEE 802.15 communication, taking account of users’ operation on smartphone applications. This is informative to discuss significance of performance analysis in IEEE802.15 TG4s.]
Purpose: [For discussion]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: A method for generating realistic wireless traffic through analysis of smartphone operation logs
Authors:
Name | Company | Address | Phone | email
Yuko Hirabe, Yutaka Arakawa, Keiichi Yasumoto | Nara Institute of Science and Technology (NAIST) | Takayama-cho 8916-5, Ikoma, Nara 630–0192, Japan | +81-743-72-5392 | hirabe.yuko.ho2@is.naist.jp ara@is.naist.jp yasumoto@is.naist.jp
Investigating influence of Wifi-interference to ZigBee communication and understanding Wifi traffic patterns by real smartphone applications

## Slide 3: Background
Popularization of the Internet of Things (IoT)
  Increase of networked home appliances
  Sensors for smart home
  ex) wattmeter, sensors of temperature, humidity, and location
Send sensor data by ZigBee
Many ZigBee and Wifi devices coexist in the home Heavy Wifi traffic may hamper ZigBee communication
Demand for performance evaluation of 802.15 (ZigBee) base system considering Wifi interference
Power sensor
Temperature, humidity sensor
Location sensor
server
Send
Sensors’ data
Internet
Gateway
Wifi interference
IoT + Smart Home
Current: realistic performance evaluation of 802.15 (ZigBee) base system is difficult due to Wifi interference.
802.11: Wifi 802.15: ZigBee

## Slide 4: Smart home environment
Smart home in our lab
Continuously record sensor data 24 hours, 365 days
Sensors
  Sensors using ZigBee:
    Power sensor × 28
    Environment sensor × 24
    Door sensor × 15
  Sensors using Bluetooth:
    Power sensor × 10
  Sensors using EnOcean:
    Door sensor × 8
    CO2 × 4
    Illuminance × 4
    Button× 3
  Etc...
Location
(Ultrasonic receiver）
Location
(Ultrasonic sender）
Power consumption
Environment sensor

## Slide 5: Users produce Wifi data traffic in smart home
①Bathroom
① Bathroom
②Bedroom
② Bedroom
③ Kitchen
④ Living room
③Kitchen
④Living room

## Slide 6: How to consider the Wifi interference?
Performance evaluation of wireless communication system
  Wireless traffic generation by random/probabilistic traffic model [1]
Wifi coexists with 802.15 in a smart home environment.
  Wifi traffic may disturb ZigBee data communication.
  Current main traffic source is a smartphone.
1. H. Zhai et al., Performance analysis of IEEE 802.11 MAC protocols in wireless LANs, Wireless Communications and Mobile Computing 4.8, 2004.
For realistic performance evaluation of 802.15 base systems, we need to clarify and consider Wifi traffic from smartphones

## Slide 7: Wifi traffic pattern depends on the type of apps.
Various mobile apps generate different traffic
  SNS: Facebook, Twitter, Instagram
    Text, Photo, Movie
  Multimedia: YouTube, Youku, iCloud, Google Photo
    Movie, photo （huge traffic [2]）
  Map: Google Maps, Apple map
    map tile data
  File: Dropbox, Box, Google drive
    Every types
Usage pattern also affects to the generated traffic.
  preload, play a video, input text, share photo
2. Chart by BI Intelligence, used in Business Insider event, IGNITION

## Slide 8: Goal and approach
Approach:
Step1: Investigate how the interference with ZigBee-traffic happens while using Wifi
Step2: Investigate how users' operation on the applications affects Wifi traffic
Step3: Propose a method to construct a realistic WiFi traffic generation model for reproducing interference with 802.15
Goal:
Clarify how 802.11(Wifi) affects the performance of 802.15 (ZigBee)
Propose a method to construct a realistic wireless traffic generation model for realistic performance evaluation of 802.15 base systems

## Slide 9: Step1: Investigate how interference with ZigBee-traffic happens while using Wifi (1/3)
Experiment environment
  802.15
  CH: 22 (2460MHz)
  7 Xbees （Sender: 5 Xbees, Receiver: 2 Xbees）
  One Macbook Air: 1
  802.11
  CH: 11 (2462MHz)
  Connection side
    Android: 10
    Macbook Air: 2
  Access point
    Macbook Pro
Actual environment
802.15
802.11

## Slide 10: Step1: Investigate how interference with ZigBee-traffic happens while using Wifi (2/3)
Set the environment as the Wifi interferences happens to ZigBee
Xbee
Macbook Air
Data receiving side
Data sending side
× 5
10 times / 1s
Total 1200 times
ZigBee data transmission
1.0 m
Android × 10
Macbook Air × 2
1.5 m
Wifi connection
Macbook Pro
Wifi access point
Interference
Play the movie (1080p) with each devices

## Slide 11: Step1: Investigate how interference with ZigBee-traffic happens while using Wifi (3/3)
We observe the following with ZigBee communication
  Transmission time between send and receive
  The number of retry
We changed the environment as follows:
  Increased ZigBee data traffic when WiFi is not used
  Changed the distance between ZigBee receiver and Wifi access point with Wifi connection
  Increased the number of WiFi devices connecting to Wifi access point

## Slide 12: 1. Increase ZigBee data traffic without WiFi （1/2） Result : Transmission time between send and receive
80 byte
2 byte
The more data transmission volume increases, the longer ZigBee takes a transmission time.
The number of data transmission time (times)
Transmission time between send and receive (s)
80 byte
2 byte

## Slide 13: 1. Increase ZigBee data traffic without WiFi （2/2） Result : The number of retry
The number of retry increases when data transmission volume is small.
When data transmission volume increased, data transmission time grows and also the number of retry decreases.
→In rest investigations, we set data transmission volume 80 byte.
Total times of data transmission: 1200
The number of retry (times)

## Slide 14: 2. Change the distance between ZigBee receiver and Wifi access point (with Wifi) Result: The number of retry
When the distance between ZigBee receiver and Wifi access point is zero, the number of retry decreased.
The distance between ZigBee receiver and Wifi access point don't affect ZigBee interference.
Total times of data transmission: 1200
The number of retry (times)
d = 1.0
d = 0.0
d: distance between ZigBee receiver and Wifi access point
  d = 0.0 or 1.0 (m)
One device is connected to Wifi access point
** Transmission time between send and receive didn’t change

## Slide 15: 3. Increase the number of WiFi devices connecting to Wifi access point (with Wifi) Result: The number of retry
The more the number of device increases, the more the number of retry grows.
The number of retry is up to six times, compared when Wifi wasn't connected.
When many devices connected to Wifi access point, the number of retry grew  the effect of the interference
Total times of data transmission: 1200
The number of retry (times)
The number of Wifi devices connecting to Wifi access point
0
1
2
3
4
6
7
8
9
10
11
12
5
6
** Transmission time between send and receive didn’t change

## Slide 16: Goal and approach
Approach:
Step1: Investigate how the interference with Zigbee-traffic happens while using Wifi
Step2: Investigate how users' operation on the applications affects Wifi traffic
Step3: Propose a method to construct a realistic WiFi traffic generation model for reproducing interference with 802.15
Goal:
Clarify how 802.11(Wifi) affects the performance of 802.15 (ZigBee)
Propose a method to construct a realistic wireless traffic generation model for realistic performance evaluation of 802.15 base systems

## Slide 17: Step2: Investigate how users’ operation on the applications affects Wifi traffic (1/3) Different traffic for different usage pattern
View posts by others (Download)
Text, picture, movie
Contents
DL happens in only displayed range
Scrolling
preload & increase of traffic
Comments：Like, text
Posts: text, picture, movie, share
larger traffic
Post items
（Upload）

## Slide 18: Step2: Investigate how users’ operation on the applications affects Wifi traffic (2/3) Traffic generation pattern on Facebook
Facebook
Posts: Upload
View：Download
With scrolling
Without scrolling
Comments
Posts
Traffic
Small (DL)
Big (DL)
Small (UL)
Big (UL)
Operations of 4 types
Investigating targets

## Slide 19: Step2: Investigate how users’ operation on the applications affects Wifi traffic (3/3) Experiment environment
Wifi connection
Access point
Macbook Pro
GALAXY Note II
Ethernet
Obtain the packets with Wireshark
Target app: Facebook
Investigate apps’ traffic by showing the obtained packet as I/O graphs

## Slide 20: Result
App’s window is just slid
Pictures and movies are selected, while sliding app's window
Packets increased depending on users’ operation

## Slide 21: Goal and approach
Approach:
Step1: Investigate how the interference with Zigbee-traffic happens while using Wifi
Step2: Investigate how users' operation on the applications affects Wifi traffic
Step3: Propose a method to construct a realistic WiFi traffic generation model for reproducing interference with 802.15
Goal:
Clarify how 802.11(Wifi) affects the performance of 802.15 (ZigBee)
Propose a method to construct a realistic wireless traffic generation model for realistic performance evaluation of 802.15 base systems

## Slide 22: Step3: Propose a method to construct a realistic WiFi traffic generation model for reproducing interference with 802.15
Approach:
Recognize a user’s operations on each app.
Measure a generated traffic for each operation
Construct a statistical traffic generation model by associating each operation with the measured traffic
Clarify the interference of 802.11 (Wifi) to 802.15 (ZigBee) by using a spectrum analyzer or packet loss evaluation.
View w/o scroll
View w. scroll
Comment
Post
Traffic distribution
Traffic generation model of each mobile user

## Slide 23: Summary and discussion
Investigated how the interference with Zigbee traffic happens while using Wifi
Investigated how users' operation on the applications affects Wifi traffic
Proposed a method to construct a realistic WiFi traffic generation model for reproducing interference with 802.15
Future work
Investigate WiFi interference with ZigBee communication when user operations on smartphone apps are changed
Actually develop classification algorithm of users' app.
  target apps: Instagram, Facebook, LINE
Construct the model, and incorporate it into network simulators
Notes: 読む。