## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Resolution of comment #13]
Date Submitted: [13 March 2016]
Source: [Kiyoshi Toshimitsu and Ko Togashi]
Company: [Toshiba Corporation]
Address1: [1-1-1 shibaura, Minato-ku, Tokyo 108-8001]
E-Mail1: [kiyoshi.toshimitsu@toshiba.co.jp, ko.togashi@toshiba.co.jp]
Re: [In response to 15-16-0162-01-003e-lb114-consolidated-comments]
Abstract: [This document presents a resolution of comment #13 in 15-16-0162-01-003e-lb114-consolidated-comments.]
Purpose: [Resolving the comment #13]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributors acknowledge and accept that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Comment and resolution
Page | Sub-clause | Line # |  | Proposed Change
 | 6 |  | Beacon and Unassociated Phase should use mandatory MCS. | As commented
Comment #13
Resolution
    In Sec.4.3.5, insert the following text at the end of a) Unassociated Phase.
a)Unassociated Phase
A PPC sends a Beacon periodically to initiate a P2P connection. Beacon includes information on the number and duration of the access slots which any target DEV can use by responding with an Association Request. The number of access slots is defined in pNAccessSlot and the duration of each slot is defined in pDAccessSlot. These values are specified in P2Plink Synchronization Parameters field format set in Beacon frames, as shown in Figure 6-50b. A target DEV selects one of access slots to send an Association Request command and sends it at the beginning of the selected access slot.
All frames shall be transmitted using an MCS from the mandatory MCS set during Unassociated Phase.

## Slide 3: END