## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Resolution of comment #25]
Date Submitted: [13 March 2016]
Source: [Kiyoshi Toshimitsu and Ko Togashi]
Company: [Toshiba Corporation]
Address1: [1-1-1 shibaura, Minato-ku, Tokyo 108-8001]
E-Mail1: [kiyoshi.toshimitsu@toshiba.co.jp, ko.togashi@toshiba.co.jp]
Re: [In response to 15-16-0162-01-003e-lb114-consolidated-comments]
Abstract: [This document presents a resolution of comment #25 in 15-16-0162-01-003e-lb114-consolidated-comments.]
Purpose: [Resolving the comment #25]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributors acknowledge and accept that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Comment and resolution
Page | Sub-clause | Line # |  | Proposed Change
56 | 7.3a.1 | 2 | What is the expected value of "Last Received Sequence Number" field of Stk-ACK in reply to an Association Response command before receiving any data frame? | Add clear description
Comment #25
Resolution
In Sec.6.2.10, change Figure 6-46a and insert the following text.
Bits: b0-b8 | b9 | b10–b19b9-b18 | b20b19 | b21b20 | b22b21 | b23b22-23
Number of Subframes | Sequence Number Type | Last Received Sequence Number | Buffer Full | Buffer Empty | HRCP Sleep | Reserved
Figure 6-46a —TX and Ack Information field format for HRCP

## Slide 3
6.2.10 TX and ACK Information field for HRCP
The Number of Subframes field indicates the number of subframes included in the current frame. Up to 256 subframes can be aggregated into a single frame.
The Sequence Number Type field indicates the type of sequence number. A value of one indicates a data frame and a value of zero indicates a command frame.
The Last Received Sequence Number field indicates the most recent contiguous sequence number of subframes that was successfully received by the DEV. The details are illustrated in 7.8.3c.
7.8.3 HRCP aggregation
HRCP data transmission uses the HRCP aggregation frame format.
Figure 7-54a illustrates the aggregation process. The originating PPC or DEV, upon receiving an MSDU, maps it into an MPDU. If the length of the MSDU exceeds the Preferred Payload Size negotiated during the association process, the MSDU shall be fragmented and mapped into multiple MPDUs. Each MPDU is assigned a unique Sequence number for identification.
All the fragments shall have unique Ssequence numbers that are assigned in ascending order between successive MSDUs. Command frames shall have another unique and successive sequence numbers. The initial numbers of both sequence numbers are zero.
In Sec.7.8.3, insert the following text.

## Slide 4: END