IEEE P802.15

Wireless Personal Area Networks

| Project | IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs) |
| --- | --- |
| Title | PHY related TBDs |
| Date Submitted | March 29th, 2016 |
| Source | Marco Hernandez, Huan-Bang Li, Igor Dotlić, Ryu Miura (NICT) |
| Response | In response to Call for Contributions to TG8 |
| Abstract |  |
| Purpose | For discussion in TG8 |
| Notice | This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15. |

Contents

1. TBD	2

TBDs

P802.15.8_D0.20.0.Marco+ssjoo+delete 5.2.4.3.2-3+BV3+258r1+256-r2.doc

Sensitivity

In page 132, replace the Table for receiver sensitivity by the Table below:

— Receiver sensitivity

| Modulation | Coding rate | Sensitivity [dBm] (10 MHz channel spacing) | Sensitivity [dBm] (20 MHz channel spacing) |
| --- | --- | --- | --- |
| BPSK | 1/2 | -97 |  |
| BPSK | 2/3 | -94.7 |  |
| BPSK | 3/4 | -93.5 |  |
| BPSK | 5/6 | -92.8 |  |
| QPSK | 1/2 | -94 |  |
| QPSK | 2/3 | -91.7 |  |
| QPSK | 3/4 | -90.5 |  |
| QPSK | 5/6 | -89.8 |  |
| 16QAM | 1/2 | -88.1 |  |
| 16QAM | 2/3 | -84.7 |  |
| 16QAM | 3/4 | -83.8 |  |
| 16QAM | 5/6 | -83.2 |  |
| 64QAM | 2/3 | -80.7 |  |
| 64QAM | 3/4 | -78.5 |  |
| 64QAM | 5/6 | -77.4 |  |

TBDs in clause 6

In MCPS-DATA.request, page 110, delete MsduHandle and DataRate (already consider in PHY service primitives).

In Table 64, page 112, delete “DataRate” row (already consider in PHY service primitives).

In MCPS-DATA.confirm, page 113, delete MsduHandle.

In MCPS-DATA.indication, page 117, delete “DataRate” row (already consider in PHY service primitives).

In Table 66, page 118, delete “DataRate” row (already consider in PHY service primitives).

Editorial in clause 9

In pages 168 and 169, delete 9.2.19 and 9.2.19.1