## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [DCN 15-16-02xx-00-0wng Tutorial presentation for IETF 95, April 2016]
Date Submitted: [14 March, 2016]
Source: [Charlie Perkins] Company [Futurewei]
Address [2330 Central, Santa Clara, CA 95050]
Voice:[+1-408-330-45860], E-Mail:[charles.perkins@earthlink.net]
Re: [Tutorial presentation for IETF 95, April 2016]
Abstract: [802.15 and 802.24 summary and descriptions for task groups, study groups, and interest groups]
Purpose: [802.15 tutorial materials targeted towards presentation at IETF 95]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Disclaimer…
“At lectures, symposia, seminars, or educational courses, an individual presenting information on IEEE standards shall make it clear that his or her views should be considered the personal views of that individual rather than the formal position, explanation, or interpretation of the IEEE.”
IEEE-SA Standards Board Operation Manual (subclause 5.9.3)
Notes: 2
3/30/2016

## Slide 3: Outline of Presentation
Adapting materials from Bob Heile and Pat Kinney (many thanks!)
Introduction to 802.15
History and market focus
802.15 task groups
Interest Groups, Study Groups
802.15.llc (ULI) description

## Slide 4: IEEE 802 Organization
Standards Activities Board
IEEE Standards Association
802.3
CSMA/CD
Ethernet
802.24
Smart Grid
TAG
802.11
Wireless
WLAN
802.15
Wireless
Specialty
Networks
802.21
Media
Independent
Handoff
802.19
Co-existence
WG
Sponsor
IEEE 802
Local and Metropolitan Area Networks
(LMSC)
Sponsor
Sponsor
Sponsor
802.18
Radio
Regulatory
TAG
802.16
Wireless
Broadband
Access
802.22
Wireless
Regional
Area
Networks
802.1
Higher
Layer
LAN
Protocols
Privacy
Study
Group
Voting Members ~102
www.ieee802.org/15
OmniRan

## Slide 5: 802.15 Scope and Purpose
Initial activities focused on wearable devices - hence “personal area networks”
Activities have proven to be much more diverse
  Data rates from 2kbps to 2gbs
  Ranges from meters to kilometers
  Frequencies from 400MHz to 800THz
  Predominantly non TCP/IP applications
  Shipping over 1 million devices per day
Focus is on “specialty”, typically short range, communications. If it is wireless and not a LAN, MAN, RAN, or WAN, odds are its 802.15
802.15 is only 802 group with multiple MACs

## Slide 6: 802.15 Completed Projects
802.15.1 Original Bluetooth (standards in 2002 and 2005)
802.15.2 Coexistence Recommended Practice Bluetooth/802.11 (standard in 2003) (in hibernation)
802.15.3 High Rate (55 Mbps) Multimedia WPAN
  (standard in 2003) (in hibernation). 15.3 amendments:
  802.15.3c High Rate (>1Gbps) mmWave 15.3 PHY
802.15.4-Low Rate (250kbps). Energy Efficient WPAN for WSN type applications
  15.4 amendments:
  802.15.4a Higher data rate 15.4 UWB PHY
  802.15.4c Sub 1 GHz 15.4 PHY for China
  802.15.4d Sub 1 GHz 15.4 PHY for Japan

## Slide 7: 802.15.4: Standard for Low-Rate Wireless Networks
Very low complexity
Broadly used in IoT
Location based services
Standard issued with 2015 date

## Slide 8: 802.15 Completed Projects
  15.4 Amendments (cont):
  802.15.4e 15.4 MAC Enhancements (GTS among others)
  802.15.4f 15.4 PHY for Active RFID
  802.15.4g 15.4 PHY for Field Area Smart Utility Networks
  802.15.4-2011: 15.4 Roll-up to include 15.4a,c & d
  802.15.4j 15.4 PHY using US dedicated medical band
  802.15.4k 15.4 PHY for Low Energy Critical Infrastructure Monitoring (LCIM)
  802.15.4m 15.4 PHY for operation in TV White Spaces
  802.15.4n 15.4 PHY for Chinese Medical Applications
  802.15.4p 15.4 PHY for Rail Communications and Control
  802.15.4q Ultra Low Power 15.4 PHY
802.15.4-2015 Revision C (bug fixes and roll-up of amendments e,f,g,j,k,m, and p)

## Slide 9: 802.15 Completed Projects
802.15.5: Mesh Networking Recommended Practice
802.15.6: Body Area Networking for medical and entertainment applications
802.15.7: Visible Light Communications using structured lighting

## Slide 10: 802.15 Active Projects/Status
IEEE802.15.3 Amendments:
  802.15.3d THz band 100Gb/s PHY layer for point to point applications (e.g., data center, 5G)
    centimeters <= Range < kilometer
    STATUS: reviewing proposals, starting draft
  802.15.3e High Rate (100Gb/s), Close Proximity Communications using mmWave for 4k HD MPEG file transfers in <250ms total transaction time
    STATUS: in WG Letter Ballot.
IEEE802.15.3 Revision A [802.15.3-2015]:
  Roll-up of amendments b and c plus conversion from 64 bit to 48 bit MAC addressing
    STATUS: On the May 2016 Stds Board agenda for approval

## Slide 11: 802.15 Active Projects/Status (cont)
IEEE802.15.4 Amendments/Projects:
  802.15.4r Common 15.4 ranging protocol for Location Based Services indoors or out
    STATUS: on hold
  802.15.4s Spectrum Resource Utilization(SRU): MAC enhancement for improvements to utilization
    STATUS: working on draft
  802.15.4t Higher Rate PHY (HRP): PHY capable of 2 Mb/s data rates, utilizing the 2.4 GHz ISM band (250 kb/s data rate), having backwards-compatibility to, and the same occupied bandwidth as, the present 2.4 GHz O-QPSK PHY, and be simple to implement.
    STATUS: CFP issued

## Slide 12: 802.15 Active Projects/Status (cont)
IEEE802.15.4 Amendments/Projects (cont):
  802.15.4u India Sub 1 GHz PHY (ISB): PHY for 865-867 MHz band in India.
    STATUS: In Working Group Letter Ballot
  802.15.4v Regional Sub 1GHz Band (RSB):
    Define 15.4 PHY clause changes to use 870-876 MHz & 915-921 MHz bands in Europe, 902-928 MHz band in Mexico, 902-907.5 MHz & 915-928 MHz bands in Brazil, 915-928 MHz band in Australia/New Zealand that are not in 15.4-2015
    Update the channel parameters for the 470-510 MHz band in China and the 863-870 MHz band in Europe to align them with current requirements.
      STATUS: On the May 2016 Stds Board agenda for approval

## Slide 13: Active Projects/Status 802.15.7a
Revision to IEEE802.15.7-2012, Standard for Visible Light Communications.
  Extend spectral range include near UV and near IR
  Renamed “Optical Wireless Communications” (OWC)
  Considers mobility of the optical link, compatibility with various light infrastructures, impairments due to noise and interference, e.g. from ambient light
  Add capability to specifically to address Optical Camera Communications for use with existing as well as future smart mobile devices
    STATUS: Developed TRD, issued CFP and are reviewing proposals

## Slide 14: New Standards Work: 802.15.8 (PAC)
  802.15.8 Peer Aware Communications (PAC)
    Infrastructure-less PAC among Mobile Devices
    data rates from 10 Kbps to 55 Mbps
    multiple channels, dynamic grouping, multiple peer-to-peer communications, location of devices, multicasting, coverage extension, low latency, fast synchronization and association of devices, low power consumption, and enhanced security
    STATUS: near completion first ballotable draft

## Slide 15: New Standards Work: 802.15.9 (KMP)
  802.15.8 Recommended Practice for a 15.4 Key Management Protocol (KMP)
    Specifies containers for Key Management Protocols (KMPs)
    Clarifies fragmentation
    STATUS: Complete, awaiting publication

## Slide 16: New Standards Work: 802.15.10 L2R (Layer 2 Routing Mesh):
Recommended Practice for Layer 2 Routing (Mesh Under) for 802.15.4
Handles all MAC and PHY layers
Handles multi-PAN networks, short addressing, peer-to-peer routing
STATUS: Completing WG Letter Ballot. To seek approval to start sponsor ballot at next opportunity

## Slide 17: New Standards Work: 802.15.12
802.15.12 Upper Layer Interface (ULI) for 15.4:
  Make IEEE 802.15.4 easier to use, like 802.11 and 802.3
  Enable the use of many of the higher layer protocol stacks used by 802.11 and 802.3 without changes
  Allow 15.4 to address new applications, yet maintain backward compatibility with existing devices and applications
  Potentially consolidate L2R, KMP, 6T,& 6lowpan in one ULI
  Will need tight coordination with 802.1 and IETF
    STATUS: On May 2016 Stds Board agenda for approval

## Slide 18: 802.15 Active Project Status
802.15 Interest Groups:
  Dependability IG (IG DEP): seeking to identify non implementation based strategies, which could be standardized, that inherently improve wireless link reliability.
  High Rate Rail Communications IG (HRRC)
  THz IG: Review and discuss the latest advances for using THz bands for wireless date applications

## Slide 19: 802.15 Other Activity
Joint effort with IETF:
6Tisch Interest Group-formed to support collaboration and coordination of 802.15 activities/positions with IETF on an activity to utilize capabilities in 15.4e in conjunction with IPv6, specifically time slotted channel hopping (TSCH).
Approaches to support 15.12 were discussed in March
Looking to broaden the liaison relationship with IETF
Partner Projects for ISO / IEC PSDO process
802.15.3 High Rate Wireless Multimedia Communications
  STATUS: Completed review period with no comments
802.15.4-2015 Low Rate Wireless Networks
  Submitted to JTC1/SC6 for information prior to formally submitting the Standard
802.15.6 Body Area Networking
  Submitted to JTC1/SC6 for information prior to formally submitting the Standard

## Slide 20: IEEE 802.15.12 (Upper Layer Interface)
New IEEE 802.15 project has progressed to:
  Make IEEE 802.15.4 easier to use, similar to IEEE 802.11 (WiFi) and IEEE 802.3 (Ethernet)
  Enable IEEE 802.15.4 to use many of the higher layer protocol stacks used by IEEE 802.11 and IEEE 802.3 without changes
  Allow IEEE 802.15.4 to address new applications yet maintain backward compatibility with existing devices and applications

## Slide 21: Target Applications for 802.15.12
Deterministic
  ISA100.11a
  IETF 6TiSCH
  Industrial Internet of Things (IIoT)
Non-Deterministic (best effort)
  Smart Grid (e.g. WiSUN™)
  Internet of Things (IoT)
  Long Range Infrastructure
    e.g., LECIM (Low energy critical infrastructure monitoring)

## Slide 22: General Concept
  Create a Data Link sublayer above the MAC that adapts and configures the 802.15.4 MAC for desired operation, and contains existing and soon to be released sub-layers for 802.15.4 such as 6LoWPAN, Key Management Protocol (KMP), Layer 2 Routing Mesh (L2R), 6top (IETF 6TiSCH)

## Slide 23: Protocol Layers
Transport Layer
Network Layer
Data Link Layer
Physical Layer
UDP, TCP, ICMP
IPv6 (IPv4 with adapter)
LLC (802.15.12)
MAC (802.15.4)
802.15.4 Modulations: O-QPSK,BFSK, FSK, OFDM
802.15.4 Frequency Bands: (433, 890, 915, 2450, et al)

## Slide 24
IEEE 802.15.4 MAC
…
TSCH
CSMA
IEEE 802.15.4 PHY
…
4k
2003
4g
LPWA:
LECIM
other non-IP
IPv4
New LLC work
Deterministic
Best Effort
6TiSCH
ISA100.11a
6LoWPAN
WiSUN
Zigbee
IP
OTF
…
…
…

## Slide 25: Conclusions and final words
802.15 is very active and dominant for IoT-style applications
  Low-power
  Range of bandwidths
  Interesting for IETF working groups 6TiSch, 6lo, roll
Participates in IEEE/IETF coordination
Looking for liaison, similar to 802.11