## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Resolution on comment #83 and #116 for HRCP MAC]
Date Submitted: [13 Apr 2016]
Source: [Keitarou Kondou, Keiji Akiyama]
Company: [Sony Semiconductor Solutions Corporation]
Address1: [4-14-1 Asahi-cho, Atsugi-shi, Kanagawa 243-0014]
E-Mail1: [Keitarou.Kondou@jp.sony.com]
Re: [In response to 15-16-0162-04-003e-lb114-consolidated-comments]
Abstract: [This document presents a resolution on comment #83 and #116 for HRCP MAC in 15-16-0162-04-003e-lb114-consolidated-comments.]
Purpose: [Resolving the comment #83, #116]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributors acknowledge and accept that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Comment #83 and the resolution
CID | Page | Sub-clause | Line # | Comment | Proposed Change
83 | 44 | 6.4.11a | 25 | The way table 6-17a, 6-17b etc are expressed would indicate that bit b22 is the MSB of the value from the table, i.e. it is 0 for 1ms-50ms and 1 for 100ms and reserved values. This means that the bit patterns needs to be formatted as bit patterns, it must not be expressed as numbers, as then the order would be LSB first, i.e. bit 22 would be the LSB of the number. Is this intended? | It would be better to really then separate the bits i.e. make one column for bit b22, another for b23 etc so it would be really clear that we are not talking about integers here.
Accepted, and Change the table to one column per bit
See next page for Changed

## Slide 3: Comment #83 and the resolution(Cont’d)
Bits: b9 | b10 | b11 | LLPS Interval
0 | 0 | 0 | 1 ms
0 | 0 | 1 | 5 ms
0 | 1 | 0 | 10 ms
0 | 1 | 1 | 50 ms
1 | 0 | 0 | 100 ms
1 | 0 | 1 | Reserved
 | … |  | …
1 | 1 | 1 | Reserved
Table 6-17a—LLPS Interval field values
Current
Changed*
Bits: b16 | b17 | Preferred Payload Size
0 | 0 | 2048 octets
0 | 1 | 4096 octets
1 | 0 | 8192 octets
1 | 1 | Reserved
Table 6-17b—Preferred Payload Size field format
*Includes other editorial corrections

## Slide 4: Comment #83 and the resolution(Cont’d)
Current
Changed*
*Includes other editorial corrections
Bits: b18 | b19 | b20 | Preferred Total Aggregation Size
0 | 0 | 0 | 16448 octets
0 | 0 | 1 | 32896 octets
0 | 1 | 0 | 65792 octets
0 | 1 | 1 | 131584 octets
1 | 0 | 0 | 263168 octets
1 | 0 | 1 | 526336 octets
1 | 1 | 0 | 1050624 octets
1 | 1 | 1 | 2099200 octets
Table 6-17c—Preferred Total Aggregation Size field format

## Slide 5: Comment #116 and the resolution
CID | Page | Sub-clause | Line # | Comment | Proposed Change
116 | 52 | 6.5.1.1 | 8 | in figure the "device utility" field form 802.15.3 is missing | add device utiity field or add two different figures (one of HRCP DEV and one for none-HRCP DEV)
Revised, Accept the comment. Also check lines 11-14 against the latest version of the .3 revision.
Description Add new Figure 6-126a for pairnet without DEV utility field. Change the 1st paragraph including description for Association request command format for pairnet. Check current D02 version of 15.3m draft (for lines 11-14)

## Slide 6
6.5.1.1 Association Request command
Change the text in the first paragraph as shown:
The Association Request command Payload field shall be formatted as illustrated in Figure 6-126 for piconet and Figure 6-126a for pairnet. The SEC field in the Frame Control field shall be set to zero. The DestID shall be set to the PNCID for piconet and HRCP PNCID for pairnet. For piconet operation, the SrcID shall be set to either the UnassocID, as described in 6.2.3, or the DEV’s newly allocated DEVID, as described in 7.3.1. For P2PLink operation, the SrcID shall be set to the DEVID obtained from the Next DevID field in the beacon, as described in 7.3a.1.
Change caption of Figure 6-126 as shown:
Figure 6-126—Association Request command Payload field format for piconet
Insert Figure 6-126a as shown:
Octets: 6 | as defined in 6.4.11b | 2 | variable
DEV Address | HRCP DEV Capability | ATP | IEs
Comment #116 Changed Text
Figure 6-126a—Association Request command Payload field format for pairnet
Insert following paragraph after 3rd paragraph:
The HRCP DEV Capability field is defined in 6.4.11b.
Insert following note after 4th paragraph:
NOTE—It is recommended that an HRCP DEV should use a short ATP length value less than or equal to 500 ms for pairnet.

## Slide 7: END