IEEE P802.15

Wireless Personal Area Networks

| Project | IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs) |
| --- | --- |
| Title | Revised draft of clause 6 and Annex G for resolving the WG LB1 comments |
| Date Submitted | Sep. 26, 2016 |
| Source | Seong-Soon Joo (ETRI) | E-Mail: [ssjoo@etri.re.kr] |
| Re: |  |
| Abstract | This document is a revised draft of clause 6 and Annex G related to the cyclic-superframe structure. |
| Purpose | This document provides the input for the TG8 WG letter ballot comment resolution. |
| Notice | This document does not represent the agreed views of the IEEE 802.15 Working Group or IEEE 802.15.8 Task Group. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

Overview

Normative references

Definitions

General description

MAC protocol

- MAC services

  - MLME-SAP primitives

    - PIB access

    - Discovery primitives

These primitives are used for the discovery of neighboring PDs.

      - MLME-DISCOVERY.request

The primitive requests a PD to perform discovery. The properties of this primitive are:

MLME-DISCOVERY.request{

DiscoveryMode;

DiscoveryInfo;

ChannelPage;

ScanChannels;

CyclicSuperframeStructure;

}

The primitive parameters are defined in Table 29.

Table 29—MLME-DISCOVERY.request parameters

| Property | Type | Valid range | Description |
| --- | --- | --- | --- |
| DiscoveryMode | Enumeration | TX, RX | Indicates transmission or reception of discovery information. |
| DiscoveryInfo | Array of PAC IDs descriptors | As defined in Table 30 | Indicates the discovery information. |
| ChannelPage | Integer | Any valid channel page as defined in Table 76 | The channel page on which to attempt discovery. |
| ChannelNumber | Integer | Any valid channel number as defined in Table 76 | The channel number on which to attempt discovery. |
| ScanChannels | Array of integers | Any valid channel number as defined in Table 76 | The channel numbers to be used for discovery. |
| CyclicSuperframeStructure | Cyclic-superframe structure descriptor | As defined in Table 31 | Indicates the structure of cyclic-superframe |

In RX mode, ChannelNumber is zero.

Discovery descriptors are defined in Table 30.

Table 30—PAC ID description

| Property | Type | Valid range | Description |
| --- | --- | --- | --- |
| Device_ID | MAC address | PD specific | MAC address of the PD. |
| MulticastGroup_ID | Integer | 0 to 216−1 | Multicast Group address of PAC network |
| Application_ID | char | 13 octets | Application name, user name, login. |

Cyclic-superframe structure descriptors are defined in Table 31.

Table 31—Cyclic-superframe structure descriptor

| Property | Type | Valid range | Description |
| --- | --- | --- | --- |
| Cyclic-superframe size | Integer | 1 octet | Number of superframes in a cyclic-superframe. |
| Number of superframe pattern A | Integer | 1 octet | Number of superframe pattern A in a cyclic-superframe |
| Type of superframe pattern A | Integer | As defined in Figure 18 (5.2.4.3.1) | Active periods in superframe pattern A |
| Type of superframe pattern B | Integer | As defined in Figure 18 (5.2.4.3.1) | Active periods in superframe pattern B |

When generated

Effect on receipt

When receiving this primitive with the CyclicSuperfreamStructure parameter, the MAC sublayer shall add on macCyclicSuperframeStructureList of the PIB with the value of the group ID and the cyclic-superframe structure descriptor. The MAC sublayer shall select the start time of a cyclic-superframe and schedule the access to active periods of a cyclic-superframe. After starting a cyclic-superframe, the MAC sublayer inserts the Cyclic-superframe descriptor IE to the MAC header of the Discovery Request command frame.

      - MLME-DISCOVERY.indication

The primitive is used to indicate the reception of a Discovery request command. The properties of this primitive are:

MLME-DISCOVERY.indication{

DiscoveryMode;

DiscoveryInfo;

ChannelPage;

ChannelNumber;

ScanChannels;

CyclicSuperframeStructure;

}

The primitive parameters are defined in Table 32.

Table 32— MLME-DISCOVERY.indication parameters

| Property | Type | Valid range | Description |
| --- | --- | --- | --- |
| DiscoveryMode | Enumeration | TX, RX | Indicates transmission or reception of discovery information. |
| DiscoveryInfo | Array of PAC IDs descriptors | As defined in Table 30 | Indicates the discovery information. |
| ChannelPage | Integer | Any valid channel page as defined in Table 76 | The channel page on which to attempt discovery. |
| ChannelNumber | Integer | Any valid channel number as defined in Table 76 | The channel number on which to attempt discovery. |
| ScanChannels | Array of integers | Any valid channel number as defined in Table 76 | The channel numbers to be used for discovery. |
| CyclicSuperframeStructure | Cyclic-superframe structure descriptor | As defined in Table 31 | Indicates the structure of cyclic-superframe |

When generated

When receiving the Discovery Request command frame with the Cyclic-superframe descriptor IE, the MAC sublayer shall add on macCyclicSuperframeStructureList of the PIB with the value of Group ID and Cyclic-superframe size field, Number of superframes pattern A field, Active period in superframe pattern A field, Number of superframes pattern B field, and Active period in superframe pattern B field. The MAC sublayer notifies the reception of the cyclic-superframe structure to the higher layer with the MLME-DISCOVERY.indication primitive. The MAC sublayer calculates the start of a cyclic-superframe with the values of Sequence Number field and Cyclic-superframe size field. The MAC sublayer starts to schedule the access to active periods of a cyclic-superframe.

Effect on receipt

      - MLME-DISCOVERY.response

The primitive is used to initiate a response to an MLME-DISCOVERY.indication primitive. The properties of this primitive are:

MLME-DISCOVERY.response{

DiscoveryMode;

DiscoveryInfo;

ChannelPage;

ScanChannels;

Status;

}

The primitive parameters are defined in Table 33.

Table 33—MLME-DISCOVERY.response parameters

| Property | Type | Valid range | Description |
| --- | --- | --- | --- |
| DiscoveryMode | Enumeration | TX, RX | Indicates transmission or reception of discovery information. |
| DiscoveryInfo | Array of PAC IDs descriptors | As defined in Table 30 | Indicates discovery information. |
| ChannelPage | Integer | Any valid channel page as defined in Table 76 | The channel page on which discovery was attempted. |
| ChannelNumber | Integer | Any valid channel number as defined in Table 76 | The channel number on which discovery was attempted |
| ScanChannels | Array of integers | Any valid channel number as defined in Table 76 | The channel numbers used for discovery. |
| Status | Enumeration | SUCCESS, FAIL, DISCOVERY_IN_PROGRESS | Status of the discovery request |

When generated

Effect on receipt

When receiving this primitive with the Status parameter set to FAIL, a PD’s MAC sublayer shall delete on  macCyclicSuperframeStructureList of the PIB referred with the Group ID of DiscoveryInfo parameter and stop to schedule the access to active periods of a cyclic-superframe, after sending a Discovery Response command frame.

      - MLME-DISCOVERY.confirm

The primitive reports the result requested by MLME-DISCOVERY.request of the initiating PD. The properties of this primitive are:

MLME-DISCOVERY.confirm{

DiscoveryMode;

DiscoveryInfo;

ChannelPage;

ScanChannels;

Status;

}

The primitive parameters are defined in Table 34.

Table 34—MLME-DISCOVERY.confirm parameters

| Property | Type | Valid range | Description |
| --- | --- | --- | --- |
| DiscoveryMode | Enumeration | TX, RX | Indicates transmission or reception of discovery information. |
| DiscoveryInfo | Array of PAC IDs descriptors | As defined in Table 30 | Indicates discovery information. |
| ChannelPage | Integer | Any valid channel page as defined in Table 76 | The channel page on which discovery was attempted. |
| ChannelNumber | Integer | Any valid channel number as defined in Table 76 | The channel number on which discovery was attempted |
| ScanChannels | Array of integers | Any valid channel number as defined in Table 76 | The channel numbers used for discovery. |
| Status | Enumeration | SUCCESS, FAIL, DISCOVERY_IN_PROGRESS | Status of the discovery request |

When generated

Effect on receipt

    - Peering primitives

These primitives are used when a PD becomes peered with another PD.

      - MLME-PEERING.request

This primitive requests peering with given PD. The properties of this primitive are:

MLME-PEERING.request{

ChannelNumber;

ChannelPage;

GroupMode

MulticastGroup_ID;

DestinationAddress;

CyclicSuperframeStructure;

PhySecuritySupport;

}

The primitive parameters are defined in Table 35.

Table 35—MLME-PEERING.request parameters

| Property | Type | Valid range | Description |
| --- | --- | --- | --- |
| ChannelNumber | Integer | Any valid channel number as defined in Table 76 | The channel number on which to attempt peering. |
| ChannelPage | Integer | Any valid channel page as defined in Table 76 | The channel page on which to attempt peering. |
| GroupMode | Integer | As defined in Table 20 | Group mode determines the type of peering procedure |
| MulticastGroup_ID | Integer | 0 to 216 −1 | Group ID provided by the application layer. |
| DestinationAddress | MAC address | IEEE 48 bit address | Address of the PD with which to peer for one-to-one peering. |
| CyclicSuperframeStructure | Cyclic-superframe structure descriptor | As defined in Table 31 | Indicates the structure of cyclic-superframe |
| PhySecuritySupport | Enumeration | TRUE, FALSE | Indicates whether the PD is using PHY layer security mode |

.

When generated

Effect on receipt

When receiving this primitive with the CyclicSuperfreamStructure parameter, the MAC sublayer shall add on macCyclicSuperframeStructureList of the PIB with the value of the group ID and the cyclic-superframe structure descriptor. The MAC sublayer shall select the start time of a cyclic-superframe and schedule the access to active periods of a cyclic-superframe. After starting a cyclic-superframe, the MAC sublayer inserts the Cyclic-superframe descriptor IE to the MAC header of the Peering Request command frame.

      - MLME-PEERING.indication

The primitive is used to indicate the reception of a Peering request command. The properties of this primitive are:

MLME-PEERING.indication{

SourceID;

GroupMode

MulticastGroupID

PHYcapability;

CyclicSuperfameStructure;

PhySecuritySupport;

}

The primitive parameters are defined in Table 36.

Table 36—MLME-PEERING.indication parameters

| Property | Type | Valid range | Description |
| --- | --- | --- | --- |
| SourceID | MAC address | PD specific | Address of the PD requesting peering. |
| GroupMode | Integer | As defined in Table 20 | Group mode determines the type of peering procedure |
| MulticastGroup_ID | Integer | 0 to 216 −1 | Group ID of the requested group. |
| PHYcapability | Enumeration | LOW_MOBILITY, HIGH_MOBILITY, GFSK, UWB_BPM_BPSK, UWB_OOK | Operational capability of the PD requesting peering. |
| CyclicSuperframeStructure | Cyclic-superframe structure descriptor | As defined in Table 31 | Indicates the structure of cyclic-superframe |
| PhySecuritySupport | Enumeration | TRUE, FALSE | Indicates whether the PD is using PHY layer security mode |

When generated

When receiving the Peering Request command frame with the Cyclic-superframe descriptor IE, the MAC sublayer shall add on macCyclicSuperframeStructureList of the PIB with the value of Group ID and Cyclic-superframe size field, Number of superframes pattern A field, Active period in superframe pattern A field, Number of superframes pattern B field, and Active period in superframe pattern B field. The MAC sublayer notifies the reception of the cyclic-superframe structure to the higher layer with the MLME-PEERING.indication primitive. The MAC sublayer calculates the start of a cyclic-superframe with the values of Sequence Number field and Cyclic-superframe size field. The MAC sublayer starts to schedule the access to active periods of a cyclic-superframe.

Effect on receipt

      - MLME-PEERING.response

The primitive is used to initiate a response to an MLME-PEERING.indication primitive. The properties of this primitive are:

MLME-PEERING.response{

SourceID;

GroupMode;

MulticastGroup_ID;

Status;

PhySecuritySupport;

}

The primitive parameters are defined in Table 37.

Table 37—MLME-PEERING.response parameters

| Property | Type | Valid range | Description |
| --- | --- | --- | --- |
| SourceID | MAC address | PD specific | Address of the PD requesting peering. |
| GroupMode | Integer | As defined in Table 20 | Group mode determines the type of peering procedure |
| MulticastGroup ID | Integer | 0 to 216 −1 | ID of the MulticastGroup |
| Status | Enumeration | SUCCESFUL, OUT_OF_CAPACITY, ACCESS_DENIED, | Status of the peering attempt. |
| PhySecuritySupport | Enumeration | TRUE, FALSE | Indicates whether the PD is using PHY layer security mode |

When generated

Effect on receipt

When receiving this primitive with the Status parameter not set to SUCCESSFUL, a PD’s MAC sublayer shall delete on  macCyclicSuperframeStructureList of the PIB referred with the MulticastGroup_ID parameter and stop to schedule the access to active periods of a cyclic-superframe, after sending the Peering Response command frame.

      - MLME-PEERING.confirm

The primitive reports the result requested by MLME-PEERING.request of the initiating PD. The properties of this primitive are:

MLME-PEERING.confirm{

DestinationAddress;

GroupMode;

MulticastGroup_ID;

Status;

PhySecuritySupport;

}

The primitive parameters are defined in Table 38.

Table 38—MLME-PEERING.confirm parameters

| Property | Type | Valid range | Description |
| --- | --- | --- | --- |
| DestinationAddress | MAC address | PD specific | Address of the peered PD. |
| GroupMode | Integer | As defined in Table 20 | Group mode determines the type of peering procedure |
| MulticastGroup_ID | Integer | 0 to 216 −1 | Group ID of the established group. |
| Status | Enumeration | SUCCESS, CHANNEL_ACCESS_FAILURE, NO_ACK, ACCESS_DENIED, | The status of the peering attempt. |
| PhySecuritySupport | Enumeration | TRUE, FALSE | Indicates whether the PD is using PHY layer security mode |

If the peering request was successful, then the Status parameter will be set to SUCCESS. Otherwise, the Status parameter will be set to indicate the type of failure.

When generated

When receiving the Peering Response command frame with the Peering status field not set to Success, the MAC sublayer shall delete on  macCyclicSuperframeStructureList of the PIB referred with the Multicast group address field and stop to schedule the access to active periods of a cyclic-superframe.

Effect on receipt

    - De-peering primitives

These primitives are used when a PD wishes to de-peer with another PD or to be de-peered from another PD.

      - MLME-DE-PEERING.request

This primitive requests de-peering of given PD. The properties of this primitive are:

MLME-DE-PEERING.request{

DestinationAddress;

SourceAddress;

GroupMode;

MulticastGroup_ID;

Reason;

}

The primitive parameters are defined in Table 39.

Table 39—MLME-DE-PEERING.request parameters

| Property | Type | Valid range | Description |
| --- | --- | --- | --- |
| DestinationAddress | MAC address | PD specific | Address of the PD with which to peer. |
| SourceAddresss | MAC address | PD specific | The address of the PD requesting peering. |
| GroupMode | Integer | As defined in Table 20 | Group mode determines the type of peering procedure |
| MulticastGroup_ID | Integer | 0 to 216 −1 | Group ID of destination PD. |
| Reason | Integer | 0 to 1 | Reasons for de-peering: 0 - Source wants to leave. 1 - Source requests destination to leave. |

      - MLME-DE-PEERING.indication

The primitive is used to indicate the reception of a De-peering request command.

MLME-DE-PEERING.indication{

SourceID;

GroupMode;

MulticastGroup ID

Reason;

}

The primitive parameters are defined in Table 40.

Table 40—MLME-DE-PEERING.indication

| Property | Type | Valid range | Description |
| --- | --- | --- | --- |
| SourceID | MAC address | PD specific | The address of the PD requesting de-peering. |
| GroupMode | Integer | As defined in Table 20 | Group mode determines the type of peering procedure |
| MulticastGroup_ID | Integer | 0 to 216 −1 | ID of MulticastGroup |
| Reason | Integer | 0 − 1 | 0 – source wants to leave 1 – source requests destination to leave |

When generated

When receiving the De-Peering Request command frame, the MAC sublayer shall delete on  macCyclicSuperframeStructureList of the PIB referred with the MulticastGroup_ID field and stop to schedule the access to active periods of a cyclic-superframe.

Effect on receipt

      - MLME-DE-PEERING.confirm

This primitive reports the result requested by MLME-DE-PEERING.request. The properties of this primitive are:

MLME-DE-PEERING.confirm{

DestinationAddress;

SourceAddress;

GroupMode;

MulticastGroup_ID;

Status;

}

The primitive parameters are defined in Table 41.

Table 41—MLME-DE-PEERING.confirm parameters

| Property | Type | Valid range | Description |
| --- | --- | --- | --- |
| DestinationAddresss | MAC address | PD specific | Address of the PD with which to de-peer. |
| SourceAddresss | MAC address | PD specific | The address of the PD requesting de-peering. |
| GroupMode | Integer | As defined in Table 20 | Group mode determines the type of peering procedure |
| MulticastGroup_ID | Integer | 0 to 216 −1 | MulticastGroup ID of destination PD. |
| Status | Enumeration | SUCCESS, NO_ACK, CHANNEL_ACCESS_FAILURE, | The status of the de-peering attempt. |

If the de-peering request was successful, then the Status parameter will be set to SUCCESS. Otherwise, the Status parameter will be set to indicate the type of failure.

When generated

When receiving the De-Peering Response command frame, the MAC sublayer shall delete on  macCyclicSuperframeStructureList of the PIB referred with the MulticastGroup_ID field and stop to schedule the access to active periods of a cyclic-superframe.

Effect on receipt

    - Frame error notification primitives

    - Reset MAC sublayer

    - Receiver enable

These primitives are used to enable or disable a receiver of a PD.

      - MLME-RECEIVER-ENABLE.request

This primitive allows the next higher layer to request that the receiver is either enabled for a finite period of time or disabled. The properties of this primitive are:

MLME-RECEIVER-ENABLE.request {

Defer;

RxOnTime;

RxOnDuration;

}

The primitive parameters are defined in Table 45.

Table 45—MLME-RECEIVER-ENABLE.request parameters

| Property | Type | Valid range | Description |
| --- | --- | --- | --- |
| Defer | Boolean | TRUE, FALSE. | TRUE if the requested operation can be deferred until the next superframe, if the requested time has already passed. FALSE if the requested operation is only to be attempted in the current superframe. |
| RxOnTime | Integer | 0 to (224 −1) | The number of symbols measured from the start of the superframe before the receiver is to be enabled or disabled. |
| RxOnDuration | Integer | 0 to (224 −1) | The number of symbols for which the receiver is to be enabled. This property is equal to 0, if the receiver is to be disabled. |

When generated

This primitive is generated by the next higher layer to request the MLME enable or disable a receiver of a PD.

Effect on receipt

Upon receiving this primitive, the MAC sublayer shall enable the radio to receiver mode for a fixed duration, at a time relative to the start of the current or next superframe, or immediately during the CAP, or according to the TDD receiver mode as defined in 9, and without conflict with another higher priority operation of the radio transceiver.

In case of conflicting operation with a higher priority task of the radio transceiver, the PD will interrupt the receive operation, until the completion of the superseded operation. The property RxOnDuration will be checked to determine whether the time has expired. If so, the ReceiverEnable primitive operation is complete. If not, the receiver is re-enabled until either the PD has another superseded task, or the time specified by the property RxOnDuration has expired. When the primitive is issued to disable the receiver, the PD will disable its receiver unless the radio transceiver has a higher priority task.

This primitive may also be generated to cancel a previously generated request to enable the receiver. The receiver is enabled or disabled exactly once per primitive request.

If the RxOnDuration parameter is equal to zero, the MLME requests the PHY to disable its receiver.

      - MLME-RECEIVER-ENABLE.confirm

This primitive reports the results of the attempt to enable or disable the receiver. The properties of this primitive are:

MLME-RECEIVER-ENABLE.confirm {

Status;

}

The primitive parameters are defined in Table 46.

Table 46—MLME-RECEIVER-ENABLE.confirm parameters

| Property | Type | Valid range | Description |
| --- | --- | --- | --- |
| Status | Enumeration | SUCCESS, PAST_TIME, ON_TIME_TOO_LONG, INVALID_PARAMETER | The result of the request to enable or disable the receiver. |

When generated

The primitive is generated by the MLME and issued to its next higher layer in response to an MLME-RECEIVER-ENABLE.request primitive.

Effect on receipt

This primitive returns a status of either SUCCESS, if the request to enable or disable the receiver was successful or the appropriate error code.

Before attempting to enable the receiver, the MLME first determines whether (RxOnTime + RxOnDuration) is less than the synchronization period interval. If (RxOnTime + RxOnDuration) is not less than the synchronization period interval, the MLME issues the MLME-RECEIVER-ENABLE.confirm primitive with the property Status=ON_TIME_TOO_LONG.

The MLME then determines whether the receiver can be enabled in the current superframe. If the current time measured from the start of the superframe is less than (RxOnTime – MIFSTime), the MLME attempts to enable the receiver in the current superframe. If the current time measured from the start of the superframe is greater than or equal to (RxOnTime – macMIFSTime) and DeferPermit is equal to TRUE, the MLME defers until the next superframe and attempts to enable the receiver in that superframe. Otherwise, if the MLME cannot enable the receiver in the current superframe and is not permitted to defer the receive operation until the next superframe, the MLME issues the MLME-RECEIVER-ENABLE.confirm with the property Status=PAST_TIME.

    - Channel scanning

      - MLME-SCAN.request

The MLME-SCAN.request primitive is used to initiate a channel scan over a given list of channels. The properties of this primitive are:

MLME-SCAN.request{

ScanType;

ChannelPage;

ScanChannels;

ScanDuration;

}

The primitive parameters are defined in Table 47.

Table 47—MLME-SCAN.request parameters

| Property | Type | Valid range | Description |
| --- | --- | --- | --- |
| ScanType | Enumeration | ED, ACTIVE, PASSIVE. | Indicates the type of scan performed. |
| ChannelPage | Integer | Any valid channel page as indicated in Table 76 | The channel page on which to perform the scan. |
| ScanChannels | Array of integers | Any valid channel number as indicated in Table 76 | The channel numbers to be scanned |
| ScanDuration | Integer | aScanDuration | A value used to calculate the length of time to spend scanning each channel for ED, active, and passive scans. |

When generated

This primitive is generated by the next higher layer to request the MLME initiate a channel scan.

Effect on receipt

Upon receiving this primitive, the MAC sublayer shall perform a channel scan on required channel pages and channel numbers for the duration of the scan.

      - MLME-SCAN.confirm

This primitive reports the result of the channel scan request. The properties of this primitive are:

MLME-SCAN.confirm{

Status,

ScanType;

ChannelPage;

UnscannedChannels;

ResultListSize;

EnergyDetectList;

DetectedCategory;

}

The primitive parameters are defined in Table 48.

Table 48—MLME-SCAN.confirm parameters

| Property | Type | Valid range | Description |
| --- | --- | --- | --- |
| Status | Enumeration | SUCCESS, LIMIT_REACHED, SCAN_IN_PROGRESS, FRAME_TOO_LONG, INVALID_PARAMETER | The status of the scan request. |
| ScanType | Enumeration | ED, ACTIVE, PASSIVE | Indicates the type of scan performed |
| UnscannedChannels | Array of integers | Any valid channel number as defined in Table 76 | A list of the channels given in the request which were not scanned. This parameter is not valid for ED scans |
| ResultListSize | Integer | Implementation specific | The number of elements returned in EnergyDetectList. |
| EnergyDetectList | Array of integers | 0 to 255 per element in the array. | The list of energy measurements, one for each channel searched during an ED scan. This parameter is null for active, passive scans. |
| DetectedCategory | Integer | 0 to 2 | Categorization of energy detection with the following values: 0: Category detection is not supported 1: UWB PHY detected 2: Non-UWB PHY signal source detected. |

When generated

The primitive is generated by the MLME and issued to its next higher layer in response to an MLME-SCAN.request primitive.

Effect on receipt

This primitive returns a status of either SUCCESS, if the channel scan was successful or the appropriate error code. If the MLME receives a MLME-SCAN.request primitive while performing a previously initiated scan operation, the MLME will not perform the scan and the Status property will be set to SCAN_IN_PROGRESS. If the MLME-SCAN.request primitive requested an active or passive scan, the EnergyDetectList property will be NULL.

    - Group configuration

These primitives are used to initiate a PAC Group.

      - MLME-GROUP-START.request

This primitive is used by a PD already peered with an existing PAC Group. The properties of this primitive are:

MLME-GROUP-START.request{

GroupID;

InitiatorID;

ChannelNumber;

ChannelPage;

StartTime;

CyclicSuperframeStructure;

}

The primitive parameters are defined in Table 49.

Table 49—MLME-GROUP-START.request parameters

| Property | Type | Valid range | Description |
| --- | --- | --- | --- |
| Initiator_ID | MAC address | PD specific | The address of the initiator PD |
| MulticastGroup_ID | Integer | 0 to 216 −1 | Group ID of initiator PD. |
| ChannelNumber | Integer | Any valid channel number a defined in Table 76 | The channel number to use. |
| ChannelPage | Integer | Any valid channel page as defined in Table 76 | The channel page to use. |
| StartTime | Unsigned integer | 0 to (224 −1) | The time at which to begin transmitting the synchronization period. If this parameter is equal to 0, the synchronization period will begin immediately. Otherwise, the specified time is relative to the received synchronization period of the current initiator PD. |
| CyclicSuperframeStructure | Cyclic-superframe structure descriptor | As defined in Table 31 | Indicates the structure of cyclic-superframe |

      - When generated

This primitive is generated by the next higher layer to request the MLME initiate a PAC group.

Effect on receipt

Upon receiving this primitive, the MAC sublayer shall start a PAC group.

      - MLME-GROUP-START.confirm

This primitive reports the results of the attempt to start a PAC group. The properties of this primitive are:

MLME-GROUP-START.confirm{

Status;

}

The primitive parameters are defined in Table 50.

Table 50—MLME-GROUP-START.confirm parameters

| Property | Type | Valid range | Description |
| --- | --- | --- | --- |
| Status | Enumeration | SUCCESS, INVALID_PARAMETER, CHANNEL_ACCESS_FAILURE | The result of the attempt to start a PAC Group |

When generated

The primitive is generated by the MLME and issued to its next higher layer in response to an MLME-GROUP-START.request primitive.

Effect on receipt

This primitive returns a status of either SUCCESS, indicating that the MAC sublayer has started a new PAC Group or using the new superframe configuration. Otherwise, an appropriate error code is return as follows:

CHANNEL_ACCESS_FAILURE – The transmission lost synchronization.

    - Synchronization

    - Channel sounding

    - Dynamic preamble selection

    - Ranging calibration

  - MAC data service

The MCPS-SAP supports the transport of data information. Table 64 lists the primitives maintained by the MCPS-SAP.

Table 64—MCPS-SAP primitives

| Name | Request | Confirm | Indication | Response |
| --- | --- | --- | --- | --- |
| MCPS.Data | 6.2.1 | 6.2.2 | 6.2.3 | − |

    - MCPS-DATA.request

The primitive requests the transfer of data to another PD. The properties of this primitive are:

MCPS-DATA.request {

phyModeSelection;

SourceAddress;

DestinationAddress;

MulticastGroupId;

EtherType;

MsduLength;

Msdu;

TransmitTimeOut;

DataType;

DataRate;

PurgeMode;

AckTX;

Ranging;

IeList;

RequestRriTx;

CyclicSuperframeStructure;

}

The primitive parameters are defined in Table 65.

Table 65—MCPS-DATA.request parameters

| Property | Type | Valid range | Description |
| --- | --- | --- | --- |
| SourceAddress | MAC address | PD specific | The address of the PD from which the frame originated. |
| phyModeSelection | Enumeration | LOW-MOBILITY, HIGH_MOBILITY, GFSK, UWB_BPM_BPSK, UWB_OOK | PHY selection |
| DestinationAddress | MAC address | PD specific | Address of the PD for which the frame is intended. |
| MulticastGroupId | Integer | 0 to 216 −1 | Group ID. |
| EtherType | Unsigned | 0 to 216-1 | The EtherType value to use in the MAC data frame. |
| MsduLength | Integer | 0-macMaxFrameLength | MSDU length in octets. |
| Msdu | array of octets | - | The octets to send in the Data Payload field of the MAC data frame. |
| DataType | Enumeration | AUDIO, VIDEO, DATA | Indicates the type of data that is sent in the stream. |
| DataRate | Integer | Valid data rate for current PHYs | Indicates the data rate |
| PurgeMode | Boolean | TRUE, FALSE | If TRUE, the MSDU in the transaction buffer corresponding to MSDUhandle, is discarded from the transaction buffer. |
| AckTX | Boolean | FALSE, TRUE | This parameter is present only when phyModeSelection is UWB. TRUE if acknowledged transmission is used, FALSE otherwise. |
| Ranging | Boolean | FALSE, TRUE | This parameter is present only when phyModeSelection is UWB. TRUE if ranging bit in PHR is to be set, FALSE otherwise. |
| IeList | Set if IEs as described in Table 11 | As described in Table 11 | This parameter is present only when phyModeSelection is UWB. Determines/supplies the IEs to be sent, including: RRRT IE, RRTD IE, RPRT IE, RRTM IE, RCDT IE and RTOF IE |
| RequestRrtiTx | Boolean | TRUE, FALSE | This parameter is present only when phyModeSelection is UWB. This parameter requests that the PD inserts an RRTI IE in the sent data frame. If the MCPS-DATA.request is early enough the data frame shall be sent at the configured macRngRrtiTime otherwise shall be sent as soon as possible thereafter. |
| CyclicSuperframeStructure | Cyclic-superframe structure descriptor | As defined in Table 31 | Indicates the structure of cyclic-superframe |

    - MCPS-DATA.confirm

The primitive reports the results of a request to transfer data to another PD. The properties of this primitive are:

MCPS-DATA.confirm {

Status;

TxRangingCounter;

RxRangingCounter;

IeList;

TxRrtiValue;

AoaAzimuth;

AoaElevation;

AoaPresent;

Rssi;

}

The primitive parameters are defined in Table 66.

Table 66—MCPS-DATA.confirm parameters

| Property | Type | Valid range | Description |
| --- | --- | --- | --- |
| Status | Enumeration | SUCCESS, TRANSACTION_EXPIRED, CHANNEL_ACCESS_FAILURE, NO_ACK, COUNTER_ERROR, INVALID_PARAMETER, PURGE_SUCESS, INVALID_HANDLE | The status of the last MSDU transmission. |
| TxRangingCounter | Unsigned Integer | 0 to (232 −1) | This parameter is present only when phyModeSelection is UWB. The timestamp of the transmitted data frame |
| RxRangingCounter | Unsigned Integer | 0 to (232 −1) | This parameter is present only when phyModeSelection is UWB. For an acknowledged transmission this is the timestamp of the received acknowledgement frame. For a non-acknowledged transmission this parameter is invalid. |
| IeList | IEs received in the ACK | As defined in Table 11 | This parameter is present only when phyModeSelection is UWB. For an acknowledged transmission this reports the IEs received in the ACK including: RRTI IE |
| TxRrtiValue | Unsigned Integer | 0 to (232 −1) | This parameter is present only when phyModeSelection is UWB. This reports the value sent in the RRTI IE where this was requested by the RequestRrtiTx parameter of the MCPS-DATA.request. |
| AoaAzimuth | Float | -π to +π | This parameter is present only when phyModeSelection is UWB. For an acknowledged transmission this is the AOA of the received signal in azimuth measured in radians, relative to some PD specific axis defined by its antenna arrangement or orientation. This parameter is valid only when the AoaPresent parameter is either AZIMUTH or BOTH. |
| AoaElevation | Float | -π to +π | This parameter is present only when phyModeSelection is UWB. For an acknowledged transmission this is the AOA of the received signal AOA of the received signal in elevation measured in radians. This parameter is valid only when the AoaPresent parameter is either ELEVATION or BOTH. |
| AoaPresent | Enumeration | NONE, BOTH, AZIMUTH, ELEVATION | This parameter is present only when phyModeSelection is UWB. Indicates validity of AoaAzimuth and AoaElevation parameter. For a non-acknowledged transmission or where AOA is not supported this parameter value shall be NONE. |
| Rssi | Integer | 0 to 255 | This parameter is present only when phyModeSelection is UWB. For an acknowledged transmission this reports the received signal strength for the ACK frame. This is a measure of the RF power level at the antenna based on the gain setting in the RX chain and the measured signal level in the channel. For the UWB PHY the RSSI value is measured during the frame Preamble and locked when a valid SFD is detected. A value of zero indicates that RSSI measurement is not supported or was not measured for this frame. |

The MCPS-DATA.confirm primitive returns a status of either SUCCESS, indicating that the request to transmit was successful, or the appropriate error code.

If the transmission uses CSMA-CA or CFP and those failed due to adverse conditions on the channel, the MAC sublayer will discard the MPDU and the Status property will be set to CHANNEL_ACCESS_FAILURE.

    - MCPS-DATA.indication

The primitive indicates the reception of data from another PD. The properties of this primitive are:

MCPS-DATA.indication{

phyModeSelection;

SourceAddress;

DestinationAddress;

MulticastGroupId;

EtherType;

MsduLength;

Msdu;

CQI;

DataSequenceNumber;

DataRate;

TxRangingCounter;

RxRangingCounter;

IeList;

AoaAzimuth;

AoaElevation;

AoaPresent;

Rssi;

Security;

}

The primitive parameters are defined in Table 67.

Table 67—MCPS-DATA.indication parameters

| Property | Type | Valid range | Description |
| --- | --- | --- | --- |
| SourceAddress | MAC address | PD specific | The address of the PD from which the frame originated. |
| DestinationAddress | MAC address | PD specific | Address of the PD for which the frame is intended. |
| MulticastGroupId | Integer |  | Group ID. |
| EtherType | Unsigned | 0 to 216-1 | The EtherType value from the received data frame. |
| MsduLength | Integer | 0-macMaxFrameLength | MDSU length in octets. |
| Msdu | array of octets | - | The octets from the Data payload field of the received data frame. |
| CQI | Integer | 0 – 4 | CQI value measured during reception of the PSDU. |
| DataSequenceNumber | Integer | 0-255 | Data number sequence of the received data frame. |
| DataRate | Integer | Valid data rate for current PHYs | Indicates the data rate. |
| RxRangingCounter | Unsigned Integer | 0 to (232 −1) | This parameter is present only when phyModeSelection is UWB. The timestamp of the received data frame |
| TxRangingCounter | Unsigned Integer | to (232 −1) | This parameter is present only when phyModeSelection is UWB. If the received frame had the AR bit set, then this is the timestamp of the transmitted acknowledgement frame, otherwise this parameter is invalid. |
| IeList | Set if IEs as described in Table 11 | As defined in Table 11 | This parameter is present only when phyModeSelection is UWB. Reports the IEs received including: RRRT IE, RRTD IE, RRTI IE, RPRT IE, RRTM IE, RCDT IE and RTOF IE |
| AoaAzimuth | Float | -π to +π | This parameter is present only when phyModeSelection is UWB. AOA of the received signal in azimuth measured in radians, relative to some PD specific axis defined by its antenna arrangement or orientation. This parameter is valid only when the AoaPresent parameter is either AZIMUTH or BOTH. |
| AoaElevation | Float | -π to +π | This parameter is present only when phyModeSelection is UWB. AOA of the received signal in elevation measured in radians. This parameter is valid only when the AoaPresent parameter is either ELEVATION or BOTH. |
| AoaPresent | Enumeration | NONE, BOTH, AZIMUTH, ELEVATION | This parameter is present only when phyModeSelection is UWB. Indicates validity of AoaAzimuth and AoaElevation parameter. Where AOA is not supported this parameter value shall be NONE. |
| Rssi | Integer | 0 to 255 | This parameter is present only when phyModeSelection is UWB. The received signal strength for received frame. This is a measure of the RF power level at the antenna based on the gain setting in the RX chain and the measured signal level in the channel. For the UWB PHY the RSSI value is measured during the frame Preamble and locked when a valid SFD is detected. A value of zero indicates that RSSI measurement is not supported or was not measured for this frame. |
| Security | Enumeration | SUCCESS, FAIL | To indicate whether the data is successfully decrypted and authenticated or not. |

  - PAC information base (PIB)

The PIB comprises the fields required to manage the MAC sublayer and PHY layer of a PD, and presented in Table 73.

The fields associate to the PHY layer and MAC sublayer use the prefix phy and mac, respectively. Constants are READ_ONLY.

Table 73—PIB fields

| Field | Type | Range | Default | Description |
| --- | --- | --- | --- | --- |
| PD_ID | IEEE EUI-48 | READ_ONLY | Implementation specific | PD MAC address |
| phyCurrentChannel | Integer | As defined in table Table 76 | Implementation specific | The RF channel number used for Tx and Rx |
| phyCurrentPage | Integer | As defined in table Table 76 | Implementation specific | The RF channel page used for Tx and Rx |
| phyTurnaroundTime | Integer | READ_ONLY | Implementation specific | RX-to-TX or TX-to-RX turnaround time (in symbol periods), as defined in Table 81 |
| phySHRduration | Integer | - | Implementation specific | The length of the PHY header in symbols for UWB |
| phySymbolsperOctect | Float | - | Implementation specific | Number of symbols per octet |
| phyModeSelection | Enumeration | LOW_MOBILITY, HIGH_MOBILITY, GFSK, UWB_BPMBPSK, UWB_OOK. | Implementation specific | PHY selection |
| phyUWBPreambleCode | Unsigned Integer | For UWB PHY: 1 to 48 for the BPM-BPSK modulation mode; and, 1 to 33 for the OOK modulation mode. | Implementation specific | For the UWB PHY the value here shall select the preamble code to employ. The value selects the code as per the “Preamble Sequence ID” column of Table 120 for the BPM-BPSK modulation mode, of Table 124 for the OOK modulation mode, For other PHY the value here is ignored. |
| phyUWBTxRmarkerOffset | Unsigned Integer | 0 to (232 −1) | Implementation specific | The propagation time from the internal transmit timestamp to the transmit antenna. The units of this are defined in 10.4.1. The PD adds this offset to its internal transmit timestamp to get the reported TxRangingCounter value. |
| phyUWBRxRmarkerOffset | Unsigned Integer | 0 to (232 −1) | Implementation specific | The propagation time from the receive antenna to the internal receiver timestamp. The units of this are defined in 10.4.1. The PD subtracts this offset from its internal receive timestamp to get the reported RxRangingCounter value. |
| macUWBRngAckRrtiSupport | Boolean | READ_ONLY | Implementation specific | Read only value indicating whether the PD is able to generate an RRTI IE within the standard macImmAckTime and insert it into a ranging ACK frame. |
| macUWBRngAckRrtiEnable | Boolean | TRUE, FALSE | Implementation specific | When set the PD MAC shall automatically generate and insert an RRTI IE in a ranging ACK frame, where the RFRAME being acknowledged carried an RRRT IE and where macRngAckRrtiSupport indicates that the PD is capable of doing this. |
| macUWBRngMinRrtiTime | Unsigned Integer | READ ONLY | Implementation specific | This is a read only value reporting the minimum RX to TX response time that the PD supports for inserting an RRTI IE into a MAC data frame. The units of this are defined in 10.4.1. A value of zero shall indicate that the PD cannot support RRTI insertion, i.e. so the upper layers know to employ an RRTD IE in the ranging exchanges. |
| macUWBRngRrtiTime | Unsigned Integer | - | Implementation specific | This sets the desired RX-to-TX response time for the PD to use when inserting an RRTI IE into a MAC data frame. The units of this are defined in 10.4.1. The value set should take account of the macRngMinRrtiTime and any upper layer delays in initiating transmission, be reflected in the preferred response time indicated via RPRT IE exchanges. |
| macGroupIdList | Array of integers | 0 – 255 per element in the array | Implementation specific | List if Group IDs |
| macPDIdList | Array of MAC addresses | PD specific | Implementation specific | List of PD IDs per Group ID |
| macAddress | IEEE EUI-48 | READ_ONLY | Implementation specific | PD MAC address |
| macPeeringPermit | Boolean | TRUE, FALSE | FALSE | Indication of whether a PD is currently allowing peering. A value of TRUE indicates that peering is permitted. |
| macDSN | Integer | 0 ─ 255 | ─ | The sequence number added to the transmitted Data frame or MAC command. |
| macREpermit | Boolean | TRUE, FALSE | TRUE | TRUE if the PD accepts RE requests. FALSE otherwise. |
| macMaxFrameRetries | Integer | - | 6 | The maximum number of retries allowed after a transmission failure. |
| macPromiscuousMode | Boolean | TRUE, FALSE | FALSE | A TRUE value indicates that the MAC sublayer accepts all frames received from the PHY. FALSE otherwise. |
| macRangingSupport | Boolean | TRUE, FALSE | FALSE | This indicates whether the MAC sublayer supports ranging features. |
| macResponseWaitTime | Integer | - | 5 | The maximum time, in multiples of aSuperframeDuration, a PD shall wait for a response command to be available following a request command. |
| macRxOnWhenIdle | Boolean | TRUE, FALSE | FALSE | Indication of whether the MAC sublayer enables its receiver during idle periods. |
| macSecurityEnabled | Boolean | TRUE, FALSE | FALSE | A value of TRUE indicates that security is enabled in the MAC sublayer. FALSE otherwise. |
| macPriorityChannelAccess | Boolean | TRUE, FALSE | FALSE | A value of TRUE indicates that PCA is enabled. FALSE otherwise. |
| macMaxFrameSize | Integer | READ_ONLY | 1500 octets | Maximum MSDU size in octets |
| macCyclicSuperframeStructureList | List of Cyclic-superframe Structure Descriptor of PAC groups | Set as list of Group ID and Cyclic-superframe Structure Descriptor defined in Table 31 | ─ | The list of the cyclic-superframe structure of PAC groups operating within communication range |
| PNExhaustionThreshold | Unsigned integer | 0 to (248−1) | N/A | Indicates the maximum range of PN counter |

Table 74—PAC constant table

| Field | Type | Default | Description |
| --- | --- | --- | --- |
| aSuperframeDuration | Integer | 100 | The length of the superframe in ms |
| aScanDuration | Integer | 5 | The time duration of Scan in the number of superframes |
| aSyncPeriodDuration | Integer | 306 | The time duration of Synchronization period in µs |
| aPeeringPeriodDuration | Integer | 10 | The time duration of Peering Period in ms |
| aDiscoveryPeriodDuration | Integer | 1 | The time duration of Discovery Period in ms |
| aCapDuration | Real | 40.694 | The time duration of CAP in ms |
| aCfpDuration | Integer | 48 | The time duration of CFP in ms |

(Normative)

QC-LDPC prototype matrices

(Normative)

Modulation mapping

# (informative)

# (informative)

## The mathematics of two-way ranging

# (informative)

## Design procedure of a primitive (n,k,t) BCH code

# (informative)

(informative)

Use of a cyclic-superframe

A PD contains the PHY and MAC sublayers defined in the standard. In practice, a PD equips also upper layers, PAC adaptation layer and application services, which are beyond the scope of this standard. The role of the PAC adaptation layer is to interface application services and MAC sublayer services.

In a typical scenario, upon receiving a service request from an application service, the PAC adaptation layer configures a cyclic-superframe structure in the consideration of following questions:

- how long discovery phase will last

- how long peering phase will last

- on which period and how many data frames will be transmitted in a certain interval

- how to minimize the duration of active period

- how to avoid interference with other PAC groups

A sequence of operation associated with application, adaptation, and MAC services is as follows:

- A variety of application services require different quality of service in terms of bandwidth and latency, etc.

- In order to provide the required quality of service, PAC adaptation layer selects appropriate types of superframe pattern A and superframe pattern B, and calculates the cyclic-superframe size as described in 5.1.1.2. The PAC adaptation layer selects the times when to start discovery, peering, or data transmission, for avoiding interference with neighboring PDs.

- Upon receiving CyclicSuperframeStrcture parameter from the PAC adaptation layer, the MAC sublayer schedules the access to active periods of a cyclic-superframe.

- Once peering completed with desired peer(s), the PAC adaptation layer informs the application service to begin to communicate.

- A PD’s MAC sublayer scans access periods of a cyclic-superframe and collects the cyclic-superframe structure of PAC groups operating within communication range by listening Discovery Request command frame or Peering Request command frame from other PDs.