IEEE P802.15

Wireless Personal Area Networks

| Project | IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs) |
| --- | --- |
| Title | Resolution for service primitive definitions: PHY Security |
| Date Submitted | September 14, 2016 |
| Source | Byung-Jae Kwak (ETRI), Nah-Oak Song (KAIST), Jeongseok Ha (KAIST), Sangseok Yun (KAIST) |
| Response |  |
| Abstract |  |
| Purpose | For discussion & Approval |
| Notice | This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15. |

Overview

Normative references

Definitions

General description

MAC functional description

MAC services

MLME-SAP primitives

PIB access

Discovery primitives

Peering primitives

De-peering primitives

Frame error notification primitives

Reset MAC sublayer

Receiver enable

Channel scanning

Group configuration

Synchronization

Channel sounding

Dynamic preamble selection

Ranging calibration

Randomness sharing primitives

MLME-GETCHVALUE.request

This primitive requests MLME to quantize and report channel information to be used as shared randomness between PDs in the secret key agreement procedure using physical layer features described in 14.6. The properties of this primitive are:

MLME-GETCHVALUES.request{

}

When generated

This primitive is generated by the next higher layer of a PD, which is engaged in the secret key agreement procedure using physical layer features, to request its MLME to quantize and report channel information.

Effect on receipt

MLME generates PLME-GETCHVALUE.request, described in 8.5.1.2.1, to request its PLME to quantize and report channel information.

MLME-GETCHVALUE.response

This primitive reports the result requested by MLME-GETCHVALUES.request. The properties of this primitive are:

MCPS-GETCHVALUES.confirm{

QuantizedCHInfo;

}

The primitive parameters are defined in Table 59.

Table 59—MLME-GETCHVALUES.response parameters

| Property | Type | Valid range | Description |
| --- | --- | --- | --- |
| QuantizedCHInfo | Integer | 0 to (252 −1) | 1bit quantized channel information |

When generated

This primitive is generated by MLME when PLME-GETCHVALUE.response, described in 8.5.1.2.2, is received from PLME to report the channel information to the next upper layer.

Effect on receipt

The channel information received in MLME-GETCHVALUE.response is appendeded to the existing channel information already received in the previous MLME-GETCHVALUE.response primitives. When enough randomness is accumulated, the next higher layer may generate MLME-POSTPROCESSING.request to MLME to initiate information reconciliation and privacy amplification described in 14.6.2 and 14.6.3, respectively.

Post processing primitives

MLME-POSTPROCESSING.request

This primitive requests post processing procedure, which is described in 14.6.2 and 14.6.3, with given PD. The properties of this primitive are:

MLME-POSTPROCESSING.request{

DestinationAddress;

InfoReconciliation;

PrivacyAmp;

}

The primitive parameters are defined in Table 60.

Table 60—MLME-POSTPROCESSING.request parameters

| Property | Type | Valid range | Description |
| --- | --- | --- | --- |
| DestinationAddress | MAC address | IEEE 48 bit addressing | Address of the PD with which to peer for one-to-one peering. |
| InfoReconciliation | Bit stream | Implementation specific | A parity part of codeword generated by initiating PD for information reconciliation |
| PrivacyAmp | Integer | Implementation specific | The number of bits which should be eliminated in privacy amplification |

When generated

When enough randomness is collected, as described in 14.6.1, the next higher layer generates MLME-POSTPROCESSING.request to request its MLME to transmit Post Processing Request command to its peer PD.

Effect on receipt

MLME transmits Post Processing Request command to its peer PD.

MLME-POSTPROCESSING.indication

This primitive is used to indicate the reception of a post processing request command. The properties of this primitive are:

MLME-POSTPROCESSING.indication{

DestinationAddress;

InfoReconciliation;

PrivacyAmp;

}

The primitive parameters are defined in Table 61.

Table 61—MLME-POSTPROCESSING.indication parameters

| Property | Type | Valid range | Description |
| --- | --- | --- | --- |
| DestinationAddress | MAC address | IEEE 48 bit addressing | Address of the PD with which to peer for one-to-one peering. |
| InfoReconciliation | Bit stream | Implementation specific | A parity part of codeword generated by initiating PD for information reconciliation |
| PrivacyAmp | Integer | Implementation specific | The number of bits which should be eliminated in privacy amplification |

When generated

This primitive is generated by MLME when a PD receives a Post Processing Request command from its peer PD.

Effect on receipt

The next higher layer performs post processing, described in 14.6.2 and 14.6.3, and the result is given to MLME in MLME-POSTPROCESSING.response described in 6.1.15.3.

MLME-POSTPROCESSING.response

This primitive is used to initiate a response to an MLME-POSTPROCESSING.indication primitive. The properties of this primitive are:

MLME- POSTPROCESSING.response{

Status;

}

The primitive parameters are defined in Table 62.

Table 62—MLME-POSTPROCESSING.response parameters

| Property | Type | Valid range | Description |
| --- | --- | --- | --- |
| Status | Enumeration | SUCCESS, FAIL | The status of CRC check after post processing |

When generated

This primitive is generated by the next higher layer upon completion of post processing which was initiated by MLME-POSTPROCESSING.indication described in 6.1.15.2.

Effect on receipt

MLME transmits a Post Processing Response command to its peer PD as a response to Post Processing Request command.

MLME-POSTPROCESSING.confirm

This primitive reports the result requested by MLME-POSTPROCESSING.request of the initiating PD. The properties of this primitive are:

MLME-POSTPROCESSING.confirm{

DestinationAddress;

Status;

}

The primitive parameters are defined in Table 63.

Table 63—MLME-POSTPROCESSING.confirm parameters

| Property | Type | Valid range | Description |
| --- | --- | --- | --- |
| DestinationAddress | MAC address | IEEE 48 bit addressing | Address of the PD with which to peer for one-to-one peering. |
| Status | Logical | SUCCESS, FAIL | The status of the request for post processing |

When generated

This primitive is generated by MLME upon reception of Post Processing Response command from its peer PD to report the result of post processing.

Effect on receipt

The reception of this primitive completes the secret key agreement procedure using physical layer features, which is described in 14.6. The status SUCCESS indicates the PDs engaged in the secret key agreement procedure have identical secret keys. The status FAIL indicates the secret key agreement procedure was not successful.

MAC data service

General PHY requirements

PHY services

Overview

PHY description

PHY procedures

PHY measurements

PHY services

PLME-SAP primitives

PHY characteristics

Channel information primitives

PLME-GETCHVALUE.request

PLME-GETCHVALUE.response

PHY-SAP primitives

PHY

Low mobility PHY specification

High mobility PHY specification

UWB Physical (PHY) layer specification

Transmit power control

Relative positioning and localization

Security’

GCMP

Key management

Handshake operation

Ephemeral ECDH key agreement scheme

Signature scheme

Secret key agreement using physical layer features

Randomness sharing

Information reconciliation

Privacy amplification

# Comments

Needs to be define.

Need to be defined.