## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Use-Cases and Technical Requirements for LPWA Networks]
Date Submitted: [6 November, 2016]
Source: [Joerg ROBERT] Company [Friedrich-Alexander University Erlangen-Nuernberg]
Address [Am Wolfsmantel 33, 91058 Erlangen, Germany]
Voice:[+49 9131 8525373], FAX: [+49 9131 8525102], E-Mail:[joerg.robert@fau.de]
Re: []
Abstract: [This document describes use-cases and technical requirements for LPWA networks]
Purpose: [Discussion within IEEE802 IG LPWA.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Use-Cases and Technical Requirements for LPWA Networks

## Slide 3: Motivation
Definition of potential LPWA use-cases for the qualitative comparison of different standards and technology options
Derivation of orthogonal technical requirements for the efficient comparison of the potential LPWA standards and technology options

## Slide 4: Potential LPWA Application Areas
Smart City
Smart Building
Consumer/Medical
Industrial
Agriculture and Environmental
Infrastructure
Logistics
...
The current list of use-cases is given in document 15-16-0770-00-lpwa

## Slide 5: Application Area Smart City
Smart City: Potential Applications
  Waste Management
  Structural Health Monitoring
  Public Lightning
  Smart Parking
  Vending Machines
Applications share common characteristics, e.g. the channel model
BUT: Other characteristics differ significantly, e.g. the required latency or the data length
 Evaluation based on application areas not useful

## Slide 6: Proposed Orthogonal Parameters
Channel Model
Interference Model
Active Interfering Users
Communication Mode
Data Period
Data Length
Availability
Latency Requirements
Localization Precision
Power Supply
Frequency Regulation

## Slide 7: Definitions of Orthogonal Parameters

## Slide 8: Channel Model
Models the linear channel
  Effects due to multi-path and path
  Devices are randomly distributed within communication cell
Proposed classes:
  Indoor (tbd.)
  Outdoor urban (3GPP spatial channel model, max. cell radius 20km)
  Outdoor rural (3GPP spatial channel model, max. cell radius 10km)
  Satellite (tbd.)

## Slide 9: Interference Model
Models the interference of other systems in license-exempt frequency bands
Proposed classes:
  Dense (tbd.)
  Medium (tbd.)
  Low (tbd.)
  None

## Slide 10: Active Interfering Users per Timeframe
Models the number of active users in a given network cell that use the same LPWA specification
  Required for modeling the number of collisions
  Interfering users may also originate from different uses-cases (e.g. for application area smart city)
  Arrivals based on Poisson distributed inter-arrival process
Proposed classes:
  Low (< 100/h)
  Medium (< 1,000/h)
  High (< 10,000/h)
  Very high (100,000/h and higher)

## Slide 11: Communication Mode
Defines the uplink/downlink characteristics of the devices
  Broadcast transmissions are e.g. firmware updates or updates of the public cyphering key
Proposed classes:
  Uplink only
  Uplink and broadcast downlink
  Uplink and downlink

## Slide 12: Data Period
Defines the transmission characteristics of the data
  Occasionally: Time of transmission cannot be predicted
  Periodically: Time of next transmission is known and can be scheduled by the system
Proposed classes:
  Occasionally, less than 1/day
  Occasionally 1/day
  Occasionally 1/hour
  Occasionally, more than 1/hour
  Periodically 1/day
  Periodically 1/hour
  Periodically, more than 1/hour

## Slide 13: Data Length (Uplink)
Defines the payload data length of each uplink message in bytes
Proposed classes:
  <= 16 bytes
  <= 64 bytes
  <= 256 bytes
  > 256 bytes

## Slide 14: Availability
Defined the minimum required probability that an uplink message of a given device is successfully received
Proposed classes:
  Best effort ( > 90%)
  Medium ( > 99% )
  High ( > 99.9% )

## Slide 15: Latency Requirements
Defines the maximum acceptable latency of a given message
Proposed classes:
  < 1s
  < 10s
  < 1min
  < 10min
  < 60 min
  < 1day

## Slide 16: Localization Precision
Defines the required localization precision if the transmit signal of the device is used for the localization
  A system based on GPS localization would not require this type of localization
Proposed classes:
  < 10m
  < 100m
  Not required

## Slide 17: Power Supply
Defines the type of power supply
Proposed classes
  CR 2025: 3V lithium coin type battery, typ. 500mWh, typ. max. 5mA
  2xAA: Two AA-batteries, 3V, typ. 5Wh, typ. max. 2A
  Energy harvesting: 100mWh/day with storage capacitor (e.g. solar cell 60x60mm, outdoor central Europe during Winter)
  External: External power supply without any restrictions on energy and current

## Slide 18: Frequency Regulation
Defines restrictions caused by the frequency regulation
  Duty cycle, transmit power, frequency hopping, ...
Proposed classes:
  NA: Not regulated (e.g. licensed frequency band)
  ETSI: Has to follow European regulations
  FCC: Has to follow US regulations
  ETSI/FCC: Has to follow US and European regulations

## Slide 19: Use-Case Example

## Slide 20: Use-Case Example ( I / II )
Field monitoring in Kansas: Hundreds of distributed sensors measure soil quality parameters and transmit this information to a central node using license-exempt frequency band
Channel model: Outdoor rural
Interference model: Low (no other systems present)
Active interfering users: Low (low traffic demands of the soil quality sensors)
Communication mode: Uplink
Data period: Periodically 1/h (no sudden changes expected)
Data length: <=16bytes (only few parameters as temperature, moisture, ...)

## Slide 21: Use-Case Example ( II / II )
Availability: Best effort (moderate loss of messages has no impact)
Latency requirement: <60min (no latency requirement, latency should not exceed data period)
Localization precision: <100m (automatic localization of the distributed sensors is preferred)
Power supply: 2xAA (size of sensor is uncritical, energy harvesting may be unsuitable)
Frequency regulation: FCC (operated in Kansas)
Additional use-cases: See document 15-16-0770-00-lpwa

## Slide 22: Thank You!
Comments and Questions?