## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Suitability Evaluation of Network Topologies]
Date Submitted: [4 September, 2017]
Source: [Joerg ROBERT, Pascal THUBERT] Company [Friedrich-Alexander University Erlangen-Nuernberg, Cisco]
Address [Am Wolfsmantel 33, 91058 Erlangen, Germany]
Voice:[+49 9131 8525373], FAX: [+49 9131 8525102], E-Mail:[joerg.robert@fau.de]
Re: []
Abstract: [This document presents the suitability evaluation for different network topologies that may be used for LPWAN.]
Purpose: [Presentation within IG LPWA]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Suitability Evaluation of Network Topologies
Joerg Robert, FAU Erlangen-Nuernberg

## Slide 3: Star (single hop) ( I / II )
One central base-station receives data of user devices
Pros
Simple user devices
Only few powerful base-stations
No additional latency due relaying
Cons
User devices have to be able to achieve the required cell radius  low bit-rates

## Slide 4: Star (single hop) ( II / II )
Power Supply
CR 2025
2xAA
Energy Harvesting
External
Communication Mode
Uplink
Downlink/Uplink
Uplink / Broadcast Downlink
Data Period
Occasionally, less than 1/day
Occasionally 1/day
Occasionally 1/hour
Occasionally, more than 1/hour
Periodically 1/day
Periodically 1/hour
Periodically, more than 1/hour
August 2017
Latency
< 0.25s
< 1s
< 10s
< 1min
< 10min
< 60 min
< 1day
Cell Radius
> 50km
< 50km
< 10km
< 5km
< 1km
Interference Model
Dense
Medium
Low
None

## Slide 5: Extended Star (single hop) ( I / II )
Multiple base-stations receive data of user devices
Pros
Simple user devices
Only few powerful base-stations
No additional latency due relaying
Additional diversity
Possibility for upgrading the network in case of increased traffic
Cons
Multiple distributed base-stations are required

## Slide 6: Extended Star (single hop) ( II / II )
Power Supply
CR 2025
2xAA
Energy Harvesting
External
Communication Mode
Uplink
Downlink/Uplink
Uplink / Broadcast Downlink
Data Period
Occasionally, less than 1/day
Occasionally 1/day
Occasionally 1/hour
Occasionally, more than 1/hour
Periodically 1/day
Periodically 1/hour
Periodically, more than 1/hour
August 2017
Latency
< 0.25s
< 1s
< 10s
< 1min
< 10min
< 60 min
< 1day
Cell Radius
> 50km
< 50km
< 10km
< 5km
< 1km
Interference Model
Dense
Medium
Low
None

## Slide 7: Device to Device ( I / II )
Only communication between devices
Pros
No infrastructure
Cons
Only short range

## Slide 8: Device to Device ( II / II )
Power Supply
CR 2025
2xAA
Energy Harvesting
External
Communication Mode
Uplink
Downlink/Uplink
Uplink / Broadcast Downlink
Data Period
Occasionally, less than 1/day
Occasionally 1/day
Occasionally 1/hour
Occasionally, more than 1/hour
Periodically 1/day
Periodically 1/hour
Periodically, more than 1/hour
August 2017
Latency
< 0.25s
< 1s
< 10s
< 1min
< 10min
< 60 min
< 1day
Cell Radius
> 50km
< 50km
< 10km
< 5km
< 1km
Interference Model
Dense
Medium
Low
None

## Slide 9: Base-Station Assisted Device to Device (single hop) ( I / II )
Base station coordinates the network
Communication also possible between the devices
Pros
Increased link margin due to devices’ proximity
Frequency reuse due to low required transmission power
Lowers Base-Station relay requirements
Cons
Significantly shorter range than for device to base station communications

## Slide 10: Base-Station Assisted Device to Device (single hop) ( II / II )
Power Supply
CR 2025
2xAA
Energy Harvesting
External
Communication Mode
Uplink
Downlink/Uplink
Uplink / Broadcast Downlink
Data Period
Occasionally, less than 1/day
Occasionally 1/day
Occasionally 1/hour
Occasionally, more than 1/hour
Periodically 1/day
Periodically 1/hour
Periodically, more than 1/hour
September 2017
Latency
< 0.25s
< 1s
< 10s
< 1min
< 10min
< 60 min
< 1day
Cell Radius
> 50km
< 50km
< 10km
< 5km
< 1km
Interference Model
Dense
Medium
Low
None

## Slide 11: Unsynchronized Mesh ( I / II )
Pros
Simple MAC and Relay operations
Self-forming, self-healing with - route-over e.g. RPL RFC 6550 - mesh-under e.g. IEEE802.15.10 Routing Protocols  non equal cost multipath no single point of failure
Distributed operation  scalable to 1000’s of nodes
Routing enables diverse PHY technilogies
Cons
Relay Devices have to support asynchronous transmission and reception  Relays are usually powered
Only support stochastic traffic, no hard reservation of resources
Cost/complexity of deploying Relays

## Slide 12: Unsynchronized Mesh ( II / II )
Power Supply
CR 2025
2xAA
Energy Harvesting
External
Communication Mode
Uplink
Downlink/Uplink
Uplink / Broadcast Downlink
Data Period
Occasionally, less than 1/day
Occasionally 1/day
Occasionally 1/hour
Occasionally, more than 1/hour
Periodically 1/day
Periodically 1/hour
Periodically, more than 1/hour
August 2017
Latency
< 0.25s
< 1s
< 10s
< 1min
< 10min
< 60 min
< 1day
Cell Radius
> 50km
< 50km
< 10km
< 5km
< 1km
Interference Model
Dense
Medium
Low
None
Green for leaf devices
Green for leaf devices

## Slide 13: Synchronized Mesh ( I / II )
Pros
Scheduled relays enable Battery operation
High predictability in case of application scheduling
Asynchronous IP operation also possible (e.g. 6TiSCH)  get all the benefits of unsynchronized meshes for unscheduled paths
Possibility to schedule fast paths for urgent data
Scheduled MAC  less interferences
Cons
MAC Level synchronization is hard to achieve and consumes energy (not that much though)
Relay devices have to support transmission and reception (but still can sleep most of the time)
Requires controller for scheduled paths  limit to scalability
Cost/complexity of deploying Relays

## Slide 14: Synchronized Mesh ( II / II )
Power Supply
CR 2025
2xAA
Energy Harvesting
External
Communication Mode
Uplink
Downlink/Uplink
Uplink / Broadcast Downlink
Data Period
Occasionally, less than 1/day
Occasionally 1/day
Occasionally 1/hour
Occasionally, more than 1/hour
Periodically 1/day
Periodically 1/hour
Periodically, more than 1/hour
August 2017
Latency
< 0.25s
< 1s
< 10s
< 1min
< 10min
< 60 min
< 1day
Cell Radius
> 50km
< 50km
< 10km
< 5km
< 1km
Interference Model
Dense
Medium
Low
None

## Slide 15: Any Questions or Comments?