## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Candidate Technologies vs. Use-case Evaluation]
Date Submitted: [11. Sept, 2017]
Source: [Joerg ROBERT] Company [Friedrich-Alexander University Erlangen-Nuernberg]
Address [Am Wolfsmantel 33, 91058 Erlangen, Germany]
Voice:[+49 9131 8525373], FAX: [+49 9131 8525102], E-Mail:[joerg.robert@fau.de]
Re: []
Abstract: [This presentation matches the potentials of the candidate technologies and existing IEEE standards against the use-case requirements ]
Purpose: [Prensentation in IG LPWA]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Candidate Technologies vs. Use-case Evaluation
Joerg Robert (FAU Erlangen-Nuernberg)

## Slide 3: Motivation
During the last plenary the suitability of different technology options wrt. the system parameters has been discussed
This presentation matches the parameters against the use-cases
The results indicate whether the proposed technologies are able to cover the use-cases
Furthermore, the suitability of existing IEEE standards wrt. the use-cases is evaluated

## Slide 4: Modulation Schemes
Scheme | # supported use-cases (max. 24)
OFDM | 24
CDMA | 8
DSSS | 1
FCSS | 0
FHSS | 18
NB-Modulation | 0
https://mentor.ieee.org/802.15/dcn/17/15-17-0495-00-lpwa-use-case-evaluation-of-modulation-schemes.xlsx

## Slide 5: Forward Error Correction
Scheme | # supported use-cases (max. 24)
No FEC | 0
Reed Solomon / BCH | 24
Convolutional Code | 24
Turbo Code (TX side) | 4
Turbo Code (RX side) | 1
LDPC Code (TX side) | 4
LDPC Code (RX side) | 1
Polar Code (TX side) | 24
Polar Code (RX side) | 4
https://mentor.ieee.org/802.15/dcn/17/15-17-0497-00-lpwa-use-case-evaluation-of-fec-schemes.xlsx

## Slide 6: MAC Schemes
Scheme | # supported use-cases (max. 24)
ALOHA | 12
Slotted ALOHA | 13
CSMA | 10
Full Coordination | 13
https://mentor.ieee.org/802.15/dcn/17/15-17-0496-00-lpwa-use-case-evaluation-of-mac-schemes.xlsx

## Slide 7: MAC Schemes
Scheme | # supported use-cases (max. 24)
ALOHA | 12
Slotted ALOHA | 13
CSMA | 10
Full Coordination | 13
https://mentor.ieee.org/802.15/dcn/17/15-17-0496-00-lpwa-use-case-evaluation-of-mac-schemes.xlsx

## Slide 8: Connectivity
Scheme | # supported use-cases (max. 24)
Gateway/Transparent | 24
Plain IPv6 | 1
SCHP IPv6 Header Compression | 24
RFC 6282 Header Compression | 4
https://mentor.ieee.org/802.15/dcn/17/15-17-0498-00-lpwa-use-case-evaluation-of-connectivitiy.xlsx

## Slide 9: Network Topologies
Scheme | # supported use-cases (max. 24)
Star | 24
Extended Star | 24
Device to Device | 12
Base Station assisted D2D | 24
Unsynchronized Mesh | 13
Synchronized Mesh | 19
https://mentor.ieee.org/802.15/dcn/17/15-17-0494-00-lpwa-use-case-evaluation-of-network-toplogies.xlsx

## Slide 10: Existing IEEE Standards
IEEE 802.11ah
IEEE 802.15.4
https://mentor.ieee.org/802.15/dcn/17/15-17-0499-01-lpwa-use-case-evaluation-of-ieee-standards.xlsx

## Slide 11: Fully Supported Use-Cases by Existing IEEE Standards
Domain | Fully Supported Use-Cases
Agriculture and Environmental | 
Consumer/Medical | Assisted Living
Industrial | Asset Tracking, Industrial Production Monitoring
Infrastructure | 
Logistics | 
Smart Building | Access Control, Alarms and Security, Light Switch, Smoke Detectors, Water Pipe Leakage Monitoring
Smart City | 

## Slide 12: Uncovered or Potentially Improvable Use-Cases
Domain | Use-Cases
Agriculture and Environmental | 
Consumer/Medical | Pet Tracking
Industrial | Industrial Plant Condition Monitoring
Infrastructure | Pipeline Monitoring – Terrestrial, Smart Grid - Fault Monitoring, Smart Grid - Load Control, Smart Metering, Structural Health Monitoring
Logistics | Global Tracking, Fast Asset Tracking
Smart Building | 
Smart City | Public Lighting, Smart Parking, Vending Machines – general, Vending Machines - Point of Sale, Waste Management

## Slide 13: Thank You for Your Interest!