## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [HRP UWB PHY enhancements]
Date Submitted: [6th July 2018]
Source: [Billy Verso] Company [Decawave Ltd.]
Address [Peter Street, Dublin 8, Ireland]
Voice:[+353.87.233.7323], E-Mail:[billy.verso (at) decawave.com]
Re: [Proposed enhancements to the HRP UWB PHY]
Abstract: [contribute a proposal to the enhanced impulse radio group w.r.t. the HRP UWB PHY ]
Purpose: []
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: The aim of this presentation:
Outline a set of enhancements to the HRP UWB PHY which will result in:
Improved ranging timestamp integrity and robustness
Reduced on-air transmission times:
  This will increase channel capacity and reduce power consumption by a factor of 8.
Also, outline MAC enhancements to reduce the number of messages to complete a two-way ranging time-of-flight (TOF) measurement:
Shortens the time to complete a TOF measurement:
  Also increases channel capacity and reduces power consumption

## Slide 3: What is meant by enhancements?
The goal of this project is to enhance the HRP UWB PHY and LRP UWB PHY
The PAR’s clear intent is not to make brand new PHYs
  We should be reusing what is present in the PHY as much as possible and not changing anything that does not need change
    i.e. if there are only marginal benefits then we should not be making a change
  We should make sure the enhanced PHYs retain modes of operation allowing interworking with the base PHY on which they are built
For the HRP UWB PHY this means that:
  The peak PRF and chipping rate should remain at 499.2 MHz
  The SHR should use the ternary periodic (Ipatov) preambles
  Data should continue to make use of the current FEC
  PHR length and error correction scheme should not change
  SFD length should not change…. Any other such fundamentals?

## Slide 4: Timestamp integrity and robustness:
The HRP UWB PHY synchronisation sequence is made up of repeated symbols consisting of (ternary) Ipatov sequences with the property of perfect periodic auto-correlation. Accumulation of this correlation yields a channel impulse response (CIR) from which the first arriving ray (RX timestamp) can be determined
The problem:
Accidental or intentional interference from other transmitters of the same sequence, or repeated energy bursts at the preamble symbol rate, can give rise to artefacts in the CIR giving erroneous RX timestamp results

## Slide 5: Timestamp integrity and robustness:
The solution:
Include a cryptographically generated pulse sequence in the transmitted PHY frame and have the receiver generate its own version of this sequence to cross correlate and accumulate to produce a CIR to get the RX timestamp
Since only valid transmitters and receivers know the key to generate this ciphered sequence, it is secure against both accidental interference and intentional malicious attack, neither of which will correlate correctly with the ciphered sequence

## Slide 6: Timestamp integrity and robustness:
Two modes to set where the ciphered sequence is placed in the frame
Mode 1 – After the SFD before PHR
  Deterministic position without needing to adjust for varying data frames length.
  Cipher CIR processing to get the RX timestamp can begin earlier
Mode 2 – After the data
  Allows interworking with receivers expecting normal HRP UWB frame format
  Data can be received without cipher alignment and used to regain alignment

## Slide 7: Ciphered sequence structure:
With the ciphered sequence generated cryptographically it will only be correctly received (correctly correlated in the receiver) when both TX and RX parties know the keys and cryptographic scheme
The receiver can validate the sequence by measuring the strength of the correlation across the whole sequence
To promote interworking between vendors the cryptographic scheme should be defined in the amendment
  The proposed scheme is based on AES-128 in counter mode
  This has a 128-bit key and a 128-bit nonce
  The resultant sequence of 1’s and 0’s define the pulse polarity for the ciphered sequence

## Slide 8
Ciphered sequence CSPRNG:
CSPRNG = Cryptographically secure pseudorandom number generator

## Slide 9
For 64 MHz PRF, the 64 bits of CSPRNG output are used to define 64 pulse polarities
  i.e. 1 gives a positive polarity pulse, 0 gives negative polarity pulse
These are spread by the delta function δL of length L = 4 to create 256 chips, and the symbol is completed with 256 zero chips
  The chipping rate is 499.2 MHz
The symbol time Tcsymb is ~1.0256 µs (mean PRF 62.4 MHz)
Sequence length can be 32 symbols up to 2048, (in steps of 8)
A gap of 512 zero chips is inserted before the start of the first cipher sequence symbol (i.e after SFD in Mode 1 or after the data in Mode 2)
Ciphered sequence structure:

## Slide 10
The 256 zero chips forming the 2nd half of each symbol reduce inter-symbol interference and also simplify the implementation of digital sidelobe minimization (DSM) algorithms
  These DSM algorithms can reduce sidelobes by 25 to 35 dB resulting in lower noise channel impulse response estimates (CIR), generated by accumulation of cross-correlated symbols
The CIR that can be achieved with the ciphered sequence and the DSM algorithm is superior to the CIR obtained from the periodic preamble sequence
  With periodic sequences, certain distortions may add coherently in a repeated way, creating specific artefacts in the resultant CIR
  With non-periodic sequences, such distortions average out, reducing the overall noise levels in the resultant CIR
More details about DSM shall be provided in separate submission
Ciphered sequence accumulation side lobes

## Slide 11
This shows the performance improvement of the ciphered sequence with DSM compared to an Ipatov preamble
The lower noise of the resultant CIR allows a lower threshold be used to find more attenuated first paths
Example ciphered sequence accumulation:
Ipatov preamble accumulation
Ciphered sequence accumulation
Whole span
Zoomed in

## Slide 12: Reduced on-air transmission times:
Frame duration is a critical parameter:
Shorter frames reduce energy consumption
  Energy consumption is proportional to frame length
Shorter frames give a smaller time window for any attack
Shorter frames cause less interference to others
Shorter frames experience less interference from others
Shorter frames give an increased channel capacity

## Slide 13: Frame compression techniques:
Send the PHR at the data rate for 6.81 Mb/s and 27 Mb/s frames
  Two-way ranging applications typically use fixed data rate and frame formats
Compress the preamble and SFD transmission phases
  Choose shorter length Ipatov codes to make shorter symbols
  Reduce the spreading factor in the preamble sequences
    The high peak PRF of the HRP UWB PHY affords this possibility
  Use Ipatov codes with greater proportion of non-zero elements
    Increases symbol energy to compensate for shorter symbols
Compress the ciphered sequence
  Remove the 256 zeros that form the 2nd half of each symbol
Compress the PHR and data symbols for new 27 Mb/s data rate
  remove the burst time hopping and reduce the guard period duration
  Use just BPSK to encode the data, (i.e. no BPM)
  Use 8 pulses per burst instead of 2
    Increases the symbol energy to get more range

## Slide 14: Compressed preamble and SFD
SFD [-1 -1 -1 -1 +1 -1 0 0] spread by the preamble symbol
Using length 31 Ipatov sequences with 25 pulses and 6 zeros
  There are 20 such sequences available
  The 5 chosen here have the lowest cross-correlation within the set
Spread by the delta function δL of length 4,
  (or for very high compression L = 1).

## Slide 15: 250 ns preamble symbol vs. 1µs
The length 31 preamble symbol allows for faster detection and carrier acquisition; instead of 40μs, it can be done in 18μs
Preamble detection works on a symbol by symbol basis using symbol cross correlation, so shorter symbols allow for faster detection
Carrier acquisition also works on a symbol basis so the carrier loop is updated more frequently and locks more quickly and robustly with a shorter symbol
The SFD duration reduces from 8μs to 2μs saving power
Shorter preambles generally have higher cross-correlation peaks, but they are less likely to collide, so they have better overall cross correlation properties
All this results in a lower energy solution with less airtime and more channel capacity

## Slide 16: Compressed cipher sequence
The duration of cipher sequence symbols is halved
This is done by removing the zero chips forming the 2nd half of the symbol
  The symbol time Tcsymb is then ~0.5128 µs and the PRF 124.9 MHz
The only gaps inserted are 256 zero chips before and after the full sequence which is otherwise continuous
  As before its length can be 32 to 2048 symbols in steps of 8
Optionally a very highly compressed mode can be supported where the delta function length L = 1
  Tcsymb is then ~0.1282 µs consisting of just 64 chips at the peak PRF of 499.2 MHz per symbol

## Slide 17: Compressed 27 Mb/s modulation mode
Using existing convolutional encoder (16.3.3.2)*, use output g0 to select 1 of 2 pulse sequences, and g1 to invert or not.
  This convolution code has maximum free distance (coding gain) and comes from Proakis, it is rate 1/8.
And scramble v(n) using the existing scrambler (16.3.2)*, giving 8 chips per burst and 8 chips guard interval.
This modulation is 6 dB better than current HRP UWB PHY 27 Mb/s,
  Same range as 6.8Mb/s in AWGN channel, and just 1 dB worse in heavy multipath environments
  Existing HRP UWB PHY Viterbi decoder can be reused, altering only the input metrics
* Clause reference to IEEE Std 802.15.4-2015

## Slide 18: Proakis reference
The proposed rate 1/8 convolutional code is the K=3 code with generators 7,7,5,5,5,7,7,7 from table 8.3-7 in Proakis, Digital Communications, Fifth Edition. (p 519). dfree is 21

## Slide 19
Operating range comparison

## Slide 20: Pulse Repetition Frequency (PRF)
There has been some discussion in previous sessions about the PRFs proposed in this submission
  In particular is a request to not to make large changes in mean PRF between the various elements of the PHY frame because of the effect this has in the adaption of AGC and ADC thresholds
However, changing PRF should not be a problem if the pulse amplitude is kept constant because AGC and ADC thresholds need to be frozen early in frame
  e.g. soon after preamble is detected
This freezing is required both for security and performance reasons

## Slide 21: Compressed PHR
Reduce PHR duration by sending it at the data rate for 6.81 Mb/s and 27 Mb/s frames.
We can make a new PHR.
  pre-4z PHY won’t be able to receive the PHR at data rate
  Don’t need data rate bits, or SYNC length specifier
  Can modify PHR to allow longer data frames at these higher rates to increase the utility of the standard.
Proposal:
  10 bit length gives 1023 max frame length.
  PHR length and SECDED unchanged so the current HRP PHY one can be reused
  GS bits multiple uses, one is to specify the gap between data and the ciphered sequence in mode 2 for “Simultaneous Ranging”, see next sheet.
    Other than that they are free for “General Signalling”

## Slide 22: Simultaneous ranging
In certain applications, it is required to measure the distance to the nearest of a number of devices.
  e.g. for automotive passive entry with “anchor” points at each corner of a car to determine how far is the key-fob from the car
Simultaneous ranging is a method to reduce airtime and battery consumption by configuring the responding devices to respond at almost the same time with overlapping frames
Savings for the key fob can be very significant since it can send a poll and treat all 4 responses as a single RX frame
  See separate submission on Simultaneous Ranging for more details and various ranging schemes based on it
  The next sheet shows the concept for 4 responding devices where each has a different delay between data and the cipher sequence

## Slide 23
Each responder has different delay but arranges for the ciphered sequences to overlap (except for any TOF differences)
The receiver locks onto one responder (possibly the strongest signal) to receive PHR and data, and then accumulates all responding ciphers
The earliest first path gives measure of nearest responder’s TOF even if that channel is too attenuated for general frame reception.
Simultaneous ranging

## Slide 24: Simultaneous ranging
The GS bits in the PHR serve to let the receiving PHY know which of the four responders it has locked onto and thereby determine the delay to the cipher sequence
To achieve this we need:
  A programmable response time (set differently in each responder)
  A programmable gap in the transmitter between data and ciphered sequence (set differently in each responder)
  A programmable table in the receiver of 4 gaps, GsRxTab[4] (one for each GS encoding 0 to 3)
When not being used for Gap Selection the GS bits can be used as “General Signals” of other application specific info
  In Mode 2 by setting all GsRxTab entries to same delay (e.g. zero)
  Always in Mode 1 where there is a fixed SFD to Cipher gap

## Slide 25: MAC changes to support the previous items:
New PIB attributes providing the API for the new features:

## Slide 26: MAC enhancements for TOF measurement:
The current MAC provides ranging counters in the MCPS-DATA primitives
  This does not promote standardised TOF interworking
  It leaves the messaging for TOF measurement to the upper layers
  In general it is necessary to communicate response times or round-trip delay times between the parties to complete the TOF calculation
The addition of Information Elements (IEs) by amendment 4e provides a mechanism to standardise ranging messages
This also provides an opportunity improve the utility of the MAC such that it would be possible for a TOF estimate to be completed with just two messages, one TX and one RX
  See next sheet

## Slide 27: Ranging mechanism: SS-TWR
For single-sided two-way ranging between two devices, A and B, we need a transmitted message from A and a response from B
  The response could be an ACK generated by the MAC or a data frame sent under upper layer control.
For device A to calculate the estimated time of flight, Tprop, device B needs to communicate its reply time, Treply, to device A.
  This could be done in a subsequent frame, but as a further enhancement we should include the option for the MAC to be able to pre-compute, Treply, and include it in an IE embedded in the reply message,

## Slide 28: Specifying the IEs for TOF measurement:
This may seem like a lot of work, but it is not, since a model for this already exists….
All the necessary IE and mechanisms (and the text) for what is needed have already been developed and included in the recently published IEEE 802.15.8-2017 standard
The proposal here is to copy the relevant text relating to ranging and IE’s from the original TG submission doc:
  15-15-0429-01-0008-text-for-relative-positioning-and-location.docx
The only change needed is re-numbering the IEs
  The 802.15.8 IEs for ranging will need to be merged into the 802.15.4 IE table which should be a small task

## Slide 29
THE END