## Slide 1: IEEE 802.15 TG13 Partial Evaluation of PM-PHY using TG7r1 Channels
Date: 2018-05-09
Author:

## Slide 2: Background
In the IEEE 802.15 TG13 March 2018 meeting (15-18-0084-01-0013), TG13 requested full or partial evaluation results using PM-PHY through either simplified or TG7r1 channel models [1] [2].
This presentation will show the setup and results of a simulation of the Pulse Modulation through the specified channel environment.
  2-PAM (OOK) modulation
  Quantify Bit Error Rate using the TG7r1 channel models
Quantify costs and benefits of Pulse Shaping
  The current draft standard does not specify any pulse shaping.
  What are the consequences of that?
  Different pulse shapes will be used:
    Square
    Root-Raised Cosine
May 2018

## Slide 3: 2-PAM PHY
As defined in the draft 15-18-0003-03-0013 Text Proposal for Pulsed Modulation PHY
Data Rates from 4.7 Mbit/s to 150 Mbit/s
Channel estimation sequences from 32 bits to 1024 bits
Optional HCM
  For this analysis, HCM(1,1) is used
Pulse shaping is not defined
May 2018

## Slide 4: Simulation
This presentation will cover 4 out of 8 of the test points in scenario 3 from TG7r1.
The simulation is agnostic to sample rate
  The data is transmitted at different oversample rates (OSR)
  This allows the results to be relative to the sample rate of the channel data in TG7r1.
A lower OSR would relate to a higher data rate
  If the sample rate were 1 GSPS, and the OSR were 5, then the data rate for 2-PAM would be 1 Mbit/s.
The simulation will run over a range of oversample rates.
May 2018

## Slide 5: Simulation
The simulation is as hardware agnostic as possible.
  The simulation will run of a range of Eb/N0, not SNR or transmit power.
  Eb/N0 does not take propagation into account. Converting transmit power to received SNR to Eb/N0 is specific to the hardware.
All signals will be real and positive valued
  There will be no negative values through the channel.
The simulation will not cover clipping at maximum amplitudes.
  Saturation at the LED is a function of that particular LED.
May 2018

## Slide 6: The Receiver
Channel
Matched Filter
Symbol Timing and Decimation
Hard Decision
*
Equalizer
May 2018

## Slide 7: Synchronization
Barker code used to confirm sampling phase.
Samples
May 2018

## Slide 8: RRC Parameters
Beta = 0.5
Span = 6
RRC has overshoot that will cause negative values.
Negative values must be prevented.
  Clip
  DC Offset
Slide 8
May 2018

## Slide 9: RRC Negative Value Solutions
Pulse Shape Filter
Channel
Matched Filter
TX
RX
*
+
Offset
DC Offset
Pulse Shape Filter
Channel
Matched Filter
TX
RX
*
Clipping Negative Values
May 2018

## Slide 10: Baseline Performance in Ideal Channel with No Corrections to RRC PAM
Both square and RRC pulses meet theoretical performance in impulse channel.
No corrections were applied to the negative values of RRC PAM for this baseline curve.
Eb/N0
Pe
May 2018

## Slide 11: CCDF without Corrections to RRC PAM
The CCDF for uncorrected PAM RRC extends to 4.38 dB
This is 1.35 dB above PAM
May 2018

## Slide 12: Ideal Channel with Offset and Clipping
Clipping the small negative values yields a better BER than expending power on a DC Offset.
Eb/N0
Pe
May 2018

## Slide 13: CCDF with Offset and Clipping
The CCDF for Offset RRC PAM is the same as uncorrected RRC PAM at 4.38 dB,
  1.35 dB above PAM.
The CCDF for Clipped RRC PAM extends to 4.87 dB.
  1.84 dB above PAM
May 2018

## Slide 14: Situation 3: Home Use
8 Locations (D1-D8)
Image from [1]
May 2018

## Slide 15: Situation 3: Home Use
Image from [1]
May 2018

## Slide 16: Channel Response – D1
D1
Samples
Image from [1]
May 2018

## Slide 17: Channel Response – D1
May 2018

## Slide 18: Equalization Process
Linear Equalization, no decision directed feedback
21 Coefficient Channel Estimate
Equalization runs after matched filter and decimation
No Noise in training sequence
Placing an upper bound on linear equalizer performance
May 2018

## Slide 19: Equalization – D1
May 2018

## Slide 20: D1, OSR = 50
Pe
Eb/N0
May 2018

## Slide 21: D1, OSR = 7
Pe
Eb/N0
May 2018

## Slide 22: Channel Response – D2
D2
Samples
Image from [1]
May 2018

## Slide 23: Channel Response – D2
May 2018

## Slide 24: D2, OSR = 7
Eb/N0
Pe
May 2018

## Slide 25: Channel Response – D4
D4
Samples
Image from [1]
May 2018

## Slide 26: Channel Response – D4
May 2018

## Slide 27: D4, OSR = 7
Pe
Eb/N0
May 2018

## Slide 28: Channel Response – D5
D5
Samples
Image from [1]
May 2018

## Slide 29: Channel Response – D5
May 2018

## Slide 30: D5, OSR = 7
Pe
Eb/N0
May 2018

## Slide 31: Results
Most data points in the scenario benefit more from spectral efficiency than the cost in PAPR when there is no equalization.
  D2 and D3 are the exceptions
Pulse Shaping Leads to Higher Spectral Efficiency
  Higher Spectral Efficiency demonstrated greater resilience to limited channel bandwidth.
The system in situation 3 clearly benefits from spectral efficiency.
May 2018

## Slide 32: References
[1] Uysal, Murat, Tuncer Baykas, Farshad Miramirkhani, Nikola Serafimovskim, and Volker Jungnickel. IEEE P802.15-15-0746-01-007a Technical Report, September 2015.
[2] Uysal, Murat, Farshad Miramirkhani, Omer Narmanlioglu, Tuncer Baykas, and Erdal Panayirci. "IEEE 802.15. 7r1 reference channel models for visible light communications." IEEE Communications Magazine 55, no. 1 (2017): 212-217.
May 2018