## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: PM PHY Parametrization
Date Submitted: 4 May 2018
Source: Malte Hinrichs, Volker Jungnickel [Fraunhofer HHI]
Address: Einsteinufer 37, 10587 Berlin, Germany
Voice:[+49-30-31002 284], E-Mail:[malte.hinrichs@hhi.fraunhofer.de]
Re: TG13 Call for Evaluation Results on PM PHY
Abstract: This document proposes a parametrization of the synch. preamble and number of required repetitions for the header based on results from documents 15-18-0173-00-0013 and 15-18-0170-02-0013.
Purpose: Contribution to IEEE 802.15.13
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: IEEE P802.15.13 PM PHY parametrization
Date: 2018-05-04 Place: Warsaw, Poland
Authors:

## Slide 3: Description
Performance of synch., header, and payload over SNR
  Evaluation of Detection Rate for synch. preamble, Packet Error Rate (PER) for header and payload
  PER = (1 - BER)L, L = packet length / bits. Here: 1 FEC codeword
  Spreading gain of HCM assumed to be equal eff. spreading factor: 6 dB for HCM(1,4), 9 dB for HCM(1,8), 12 dB for HCM(1,16)
  Similar spreading gain through repetition assumed for header
Criteria1:
  Sync preamble: Detection rate > 0.999
  Header: (1 - PER) > 0.99
  Payload: (1 - PER) > 0.9
1 SNR values given for the criteria in the graphics are interpolated

## Slide 4: Evaluation in AWGN
Preamble lengths: 48, 96, 192, 384 samples
Coding schemes
  Header: 8B10B + RS 36,24 + 8B10B on parity bits
  Payload: 8B10B + RS 256,248 + 8B10B on parity bits
  Payload (with HCM): RS 256,248 only

## Slide 5: Results: PAM-2 modulation

## Slide 6: Results: PAM-2 with HCM(1,4)

## Slide 7: Results: PAM-2 with HCM(1,8)

## Slide 8: Results: PAM-2 with HCM(1,16)

## Slide 9: Summary AWGN
Following table lists proposed parameters for PM-PHY operation in AWGN:
Payload modulation | Synch preamble length | Repetitions for header
2-PAM+8B10B+RS(256,248) | 48 | 1
2-PAM+RS(256,248)+HCM(1,4) | 96 | 4
2-PAM+RS(256,248)+HCM(1,8) | 192 | 8
2-PAM+RS(256,248)+HCM(1,16) | 384 | 16

## Slide 10: Evaluation with CIR
Evaluated OCRs:
  S3/D3: 200 MHz
  S4/D7: 25 MHz
  Higher OCRs do not work without equalization
  Lower OCRs very similar to AWGN (see docs. 18-170, 18-173)
Short preamble (48 samples)
Coding schemes
  Header: 8B10B + RS 36,24 + 8B10B on parity bits
  Payload: 8B10B + RS 256,248 + 8B10B on parity bits

## Slide 11: PAM-2 over channel S3/D3 @200 MHz

## Slide 12: PAM-2 over channel S4/D7 @25 MHz

## Slide 13: Evaluation with CIR, enhanced synchronization, and FDE
Evaluated OCRs:
  S3/D3: 200 MHz
  S4/D7: 50, 100, 200 MHz
Enhanced synchronization (tolerance & integration window)
  Not evaluated for short preamble yet, thus using 96 samples
FDE with ideal channel knowledge
Coding schemes
  Header: 8B10B + RS 36,24 + 8B10B on parity bits
  Payload: 8B10B + RS 256,248 + 8B10B on parity bits

## Slide 14: PAM-2 over channel S3/D3 @200 MHz with enhanced sync. & FDE

## Slide 15: PAM-2 over channel S4/D7 @50 MHz with enhanced sync. & FDE

## Slide 16: PAM-2 over channel S4/D7 @100 MHz with enhanced sync. & FDE

## Slide 17: PAM-2 over channel S4/D7 @200 MHz with enhanced sync. & FDE

## Slide 18: Conclusions
Choice of preamble length, header repetition, and HCM enable operation in different SNR ranges
Operation without equalization is possible over S3/D3 up to OCR 200 MHz, over S4/D7 up to 25 MHz
Operation with Frequency Domain Equalization and enhanced synchronization (see doc. 18-275) is possible up to OCR 200 MHz over both channels (S3/D3 & S4/D7)