## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: 802.15.4z Comments on 802.11ax Coexistence Assurance Document
Date Submitted: 09-May-2018
Source: Benjamin A. Rolfe
Company: Blind Creek Associates
Address: PO Box 798 Los Gatos CA 95031
Voice: +1 408 332 0725, E-Mail: ben @ blindcreek.com
Re: 802.11 and 802.15 coexistence in 6 GHz bands
Abstract: Comments and suggestions from review of the 802.11ax CAD
Purpose: Promote coexistence analysis and positive coexistence
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Review of doc IEEE 802.11-16/1348r3 TGax Coexistence Assurance Document May 2018 Wireless Interim

## Slide 3: Summary
802.11ax Scope has been changed to include use of the 6 GHz band
Systems based on 802.15.4 UWB PHYs are widely used in the 6 GHz band
Task Group 15.4z has reviewed the CAD and provides comments and suggestions the 11ax TG to help improve the CAD so that there is better understanding of the coexistence characteristics

## Slide 4: 3 Coexistence with non-802.11 systems
Add consideration of 802.15.4 HRP UWB and LRP UWB PHYs which both include channel definitions operating in 6 GHz band. Coexistence has not been characterized or analyzed with respect to impulse modulations in the same band (802.15.4 HRP UWB and LRP UWB).
With reference to CCA/CSMA as a coexistence mechanism, does the current anticipated CCA/CSMA mechanism able to detect 802.15.4 UWB signals for bands above 6 GHz; How does this affect coexistence with 802.15.4 UWB based systems?
An assessment of the impacts on 802.15.4 UWB based on the different 802.11ax channelization options would be helpful.
It would be really helpful to provide analysis of 802.11ax with respect to the 802.15.4 UWB systems as both victim and assailant. This has not been done in a prior 802.11 CAD as far as we can find.
We are aware that there has been extensive consideration of coexistence between 802.11 and 3GPP LAA systems. As this is relevant to the coexistence of 802.11ax. It would be helpful to mention it and provide a reference.

## Slide 5: 5.1 Uplink Multi-User Operation 5.2 Spatial Reuse
Compare 11ax noise floor to the noise floor of HRP UWB and LRP UWB and different distances, different channel widths.

## Slide 6: 5.6 Operation in the 6 GHz Band
An analysis of Packet error rate for 802.11ax, and frame error rate or bit rate for LRP and HRP when used within a representative set of operational ranges would be useful.
Analysis of the effects of 802.11ax CSMA on UWB: How will CSMA hear HRP and LRP pulses?
How will the different bandwidth options affect UWB devices?
What are the effects at similar center frequencies, and at different frequencies for LRP UWB, HRP UWB, and 802.11ax?. What happens at the extremes?