IEEE P802.15
Wireless Personal Area Networks

Project	IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Title	Yang security example
Date Submitted	09 November, 2015
Source	Tero Kivinen Finland	Voice: +358 40 547 4476 E-mail: kivinen@iki.fi
Re:	Example of Yang module for security parts.
Abstract	This document is cut & paste of the text yang module for the security.
Purpose	Start working on the yang module for ULI.
Notice	This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release	The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

typedef key_index {
  type uint8 {
    range 1..255;
  }
}

typedef key_id_mode {
  type enumeration {
    enum ImplicitKeying_0;
    enum GlobalKeyIndexOnly_1;
    enum GlobalShortAddressOwner_2;
    enum GlobalExtendedAddressOwner_3;
  }
}

typedef frame_type {
  typedef enumeration {
    enum Beacon;
    enum Data;
    enum Acknowledgment;
    enum MAC_command;
    enum Reserved;
    enum Multipurpose;
    enum Fragment;
    enum Extended;
  }
}

typedef device_addressing_mode {
  type enumeration {
    enum NONE;
    enum SHORT;
    enum EXTENDED;
  }
}

typedef extended_address {
  type binary;
  length 8;
}

typedef short_address {
  type unit16;
}

typedef pan_id {
  type unit16;
}

typedef ie_type {
  type enumeration {
    enum HEADER;
    enum PAYLOAD;
    enum NESTED_SHORT;
    enum NESTED_LONG;
  }
}

container {
  list key_id_lookup_list {
    key "";
    unique "";
    leaf secKeyIdMode {
      type key_id_mode;
    }
    choice secKeySource {
      case GlobalShortAddressOwner_2 {
        leaf panId {
        type pan_id;
        }
        leaf shortAddress {
        type short_address;
        }
      }
      case GlobalExtendedAddressOwner_3 {
        leaf extendedAddress {
        type extended_address;
        }
      }
    }
    leaf secKeyIndex {
      type key_index;
    }
    leaf secKeyDeviceAddrMode {
      type device_addressing_mode;
    }
    leaf secKeyDevicePanId {
      type pan_id;
    }
    leaf secKeyDeviceAddress {
      choice secKeyDeviceAddrMode {
        case SHORT {
        leaf shortAddress {
        type short_address;
        }
        }
        case EXTENDED {
        leaf extendedAddress {
        type extended_address;
        }
        }
      }
    }
    container secKeyDescriptor {
      list secKeyUsageList {
        key "secKeyUsageFrameType";
        unique "secKeyUsageFrameType secKeyusageCommandId";
        leaf secKeyUsageFrameType {
        type frame_type;
        }
        leaf secKeyUsageCommandId {
        type uint8;
        }
        list secKeyIeUsageDescriptor {
        key "SecKeyIeId";
        unique "secKeyIeId secKeyIeId";
        leaf secKeyIeType {
        type ie_type;
        }
        leaf secKeyIeId {
        type uint8;
        }
        }
      }
      leaf secKey {
        type binary;
        length 16;
      }
      leaf secKeyFrameCounter {
        type uint32;
      }
      leaf secFrameCounterPerKey {
        type boolean;
      }
      list secKeyDeviceFrameCounterList {
        key "secDeviceExtAddress";
        unique "secDeviceExtAddress";
        leaf secDeviceExtAddress {
        type extended_address;
        }
        leaf secDeviceFrameCounter {
        type uint32;
        }
      }
    }
  }
}