## Slide 1
Project: IEEE 802.15 Working Group for Low Power Wide Area Network (LPWAN)
Submission Title: Kookmin Updating Draft Text
Date Submitted: November, 2018
Source: Thang Nguyen, Yeong Min Jang, Sangsung Choi*
Company: Kookmin University, Woosong University*
Address
Voice: +82-2-910-5068
FAX: +82-2-910-4449
E-Mail: yjang@kookmin.ac.kr
Re:[]
Abstract:
Purpose:
Notice: This document has been prepared to assist the IEEE 802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by 802.15.

## Slide 2
Table 7-9─LECIM PHY Type and Bands Supported field encoding (continued)
Bit number | Description
12 | Band 262~264 supported
13-15 | Reserved
  7.4.2.12 LECIM Capabilities IE
  For band supported field encoding, add band 262~264 supported as shown in the table 7-9
  Bit 1-12 indicates supported for different band. The encoding for the field is shown in Table 7-9

## Slide 3
Table 7-11─LECIM PHY Features Supported field encoding for FSK (Continued)
Bit number | Description
7 | Symbol rate 6.25 ksymbol/s supported, 200 kHz channel spacing
8 | Symbol rate 6.25 ksymbol/s supported, 100 kHz channel spacing
9 | Symbol rate 2.4 ksymbol/s supported, 12.5 kHz channel spacing
10 | Symbol rate 4.8 ksymbol/s supported, 12.5 kHz channel spacing
  7.4.2.12 LECIM Capabilities IE
  Add lower symbol rate 6.25 ksymbol/s supported with 100/200 kHz channel spacing.
  For narrowband system, add 2.4 and 4.8 ksymbol/s supported with 12.5 kHz channel spacing

## Slide 4
Field value | Symbol rate
0 | 37.5 ksymbol/s
1 | 25 ksymbols/s
2 | 12.5 ksymbol/s
3 | 6.25 ksymbol/s
  7.4.4.17 LECIM FSK Operating Mode IE
  For symbol rate field valid values, add 6.25 ksymbol/s optional PHY as defined in the table 7-31
Table 7-31─Symbol rate field valid values

## Slide 5
  10.1.1 Operating frequency range
  For LECIM FSK PHY operating frequency ranges, an additional band designation 262~264 MHz is added in Table 10-3 below.
  The modulation for narrowband system shall be FSK or Gaussian-based FSK (G-FSK)
Table 10-3─LECIM FSK PHY operating frequency ranges (Continued)
Band designation | Bandwidth (kHz) | Modulation | Bit rate (kb/s)
262~264 MHz | 12.5 | FSK/G-FSK | 2.4
 |  |  | 4.8

## Slide 6
  10.1.2.10.2 Channel numbering for LECIM FSK PHY
  The parameters TotalNumChan and ChanCenterFreq0 for 262~264 MHz band are specified in Table below
  Flexible channel bandwidth (<200kHz) of 262~264MHz band allows to adapt the narrowband FSK transceivers (no center frequency)
Band designation | TotalNumChan | ChanCenterFreq0 (MHz)
262~264MHz | 160 | -
Table 10-15─TotalNumChan and ChanCenterFreq0 when ChanSpacing = 12.5kHz

## Slide 7
  11.3 PHY PIB attributes
  For SFD spreading, add PHY PIB attributes as shown in table 11-2 below
Attribute | Type | Range | Description
phyLECIMFSKSFDSpreading | Boolean | TRUE, FALSE | A value of TRUE indicates that SFD spreading is enabled. A value of FALSE indicates that SFD spreading is disabled
phyLECIMFSKSFDSpreadingFactor | Enumeration | 1, 2, 4, 8, 16 | The SFD spreading factor (SF) to be used when phyLECIMFSKSFDSpreading is TRUE. This attribute is only valid for the LECIM FSK PHY
Table 11-2—PHY PIB attributes(continued)

## Slide 8
  24.3 Modulation and coding for LECIM FSK
  The modulation for the LECIM FSK PHY shall be FSK, PFSK/GFSK
    In the 169 MHz band, the modulation index shall be follow:
      0.5 for 25 kb/s
      1.0 for 12.5 kb/s
  In the 262~264 MHz band, the modulation index shall be as follows:
    2.0 for 2.4kb/s
    1.0 for 4.8 kb/s
      For all other FSK PHY band identifiers, the modulation index shall be as follow:
        0.5 for 37.5 kb/s
        1.0 for 25 kb/s
        2.0 for 12.5 kb/s
        2.0 for 6.25 kb/s
        Either 100kHz or 200kHz channel spacing may be used as permitted by local regulation

## Slide 9
  24.3.6 Spreading
  SFD spreading is determined by PIB attribute phyLECIMFSKSpreading
The SFD spreading factor (SF) can be 1, 2, 4, 8, 16, and the SF value is determined by the PIB attribute phyLECIMFSKSFDSpreadingFactor.
SFD spreading is a function that the input bit (s0) of the SFD sequence is mapped to the spread bit stream (c0, c1, ..., cSF-1) and is shown in Table 24-4-1.
SFD spreading factor | Input bit (s0) = 0 | Input bit (s0) = 1
2 | (c0,c1) = 01 | (c0,c1) = 10
4 | (c0,…,c3) = 0101 | (c0,…,c3) = 1010
8 | (c0,…,c7) = 0101 0110 | (c0,…,c7) = 1010 1001
16 | (c0,…,c15)=0101 0110 0101 0110 | (c0,…,c15)= 1010 1001 1010 1001
Table 24-4-1 --- Input bit to SFD spreading bits mapping