## Slide 1
IEEE 802.15 TG13 Proposal of several new MAC frames
Date: 2018-11-13
Author:

## Slide 2: Table of Content
GTS allocation
HCM allocation
MCS Update
LED selection

## Slide 3: GTS allocation/deallocation
GTS request command
  GTS direction
    Indirect transmission is removed from the standards
    Device doesn’t have criteria to request receive GTS
    Propose:
      Remove receive GTS
      Remove requirement of acknowledgment for GTS request
  GTS assignment mechanism
    First come first serve
    Decline or accept as is
    Propose:
      Balance the requests from all devices
      Accept based on capacity
GTS allocation/deallocation frequency
  Beacon frame vs. GTS response command:
    GTS response command in Draft 3.1 as in section I.16 will not work
    Propose: New GTS response command (next slide)
  Each request can only be granted as early as the next superframe
  Propose: Coordinator evaluates GTS assignment in every superframe
GTS deallocation initiator
  Propose: No GTS requests means deallocation

## Slide 4
Bits: 0-3 | 4 | 5 | 6-7
GTS Length | GTS Direction | Characteristics Type | Reserved
Figure 140
D3.1
Bits: 0-7
Outgoing FIFO size
Proposing
To replace Figure 140
Bits: 0-3 | 4-7
GTS Starting Slot | GTS Length
To replace Figure 142
Octets: 7 | 1
MHR fields | GTS characteristics
GTS characteristics

## Slide 5
HCM allocation (new)
HCM allows for simultaneous downlink transmission for all devices
Each HCM row of HCM matrix can be assigned to different devices
The data rate is proportional to the number of rows assigned
Propose: HCM allocation command Type:Subtype 00:0110
HCM allocation is based on current outgoing traffic size for each device.
The HCM allocation is balanced among all devices based on outgoing traffic size
The mechanism of balancing is out of scope.

## Slide 6
HCM Allocation Command frame format
Octets: 7 | 1
MHR fields | HCM Mask
Each bit in HCM mask represents one row in HCM matrix (total of 8 rows)

## Slide 7
MCS Request Command (new)
Receiver requests MCS adjustment based on channel condition
Type:Subtype 00:1100
The requested MCS is absolute value in order to avoid out-of-sync update caused by frame loss
Requested MCS is calculated based on the current reception MCS and channel condition measurement.
The modulation and coding scheme (MCS) ID from Table 76 shall be used.
The requested MCS is not guaranteed. The transmitter acknowledges the decision by updating MCS field in the PHY header.
The mechanism to generate the requested MCS is out of scope.

## Slide 8
Octets: 7 | 1
MHR fields | New MCS for future RX
MCS Request Command frame format

## Slide 9
LED Selection Request (new)
LED selection mechanism selects the LED in a multi-LED transmitter
Transmitter transmits LED selection request frame
  Header: using previous selected LED
  Payload: using all LEDs in sequence

## Slide 10
Start
Receive LED Selection Request?
Resume data transmission
no
Count the errors in each repetition of test pattern from each LED; Find the LED with least errors
yes
Create LED Selection Response
Send LED Selection Response
  Example LED Selection mechanism

## Slide 11
Octets: 7 | 16 | 16 | … | 16
MHR fields | LED selection pattern using LED #1 | LED selection pattern using LED #2 | … | LED selection pattern using LED #N
LED Selection Request Frame Format

## Slide 12
LED Selection Response (new)
Receiver examines bit errors of the received LED Selection Request
Receiver compares the bit errors among different LEDs
Receiver makes decision of LED selection based on the comparison
The mechanism to select LED is out of scope
Receiver sends LED Selection Response to indicate the transmitter the selected LED for the future transmission

## Slide 13
Octets: 7 | 1
MHR fields | LED Response Number
LED Selection Response Frame Format