## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Revised proposal of SRM Request/Response flows and related primitives]
Date Submitted: [11 March, 2019]
Source: [Hidetoshi Yokota, Shoichi Kitazawa] Company [Landis&Gyr, Muroran IT]
Address: [Tokyo Japan, Hokkaido Japan]
Voice: [], E-Mail: [hidetoshi.yokota@landisgyr.com, kitazawa@ieee.org]
Re: [Proposal of SRM Request/Response flows and primitives]
Abstract: [This contribution proposes new SRM Request/Response flows and related primitives based on the discussion in TG4md CRG.]
Purpose: [Discussion and Approval]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Current flow of SRM Request/Response (1)
Device
MLME
Device next
higher layer
MLME-SRM.request
SRM Request
SRM Response
MLME-SRM.indication
MLME-SRM.response
MLME-SRM.confirm
Device
MLME
Device next
higher layer
MLME-GET.request
MAC PIB
MLME-GET.confirm
Example procedure
Figure 6-85 (Page 166, Sub clause 6.17.2.3, Line#1)

## Slide 3: Current flow of SRM Request/Response (2)
Device
MLME
Device next
higher layer
MLME-SRM.request (TPC)
SRM Request (TPC)
SRM Response
MLME-SRM.confirm
Device
MLME
Device next
higher layer
Device
PHY
MLME-SET.request
MLME-SET.confirm
TPC process
Figure 6-86 (Page 166, Sub clause 6.17.2.3, Line#5)
Example procedure
(*)

## Slide 4: Modified flow of SRM Request/Response (1)
Device
MLME
Device next
higher layer
MLME-SRM-REQ.request
SRM Request
SRM Response
MLME-SRM-REQ.indication
MLME-SRM-RES.request
MLME-SRM-RES.indication
Device
MLME
Device next
higher layer
MLME-GET.request
MAC PIB
MLME-GET.confirm
Example procedure
Initiating device does not need to wait for SRM Response, which supports the case for a long-term measurement or the case where the completion of the measurement is not predictable.
MLME-SRM-REQ.confirm
MLME-SRM-RES.confirm

## Slide 5: Modified flow of SRM Request/Response (2)
Device
MLME
Device next
higher layer
MLME-SRM-REQ.request (TPC)
SRM Request (TPC)
SRM Response
MLME-SRM-REQ.confirm
Device
MLME
Device next
higher layer
Device
PHY
MLME-SET.request
MLME-SET.confirm
TPC process
Example procedure
(*)
MLME-SRM-RES.indication

## Slide 6: Proposal for MLME-SRM-REQ.confirm and its parameters
Add sub-clause 8.2.26.4:
8.2.26.4 MLME-SRM-REQ.confirm
The MLME-SRM-REQ.confirm primitive reports the results of the MLME-SRM-REQ.request.
The semantics of this primitive are as follows:
MLME-SRM-REQ.confirm (
SrmHandle,
DeviceAddrMode,
DeviceAddress,
Status
)
The primitive parameters are defined in Table 8-78.

## Slide 7: Proposal for MLME-SRM-REQ.confirm and its parameter (cont’d)
Name | Type | Valid range | Description
SrmHandle | Integer | 0x00–0xff | The identifier of the corresponding MLME-SRM-REQ.request primitive.
DeviceAddrMode | Enumeration | SHORT, EXTENDED | The addressing mode of the device requesting to execute SRM operation.
DeviceAddress | Short address or extended address | As specified by the DeviceAddrMode Parameter | The address of the device requesting to execute SRM operation.
Status | Enumeration | CHANNEL_ACCESS_FAILURE, NO_ACK, SUCCESS | The status of the SRM Request attempt.
Table 8-78 --- MLME-SRM-REQ.confirm parameters

## Slide 8: Proposal for MLME-SRM-RES.request parameters
Change Sub-clause 8.2.26.3 as follows. The parameters in the primitive are the same as those in the original MLME-SRM.response
8.2.26.3 MLME-SRM-RES.request
The MLME-SRM-RES.request primitive is used to initiate a response to an MLME-SRM-REQ.indication primitive.
The semantics of this primitive are as follows:
MLME-SRM-RES.request (
...
)
The primitive parameters are defined in Table 8-77, which are provide by the device next higher layer.

## Slide 9: Proposal for MLME-SRM-RES.request parameters (cont’d)
Name | Type | Valid range | Description
SrmHandle | Integer | 0x00-0xff | An identifier which can be used to refer to the particular primitive transaction; used to match an SRM Response with the corresponding SRM Request.
DeviceAddrMode | Enumeration | SHORT, EXTENDED | The addressing mode of the device requesting to execute SRM operation.
DeviceAddress | Short address or extended Address in 7.4.3 | As specified by the DeviceAddrMode Parameter | The address of the device requesting to execute SRM operation.
Table 8-77 --- MLME-SRM-RES.request parameters
Add or change the following parameters in red on Table 8-77:

## Slide 10: Proposal for MLME-SRM-RES.request parameters (cont’d)
PayloadIeList | Set of payload IEs as described in 7.4.3 | --- | The payload IEs, excluding Termination IEs, that are provided by the device next higher layer. If empty, then no payload IEs are included.
The rest of the parameters are the same as in Table 8-77

## Slide 11: Proposal for MLME-SRM-RES. indication parameters
Add Sub-clause 8.2.26.3a as follows:
8.2.26.3a MLME-SRM-RES.indication
The MLME-SRM-RES.indication primitive is used to report the reception of an MLME-SRM Response command.
The semantics of this primitive are as follows:

## Slide 12: Proposal for MLME-SRM-RES. indication parameters (cont’d)
MLME-SRM-RES.indication (
                SrmHandle
                DeviceAddrMode,
                DeviceAddress,
                PayloadIeList,
                MeasureddDeviceAddr,
                MeasuredDeviceAddress,
                SrmStatus,
                SecurityLevel,
                KeyIdMode,
                KeySource,
                KeyIndex
)
The primitive parameters are defined in Table 8-77a.

## Slide 13: Proposal for MLME-SRM-RES. indication parameters (cont’d)
Name | Type | Valid range | Description
SrmHandle | Integer | 0x00-0xff | An identifier which can be used to refer to the particular primitive transaction; used to match an indication primitive with the corresponding MLME-SRM-REQ.request.
DeviceAddrMode | Enumeration | SHORT, EXTENDED | The addressing mode of the device requesting to execute SRM operation.
DeviceAddress | Short address or extended Address | As specified by the DeviceAddrMode Parameter | The address of the device requesting to execute SRM operation.
Table 8-77a --- MLME-SRM-RES.indication parameters
Add the following table:

## Slide 14: Proposal for MLME-SRM-RES. indication parameters (cont’d)
PayloadIeList | Set of payload IEs as described in 7.4.3 | --- | The SRM-related payload IEs, excluding Termination IEs, that were included in the frame. If empty, then no payload IEs are included.
MeasuredDeviceAddrMode | Enumeration | SHORT, EXTENDED | The addressing mode of the device, for which the measurement was executed
MeasuredDeviceAddress | Short address or extended address | As specified by the DeviceAddrMode Parameter | The address of the device, for which the measurement was executed.
SrmStatus | Enumeration | SUCCESS, NON_SUPPORTED, REJECTED | The status of the SRM attempt.

## Slide 15: Proposal for MLME-SRM-RES. indication parameters (cont’d)
SecurityLevel | Integer | As defined in Table 8-77 | As defined in Table 8-77.
KeyIdMode | Integer | As defined in Table 8-77 | As defined in Table 8-77.
KeySource | Set of octets | As defined in Table 8-77 | As defined in Table 8-77.
KeyIndex | Integer | As defined in Table 8-77 | As defined in Table 8-77.

## Slide 16: Proposal for MLME-SRM-RES.confirm parameters
Add sub clause 8.2.26.3b and Table 8-77b as follows:
8.2.26.3b MLME-SRM-RES.confirm
The MLME-SRM-RES.confirm primitive reports the results of the MLME-SRM-RES.request.
The semantics of this primitive are as follows:
MLME-SRM-RES.confirm (
SrmHandle,
DeviceAddrMode,
DeviceAddress,
Status
)
The primitive parameters are defined in Table 8-77a.

## Slide 17: Proposal for MLME-SRM-RES.confirm parameters (cont’d)
Name | Type | Valid range | Description
SrmHandle | Integer | 0x00–0xff | The identifier of the corresponding MLME-SRM-RES.request primitive.
DeviceAddrMode | Enumeration | SHORT, EXTENDED | The addressing mode of the device requesting to execute SRM operation.
DeviceAddress | Short address or extended address | As specified by the DeviceAddrMode Parameter | The address of the device requesting to execute SRM operation.
Status | Enumeration | CHANNEL_ACCESS_FAILURE, NO_ACK, SUCCESS | The status of SRM Response attempt.
Table 8-77b --- MLME-SRM-RES.confirm parameters

## Slide 18: Proposal for MLME-SRM-REPORT.confirm parameters
Name | Type | Valid range | Description
SrmHandle | Integer | 0x00–0xff | An identifier which can be used to refer to the particular primitive transaction; used to match a confirm primitive with the corresponding request.
Status | Enumeration | CHANNEL_ACCESS_FAILURE, NO_ACK, SUCCESS | The result of the attempt to send SRM Report.
Table 8-81 --- MLME-SRM-REPORT.confirm parameters

## Slide 19: Proposal for MLME-SRM-INFORMATION.confirm parameters
Name | Type | Valid range | Description
SrmHandle | Integer | 0x00–0xff | An identifier which can be used to refer to the particular primitive transaction; used to match a confirm primitive with the corresponding request.
Status | Enumeration | CHANNEL_ACCESS_FAILURE, NO_ACK, SUCCESS | The result of the attempt to send SRM Information.
Table 8-84 --- MLME-SRM-INFORMATION.confirm parameters