## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Supplementary document for CID#135]
Date Submitted: [15 September, 2019]
Source: [Shoichi Kitazawa, Ruben Salazar, Chris Hett and Hidetoshi Yokota] Company [Muroran IT, Landis+Gyr]
Address: [Hokkaido Japan, Alpharetta GA, USA]
Voice: [], E-Mail: [kitazawa@ieee.org, {ruben.salazar, chris.hett, hidetoshi.yokota}@landisgyr.com]
Re: []
Abstract: [This contribution is a supplementary document to support the proposed resolution for CID#135]
Purpose: [Discussion]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Definition of Energy Detection
10.2.5 Receiver ED (p.482, l.15)
The receiver ED measurement is intended for use by a network layer as part of a channel selection
algorithm. It is an estimate of the received signal power within the bandwidth of the channel. No attempt is
made to identify or decode signals on the channel. The ED measurement time, to average over, shall be
equal to 8 symbol periods.
The ED result shall be reported to the next higher layer using MLME-SCAN.confirm. The minimum ED
value (zero) shall indicate received power less than 10 dB above the lowest specified receiver sensitivity, in
dBm, for the PHY. The range of received power spanned by the ED values shall be at least 40 dB. Within
this range, the mapping from the received power in decibels to ED value shall be linear with an accuracy of
± 6 dB.

## Slide 3: Current definition (example)
40 dB (minimum)
-120 dBm
-110 dBm
-104 dBm
-98 dBm
-92 dBm
-86 dBm
-80 dBm
-20 dBm
+10 dBm
0 (0x0)
1 (0x1)
2 (0x2)
3 (0x3)
4 (0x4)
5 (0x5)
15 (0xf)
90 dB (4bit expression)
(-70 dBm)
10 dB
6 dB
6 dB
6 dB
6 dB
6 dB
Lowest specified receiver sensitivity (depends on the device)
macED
ED (dBm)
4 bit
Current definition
This satisfies “Receiver ED” requirements

## Slide 4: Proposed resolution (example)
40 dB (minimum)
-120 dBm
-110 dBm
-104 dBm
-98 dBm
-92 dBm
-86 dBm
-80 dBm
-20 dBm
+10 dBm
0 (0x0)
1 (0x1)
2 (0x2)
3 (0x3)
4 (0x4)
5 (0x5)
15 (0xf)
144 dB (8bit expression)
(-70 dBm)
0 (0x00)
6 (0x06)
12 (0x0C)
18 (0x12)
24 (0x18)
30 (0x1E)
90 (0x5A)
120 (0x78)
10 dB
6 dB
6 dB
6 dB
6 dB
6 dB
Lowest specified receiver sensitivity (depends on the device)
macED
ED (dBm)
4 bit
8 bit
Proposed resolution
This looks more than enough, but 8 bit (one octet) expression is aligned with “EnergyDetectList” in MLME-SCAN parameters (Table 8-30, p.313)