## Slide 1
Project: IEEE P802.15 Interest Group for Wireless Personal Area Networks (WPANs)
Submission Title: Application of OFDM waveform for OCC/OWC system based on the rolling-shutter effect of camera.
Date Submitted: Nov 2019
Source: Huy Nguyen, Yeong Min Jang [Kookmin University].
Contact: +82-2-910-5068 E-Mail: yjang@kookmin.ac.kr
Re:
Abstract: Summary considerations about the application of OFDM waveform for OCC/OWC system based on the rolling-shutter effect of the camera.
Purpose: To consider the compatibility of RF in optical V2X communication system
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Introduction
OFDM waveform an important technique in high-speed communication in RF system or LiFi system due to its ability to eliminate Inter-Symbol Interference (ISI).
Application of OFDM waveform to OCC/OWC is required for High Rate OCC system.
Therefore, OFDM system based on the rolling shutter effect is proposed to supplement IEEE 802.15

## Slide 3: Rolling Shutter OFDM scheme architecture
Block diagram of Architecture of Rolling Shutter-OFDM system
Unlike the conventional OFDM in Radio Frequency, instead of feeding the data symbol directly into the IDFT block, each symbol must pass through the Hermitian block.

## Slide 4: Data Structure for Rolling Shutter OFDM scheme
Proposed data frame structure for Rolling Shutter-OFDM system
To support the compatibility of frame rate variation, every packet can contain many sub-packets, and each sub-packet in the same packet has the same data payload with a Sequence Number (SN).
The SN represents the serial number of packets.

## Slide 5: Advantages of Rolling Shutter-OFDM scheme
Frame rate variation support.
Data merger algorithm.
Detection of missing packets.
Reducing Inter-Symbol Interference.
Easy to reduce the trouble of complex noise(blur image, interference, irregular attenuation).

## Slide 6: Proposed Algorithm
Merging packet method and detecting missed packets of the Rolling Shutter-OFDM schemes
Over-sampling:
The Oversampling caused by the frame rate variation of the rolling shutter camera when the frame rate of a rolling-shutter camera becomes many times greater (at least double) than the packet rate of the transmitter, every data packet is sampled at least twice (i.e., two images).
The receiver will eliminate consecutive packets with the same SN and choose packets with consecutive SN (n-1, n, n+1) to the merger.

## Slide 7: Proposed Algorithm
Merging packet method and detecting missed packets of the Rolling Shutter-OFDM schemes
Under-sampling:
It occurs if the frame rate drops to below the packet rate of the transmitter. In this case, the payload will be lost. The detection of a missed payload using the SN.
The data frame achieved from the payload n-1 represents the SN as n-1. The next data frame indicates that the SN is n, but the actual data frame carries SN n+1. This demonstrates that the payload n is missed and the loss is detected by comparing the SN of the two adjacent data sub-packets.

## Slide 8: References
[1] Huy Nguyen, Minh Duc Thieu, Trang Nguyen, and Yeong Min Jang “Rolling OFDM for Image Sensor Based Optical Wireless Communication,” IEEE Photonics Journal, Volume: 11 , Issue: 4 , Aug. 2019.