## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title : Bit-error rate measurement using intensity-shift on-off keying
Date Submitted : [Nov, 2019]
Source : Moh. Khalid Hasan, Md. Shahjalal, Md. Mainul Islam, Mostafa Zaman Chowdhury, and Yeong Min Jang
Company : [Kookmin University]
Address : [Seoul, Korea]
Voice : [+82-2-910-5068], E-Mail: [yjang@kookmin.ac.kr]
Re :
Abstract : This document presents an efficient method for bit-error measurement of intensity-shift on-off keying scheme.
Purpose : To determine the reliability of hybrid OCC/LiFi system.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release : The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
Slide 1

## Slide 2: Introduction
Hybrid OCC/LiFi systems can have great advantage to reduce the bandwidth burden from the radio-frequency based technologies.
LiFi can be used for high data rate transmission, whereas OCC can be used for reliable communication at high distances.
The simultaneous transmission of both technologies will let us to have the benefits of both technologies at the same time.
A single multilevel LED can be used to transmit the data.

## Slide 3: Simultaneous data transmission
Two data streams are transmitted, where each stream is intended for LiFi and OCC.
The first stream is transmitted at a very high frequency using the LED.
The LED flickers in two different power levels creating consecutive sequences.
A smartphone camera receives the sequences as binary successions, wherein the second data stream is modulated.
The modulation is termed intensity-shift on-off keying (ISOOK).

## Slide 4: Threshold
A decision threshold is used in LiFi to decode the data.
The value of the threshold is chosen based on the power levels.
Both levels are defined when PD detects the preamble symbol.
In ISOOK, the images are binarized using another threshold.
The decision threshold is utilized for both OCC and LiFi to measure the bit-error rate (BER).
The bit error rate also depends on the received signal power of PD or camera.

## Slide 5: BER calculation
In OOK signaling, the decision threshold is predominantly used to estimate the BER.
The following equation is used to estimate the BER for the ISOOK scheme:
………….1

## Slide 6: BER calculation
In eq. 1, b0 and b1 correspond to bit “0” and “1”, respectively.
Si is the signal power at the receiver and N0 is the power spectral density of the noise.
l is the length of the transmitted bit sequence.
Td denotes the decision threshold, which is set based on the received power and varied to achieve the optimum BER performance.
For OCC, Si indicates the received power corresponding to the sum of the pixel values that is covered by a stripe in the image sensor.
The stripe width is calculated using the readout time of camera pixels.