## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title : Technical challenges in hybrid OCC/LiFi system.
Date Submitted : [Nov, 2019]
Source : Moh. Khalid Hasan, Md. Shahjalal, Md. Mainul Islam, Mostafa Zaman Chowdhury, and Yeong Min Jang
Company : [Kookmin University]
Address : [Seoul, Korea]
Voice : [+82-2-910-5068], E-Mail: [yjang@kookmin.ac.kr]
Re :
Abstract : This document presents an overview of technical limitations considering transmission of OCC and LiFi data.
Purpose : To discuss the challenges of data transmission in hybrid OCC/LiFi system.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release : The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
Slide 1

## Slide 2: Introduction
In recent times, visible light communication (VLC) has significant potential in both indoor and outdoor environments because existing lighting infrastructures can be used to transmit data.
VLC exhibits numerous beneficial characteristics, such as energy efficiency, low cost, high throughput, high security, and completely free bandwidth.
Currently, radio frequencies (RF) are comprehensively used for communication, whose spectrum is typically licensed and regulated.
VLC is already recognized as a compatible complementary system to RF for reducing the burden of the massive future wireless connectivity.
A single multilevel LED can be used to transmit the data.

## Slide 3: LiFi
Light-fidelity (LiFi) is a latest bi-directional VLC system that utilizes ultra-high-rate flickering of a light-emitting diode (LED) to transmit data.
A photodiode (PD) is integrated into the user device that acts as the receiver.
LiFi supports ultra-high data rates, particularly in Gbps ranges.
The widespread deployment of LED infrastructures has augmented the potential applications of LiFi to a great extent.
However, the impact of interference generated from neighboring light sources is considerable.
Consequently, the average signal-to-interference-plus-noise ratio (SINR) and the bit-error rate (BER) are frequently observed in LiFi.

## Slide 4: OCC
Optical camera communication (OCC) is another promising VLC technology that overcomes the interference problem.
Herein, a camera image sensor is used to receive optical pulses.
In OCC, the interfering elements can be spatially separated from the image sensor.
As a result, the SINR and BER are improved in OCC.
However, most commercial cameras are built with a limited frame rate, which limits the overall data rate for OCC.
Therefore, in particular, OCC is considered promising in the applications where achieving excellent SINR and BER are more important than high data rates.

## Slide 5: Hybrid OCC/LiFi system
LiFi and OCC can be integrated to utilize their advantageous features.
By integrating OCC and LiFi, the question of data rate and reliability can be mitigated to a great extent.
The user quality of service will increase consequently.
LiFi can be used in the scenarios where the data rate is the prime concern.
OCC can be used in the scenario where the reliability (e.g., bit-error rate) is the main issue.

## Slide 6: Challenges
Different LEDs are required to transmit data streams because the modulation bandwidth is completely different for both technologies.
Identifying the correct LED to communicate for a specific application would be challenging.
The same LED can be used for the hybrid system using multiple access techniques. However, the implementation complexity of the network assignment will be high.
Using different LEDs for LiFi and OCC increases the overall cost.