## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [New data rates for HRP UWB]
Date Submitted: [15th Jan 2020]
Source: [Michael McLaughlin, Billy Verso] Company [Decawave Ltd.]
Address [Adelaide Chambers, Dublin 8, Ireland]
E-Mail:[billy.verso (at) decawave.com]
Re: [Data modes for the HRP UWB PHY]
Abstract: [contribute to the enhanced impulse radio group w.r.t. the HRP UWB PHY ]
Purpose: []
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Reminder: Current Draft 802.15.4z Data Modulation, HRP, 27.2 Mb/s mode

## Slide 3: Suggested Lower Bitrate Modulation
Add a modulation mode where each data symbols consists of 128 chips, essentially stretching the 27.2 Mb/s mode by 8x , (PHR uses double this again)
Suggest to limit this optional modulation format (effectively ~3.4 Mb/s) to the following optional frame format:
  HPRF
  PSR = 64 (We think 32 is too short for -96dBm esp. at +/-40ppm)
    Only 12% more pulses for a 20-byte PSDU, 8% more for 40 bytes
    Agree it is best to only have one option here
  SFD length 8 (binary)
  0 or 16 STS symbol repetitions (STS allows sender to be verified)
  Maximum of 40 bytes payload to limit the maximum air time
Twice the bitrate → almost halves power consumption, less air-time → less collisions
Over-the-air looks same as 27.2Mbps mode.
Same number of pulses as PRF128 => same pulse amplitude => same performance
Peak power in 50MHz lower than 27.2Mbps mode
4 guard chips
4 pulses spread 1x
4 guard chips
One symbol (128 chips, 64 pulses)
4 pulses spread 1x
…

## Slide 4: Suggested Higher Bitrate Modulation: 54.4Mbps
Add a modulation mode where each data symbols consists of 8 chips, essentially first half of the 27.2 Mb/s symbols
PHR uses double this again
Range >40m over CM1 multipath channel
4 guard chips
One symbol (8 chips)
4 pulses spread 1x