## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Technical Proposal for TG4aa JRE]
Date Submitted: [26 October, 2020]
Source: [Hiroshi Harada, Ryota Okumura] Company [Kyoto University]
Address [Yoshidahonmachi, Sakyo-ku, Kyoto 606-8501 Japan]
Voice:[+81-75-753-5318], FAX: [], E-Mail:[hiroshi.harada@i.kyoto-u.ac.jp]
Re: [] Abstract: [This document includes Technical Contributions toward the development the amendment of IEEE Std 802.15.4-2020] Purpose: [Technical Proposal for TG4aa JRE.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
Slide 2
Current SUN FSK options for Japan in IEEE 802.15.4
Frequency band (MHz) | Parameter | Operating mode |  |  |  |  |  |  | 
 |  | #1 | #2 | #3 | #4 |  |  |  | 
920-928 MHz | Data rate (kb/s) | 50 | 100 | 200 | 400 |  |  |  | 
 | Modulation | 2-FSK | 2-FSK | 2-FSK | 4-FSK |  |  |  | 
 | Modulation index | 1.0 | 1.0 | 1.0 | 0.33 |  |  |  | 
 | Channel spacing (kHz) | 200 | 400 | 600 | 600 |  |  |  | 
 | Standard | 802.15.4-2020 |  |  |  |  |  |  | 

## Slide 3
Frequency band (MHz) | Parameter | Operating mode |  |  |  |  |  |  | 
 |  | #1 | #2 | #3 | #4 | #XX | #XX | #XX | #XX
920-928 MHz | Data rate (kb/s) | 50 | 100 | 200 | 400 | 400 | 600 | 600 | 800
 | Modulation | 2-FSK | 2-FSK | 2-FSK | 4-FSK | 2-FSK | 2-FSK | 4-FSK | 4-FSK
 | Modulation index | 1.0 | 1.0 | 1.0 | 0.33 | 0.5 | 0.4 | 0.5 | 0.33
 | Channel spacing (kHz) | 200 | 400 | 600 | 600 | 200 * N 1≦N≦5 [2] | 200 * N 1≦N≦5 [2] | 200 * N 1≦N≦5 [2] | 200 * N 1≦N≦5 [2]
 | Standard | 802.15.4-2020 [1] |  |  |  | Proposed |  |  | 
Note: N is integer number
Proposal

## Slide 4
Feasibility Study [3]

## Slide 5
Prototype IC and evaluation board
  Support data rates from 50 kbps to 600 kbps by 2-FSK
  Support IEEE 802.15.4-compliant FEC
  Certified by a certification body in Japan
    Meet the requirements of ARIB STD-T108 under the proposed parameters
High-speed FSK Transmission Scheme
Prototype IC

## Slide 6
Static characteristics of IC
  External LNA: improve transmission quality
  PER and average RSSI calculated by PC from 1,000 transmitted packets
  Input power to receiver: power at the input of the LNA
High-speed FSK Transmission Scheme
Input power to receiver

## Slide 7
Static characteristics of IC
High-speed FSK Transmission Scheme
Parameters | Values |  | 
Modulation Scheme | 2-GFSK |  | 
CH Frequency | 926.9 MHz | 927.0 MHz | 
Data Rate | 100 kbps | 300 kbps | 600 kbps
Modulation Index | 1.0 | 0.5 | 0.4
Preamble Length | 15 octets |  | 
Payload Length | 250 octets |  | 
FEC | OFF, ON |  | 
Encoding Scheme | RSC |  | 
Decoding Scheme | Viterbi (Hard decision) |  | 
Interleaver | ON |  | 
CRC | 16 bits |  | 
Inter-packet Time | 0.35 s |  | 

## Slide 8
Static characteristics of IC
High-speed FSK Transmission Scheme
Target PER = 10%
LNA gain: about 12 dB
Data Rate (kbps) | Required Input Power (dBm)
100 | –105.6
300 | –99.7
600 | –98.6
7.0 dB
Feasibility of proposed high-speed FSK scheme
Possibility of using FEC to improve transmission quality
  600 kbps achieved with a deterioration of 7.0 dB
  FEC improvement: 2.4 dB
  600 kbps w/ FEC is better than 300 kbps w/o FEC

## Slide 9
Measurement field
  Typical urban environment assuming smart metering system
  Transmitter is fixed while receiver keeps moving along different routes
Field Experiment with High-speed FSK
Route A (mostly LoS)
Route B (mostly NLoS)

## Slide 10
Radio stations
Field Experiment with High-speed FSK
Transmitter (concentrator)
  Antenna height: 4.5 m
  Transmission power: 20 mW
Receiver (smart meter device)
  Antenna height: 1.1 m
  SAW filter: remove signals from out bands
  GPS loggers: log location information of receiver while moving
SAW: Surface acoustic wave
GPS: Global position system

## Slide 11
Average input power to receiver
  Input power to receiver: power at the input of the SAW filter
  Average value: calculated from 51 packets before and after
Field Experiment with High-speed FSK

## Slide 12
Average input power to receiver
Field Experiment with High-speed FSK

## Slide 13
Packet error rate
Field Experiment with High-speed FSK

## Slide 14
Packet error rate (for distance)
Field Experiment with High-speed FSK
320 m
200 m

## Slide 15
Communication distance
  High-speed FSK is applicable with a shorter communication distance
  On an LoS road without obvious obstacles, 600 kbps achieves 250 m
  The communication distance of 600 kbps is sufficient in a massive and dense network using multi-hop communication
Field Experiment with High-speed FSK
The shortest distance where PER exceeds 10%
Communication Distance
Data Rate (kbps) | Communication Distance (m) | 
 | Route A (LoS) | Route B (NLoS)
100 | > 320 | 150
300 | > 320 | 120
600 | 250 | 100

## Slide 16
[1] IEEE, “IEEE 802.15.4-2020,” July 2020.
[2] ARIB, “ARIB STD-T108 920MHz-BAND TELEMETER, TELECONTROLAND DATA TRANSMISSION RADIO EQUIPMENT ver 1.3,” Apr. 2019.
[3] Y. Xiang, R. Okumura, K. Mizutani, and H. Harada, “Field Experiment of IEEE 802.15.4 Based High-Speed FSK Transmission Scheme,” IEICE Technical Report, Jan. 2020.
Reference