## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: MIMO-COOK scheme based enhancing performance of OCC system
Date Submitted : November, 2020
Source : Van Hoa Nguyen and Yeong Min Jang
Company : [Kookmin University]
Address : [Seoul, Korea]
Voice : [+82-2-910-5068], E-Mail: [yjang@kookmin.ac.kr]
Re :
Abstract : This document discusses about the MIMO-COOK technique applied in OCC system.
Purpose : To get data from the multiple transmitters and increase the performance of OCC system.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release : The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Introduction
On off keying (OOK) scheme is known as the simplest form of amplitude-shift keying modulation by using two statuses: ON/OFF to transmit data
C-OOK stands for Camera- On Off Keying, a communication mode within the IEEE 802.15.7-2018 Optical Wireless Communication standard. Particularly, C-OOK is within the PHY V layer of IEEE 802.15.7-2018 standard.
MIMO C-OOK scheme, which updated the conventional C-OOK scheme, used MIMO, region of interest, and match filter techniques

## Slide 3: Introduction
The OCC system can easily deploy the MIMO technique. It can cope with the big OCC problem of simultaneous connection with many light sources, and it can make it feasible for the camera as well.
So the main goal of this contribution is to collect data from the multiple transmitters and also enhance performance of existing OCC system such as increase data rate, distance communication

## Slide 4
Figure 1. Reference architecture of the multiple-input multiple-output–camera on–off keying (MIMO–COOK) scheme.

## Slide 5: Advantages of MIMO C-OOK scheme in OCC system
Frame rate variation support. The sequence number (SN) allows the receivers to decode data.
Improve system performance as compared with the conventional C-OOK due to using a matched filter
Improve data rate: Due to using multi-LEDs, the data rate will be increased as compared with the conventional C-OOK.
Improve the communication distance: by using the matched filter to detect the start of frame and decode data, the communication distance is improved than the conventional C-OOK.

## Slide 6: References
[1] V.H. Nguyen, M.D. Thieu, H. Nguyen, and Y. M. Jang, “Design and Implementation of the MIMO–COOK Scheme Using an Image Sensor for Long-Range Communication,” MDPI Sensors Journal, 2020.