## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [The 5 Criteria table and differences in technical requirements for NG UWB - draft for discussions]
Date Submitted: [2nd Feb 2021]
Source: [Boris Danev, David Barras] Company [3db Access]
Address [ ]
E-Mail:[boris.danev(at)3db-aceess.com]
Re: [Criteria for Standards Development (CSD) and PAR for next generation UWB project]
Abstract: [Summary table of features and main characteristics in next generation UWB for CSD and PAR – Draft to fill-in]
Purpose: []
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Table for CSD
Five Criteria (5C) requirements, or “The 5 Critters” for UWB NG
Classes of Devices | Application / Use cases | Broad Market Potential | Compatibility | Distinct Identity | Technical feasibility | Economic feasibility
 |  | a) Broad sets of applicability b) Multiple vendors and numeours users | a) Will comply with 802? b) supply response if a) = no c) Compatibility with IEEE 802.15 d) Conformance with IEEE 802.15 MAC | Substantially different from other 802.15 specs/solutions | a) demonstrated feasability b) proven similar technology via test/mod/sim c) confidence in reliability | a) known cost factors b) balanced costs c) installation costs d) operational costs
Ranging (no infrastructure) | Device-to-Device Distance & Angle of Arrival - access - payment (mobile & transp.) - contact tracing | a) Yes, see applications b) Yes, many players already there | 802.15 WPAN | reduce complexity enable lower power operation enhanced ranging resol. & accuracy low-power discovery enhance coex. w/ narrow band | a) Yes b) Yes via 4z c) Yes via 4z | a) yes, products on the market b) no infrastructure cost c) little installation costs d) no operation costs
Localization (infrastructure) | RTLS - asset tracking - robotic, drone, UAV - trains - shopping analytics | a) Yes, see applications b) Yes, many players already there | 802.15 WPAN | reduce complexity enable lower power operation enhanced ranging resol. & accuracy low-power discovery enhance coex. w/ narrow band | a) Yes b) Yes via 4z c) Yes via 4z | a) yes, products on the market b) known infrastructure costs c) known installation costs d) no operational costs
Sensing | Sensing - mono- or bi-static radars - presence/obstacle detection - gesture/context detection | a) Yes b) Novelda, ... ? | Need of interoperability? | ? | a) Yes, on wider BW ? b) ? c) ? | a) ? b) ? c) ? d) ?
Data streaming | Real time streaming - audio (headphones) | a) ? b) ? | a) ? b) ? c) ? d) ? | ? | a) ? b) ? c) ? | a) ? b) ? c) ? d) ?
 | - AR with multi-channel a/v | a) ? b) ? | a) ? b) ? c) ? d) ? | ? | a) ? b) ? c) ? | a) ? b) ? c) ? d) ?

## Slide 3: Main Features and characteristics
Differences in technical requirements and constraints
Classes of Devices | Application / Use cases | Link budget | Payloads | Current cons. (in active state) | Market acceptance criteria
 |  | classification (assumptions: 0dBi antenna): - very high (PL > 90 dB, d > 100m) - moderate (PL≈ 80 dB, d ≈ 30 m) - proximity (PL≈ 60 dB, d ≈ 3m) | classification: - short payload, small duty cycles - continous payload, larger duty cycle | classifications: - very low to low (up to 10 mA) - moderate to high (100mA+) | key words: cost, reliability (QoS), integrity, security
Ranging (no infrastructure) | Device-to-Device Distance & Angle of Arrival - access - paymanent (mobile & transp.) - contact tracing | very high | short payload, small duty cycles | very low to low (smartwatches, bracelet, fob,…) | costs, costs, costs… precision (cm) Integrity (security) [mostly consumer]
Localization (infrastructure) | RTLS - asset tracking - robotic, drone, UAV - trains - shopping analytics | very high | short payload, small duty cycles | very low to low (tags,…) moderate to high (anchors/infrastructure) | scalability reliability precision (cm) [mostly industrial]
Sensing | Sensing - mono- or bi-static radars - presence/obstacle detection - gesture/context detection | proximity | no payload, small duty cycles ? | ? | costs precision (mm, larger BW) reliability (safety app. ?) [consumer & industrial]
Data streaming | Real time streaming - audio (headphones) | moderate | continuous payload, larger duty cycles | very low to low (headphone, in-ear devices, ...) | ? [consumer]
 | - AR with multi-channel a/v | proximity ? | continuous payload, larger duty cycles | moderate to high (AR glasses, ...) ? | ? [consumer]

## Slide 4
Source file:
References:
https://www.ieee802.org/3/B400G/public/21_0114/healey_b400g_01_210114.pdf