## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Promising of OFDM waveform for OCC system based on rolling shutter effect
Date Submitted: March 2021
Source: Huy Nguyen, Yeong Min Jang [Kookmin University].
Contact: +82-2-910-5068 E-Mail: yjang@kookmin.ac.kr
Re:
Abstract: Promising of OFDM waveform for OCC system based on rolling shutter effect
Purpose: To discuss about the promising of OFDM waveform for OCC system based on rolling shutter effect.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
Promising of OFDM waveform for OCC system based on rolling shutter effect

## Slide 3: Introduction
Orthogonal Frequency-Division Multiplexing (OFDM) is a digital multi-carrier modulation scheme that is employed in broadband wired and wireless communication as an effective solution with Inter-Symbol Interference (ISI) caused by a multipath channel.
In Light Fidelity (Li-Fi), the OFDM waveform is well-known and frequently implemented; however, the use of OFDM technology with Optical Camera Communication (OCC) is new technology.
[1] has been discussed the potential of using OFDM waveform in Optical Camera Communication system. These advantages of using OFDM waveform in OCC system can be summarized as follow.

## Slide 4: Advantages of using OFDM waveform in OCC system (1)
OFDM waveform can reduce Inter-Symbol Interference
Multipath: In the real environment, the light source can be reflected from water, terrestrial object. From that, the camera receives many versions of signal causing ISI.
Blur phenomenon. The blur phenomenon also is the main cause of ISI; one pixel affects another pixel then one OFDM symbol will be interfered by another symbol causing ISI. With adding a cyclic prefix, ISI will be mitigated if the maximum delay time is less than the guard interval.

## Slide 5: Advantages of using OFDM waveform in OCC system (2)
In an OCC system, the trouble of complex noise (blur image, interference, irregular attenuation) is difficult within the time domain but can be easily resolved in the frequency domain by ignoring the DC-component.
OFDM waveform support high-speed data for Optical Camera Communication system

## Slide 6: Rolling shutter OFDM scheme
Block diagram of Architecture of Rolling Shutter-OFDM system
Unlike the conventional OFDM in Radio Frequency, instead of feeding the data symbol directly into the IDFT block, each symbol must pass through the Hermitian block.

## Slide 7: Data structure of Rolling Shutter OFDM scheme
Proposed data frame structure for Rolling Shutter-OFDM system
To support the compatibility of frame rate variation, every packet can contain many sub-packets, and each sub-packet in the same packet has the same data payload with a Sequence Number (SN).
The SN represents the serial number of packets.

## Slide 8: Rolling Shutter OFDM waveform

## Slide 9: Rolling Shutter OFDM demonstration
Video demo

## Slide 10
[1] Huy Nguyen, Thieu Minh Duc, Trang Nguyen, and Yeong Min Jang, “Rolling OFDM for Image Sensor Based Optical Wireless Communication,” IEEE Photonics Journal, Volume 11, Issue 4.
References