## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [15.4aa JRE modulation and channel parameters Proposal - CID1 and 2]
Date Submitted: [17th June,2021]
Source: [Takashi Kuramochi] Company [LAPIS TECHNOLOGY]
Address [2-4-8 Shinyokohama,Kouhoku-ku,Yokohama 222-8575 Japan]
Voice:[+81-45-476-9295], FAX: [], E-Mail:[kuramochi722@lapis-tech.com]
Re: [] Abstract: [This document contains technical proposals for modulation and channel parameters] Purpose: [information]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: 802.15.4-2020 Table 19-8[1]
Band Designation (MHz) | Parameter | Operating mode (Table19-8) |  |  |  |  |  |  |  |  | 
 |  | #1 | #2 | #3 | #4 | #5 |  |  |  |  | 
920 | Data rate(kb/s) | 50 | 100 | 200 | 400 | - |  |  |  |  | 
 | Modulation | 2-FSK | 2-FSK | 2-FSK | 4-FSK | - |  |  |  |  | 
 | Modulation index | 1.0 | 1.0 | 1.0 | 0.33 | - |  |  |  |  | 
 | Channel spacing(kHz) | 200 | 400 | 600 | 600 | - |  |  |  |  | 
(1) The Term “Channel separation” is used to calculate channel frequency.

## Slide 3: Current extension in D07 (Table19-8/Table19-9a) [2]
Band Designation (MHz) | Parameter | Operating mode (Table19-8) |  |  |  |  | Operating mode (Table19-9a) |  |  |  | 
 |  | #1 | #2 | #3 | #4 | #5 | #6 | #7 | #8 |  | 
920 | Data rate(kb/s) | 50 | 100 | 200 | 400 | 400 | 600 | 600 | 800 |  | 
 | Modulation | 2-FSK | 2-FSK | 2-FSK | 4-FSK | 2-FSK | 2-FSK | 4-FSK | 4-FSK |  | 
 | Modulation index | 1.0 | 1.0 | 1.0 | 0.33 | 0.5 | 0.4 | 0.5 | 0.33 |  | 
 | Channel spacing(kHz) | 200 | 400 | 600 | 600 | 1000(1) | 1000(1) | 1000(1) | 1000(1) |  | 
(1) The Term “Channel separation” is used to calculate channel frequency.

## Slide 4: Proposed extensions to Table19-8/Table19-9a to resolve CID 1,2 of 15-21-0332-00-04aa [3]
Band Designation (MHz) | Parameter | Operating mode (Table19-8) |  |  |  |  | Operating mode (Table19-9a) |  |  |  | 
 |  | #1 | #2 | #3 | #4 | #5 | #6 | #7 | #8 | #9 | #10
920 | Data rate(kb/s) | 50 | 100 | 200 | 400 | - |  |  |  |  | 
 | Modulation | 2-FSK | 2-FSK | 2-FSK | 4-FSK | - |  |  |  |  | 
 | Modulation index | 1.0 | 1.0 | 1.0 | 0.33 | - |  |  |  |  | 
 | Channel spacing(kHz) | 200 | 400 | 600 | 600 | - |  |  |  |  | 
920-c | Data rate(kb/s) | 50 | 100 | 150 | 200 | 300 | 400 | 400 | 600 | 600 | 800
 | Modulation | 2-FSK | 2-FSK | 2-FSK | 2-FSK | 2-FSK | 4-FSK | 2-FSK | 2-FSK | 4-FSK | 4-FSK
 | Modulation index | 1.0 | 1.0 | 0.5 | 1.0 | 0.5 | 0.33 | 0.5 | 0.4 | 0.5 | 0.33
 | Channel spacing(kHz) | 200 | 400 | 400 | 600 | 400 | 400 | 1000(1) | 1000(1) | 1000(1) | 1000(1)
920-d | Data rate(kb/s) | 50 | 100 | 150 | 200 | 300 | 400 | 400 | 600 | 600 | 800
 | Modulation | 2-FSK | 2-FSK | 2-FSK | 2-FSK | 2-FSK | 4-FSK | 2-FSK | 2-FSK | 4-FSK | 4-FSK
 | Modulation index | 1.0 | 1.0 | 0.5 | 1.0 | 0.5 | 0.33 | 0.5 | 0.4 | 0.5 | 0.33
 | Channel spacing(kHz) | 200 | 400 | 400 | 600 | 600 | 600 | 1000(1) | 1000(1) | 1000(1) | 1000(1)
Newly added
(1) The Term “Channel separation” is used to calculate channel frequency.

## Slide 5: Reference
[1]IEEE Std 802.15.4-2020
[2] P802.15.4aa-D7
[3] 15-21-0332-00-04aa - 802.15.4aa D07 Recirculation Letter Ballot Consolidated Comments(LB185)