## Slide 1
Project: IEEE P802.15 Working Group for Wireless Specialty Networks
Submission Title: Coordinator-to-coordinator communication for Body Area Networks
Date Submitted: November 16th, 2021
Source: Minsoo Kim1, Takumi Kobayashi1,2, Marco Hernandez1, Ryuji Kohno1,2
Company: 1Yokosuka Research Park International Alliance Institute (YRP-IAI), Japan; 2Yokohama National University (YNU), Japan
Address: 1YRP 1, 3-4 Hikarino-oka, Yokosuka, 239-0847 Japan; 279-5 Tokiwadai, Hodogaya-ku, Yokohama, 240-8501 Japan
Voice: 2+81-90-5408-0611, Fax: 2+81-45-383-5528, E-Mail:[minsoo@minsookim.com; kobayashi-takumi-ch@ynu.ac.jp, Marco.Hernandez@ieee.org; kohno@ynu.ac.jp]
Re: In response to call for technical contributions
Abstract: This document contains a discussion of coordinator-to-coordinator communication to realize the enhanced reliability of P802.15.6a.
Purpose: Material for discussion in P802.15.6a TG
Notice: This document has been prepared to assist the IEEE P802.15.6a. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.6a.

## Slide 2: Coordinator-to-coordinator communication for Body Area Networks
Minsoo Kim1, Takumi Kobayashi1,2,
Marco Hernandez1, Ryuji Kohno1,2
1Yokosuka Research Park International Alliance Institute (YRP-IAI)
2Yokohama National University (YNU)

## Slide 3: Coordinator-to-coordinator communication
Coordinator-to-coordinator (C2C) communication is performed through a link between BAN Coordinators, separate from links between a BAN Coordinator and BAN Nodes.
To avoid complexity, it would be preferable to use the same PHY as the link between a BAN Coordinator and BAN Nodes.
BAN
Node
BAN
Node
BAN
Coordinator
BAN
Node
BAN
Node
BAN
Node
BAN
Coordinator
BAN
Node
Link between Coordinators
to talk to each other

## Slide 4: Need for C2C communication
Interference and collisions in dense situations
  Links between coordinators can be utilized to control channel access between 2 or more BANs to reduce collisions and interference, especially in situations where BANs are densely located.
Support for various use cases
BAN
Node
BAN
Node
BAN
Coordinator
BAN
Node
BAN
Node
BAN
Node
BAN
Coordinator
BAN
Node
desired signal
desired signal
collision
interference

## Slide 5: Possible Scenarios of C2C
Vehicle BAN and Human BANs inside the vehicle (n <= 5)
  As passengers are in the confined space, the probability of collision and the need for interference management increase.
  If a star topology is applied, Vehicle BAN can be a super-coordinator and perform central management.
  A Vehicle BAN coordinator may support up to 5 Human BAN coordinators for a passenger vehicle, such as sedan, pickup, SUV, utility vehicle.
Human BAN
Coordinator
Vehicle BAN
Coordinator
Human BAN
Coordinator

## Slide 6: Possible Scenarios of C2C
Vehicle BAN and Human BANs around the vehicle
  A link between a VBAN coordinator and a HBAN coordinator outside the vehicle can also be useful in various situations.
    When approaching a pedestrian who is a family member
    When authenticating the owner of a car
Human BAN Coordinator
Human BAN
Coordinator
Vehicle BAN
Coordinator
Human BAN
Coordinator

## Slide 7: Possible Scenarios of C2C
Vehicle BAN and Human BANs inside the vehicle (n > 5)
  For a van or a bus that can accommodate more than 5 people, its Vehicle BAN should be able to accommodate more Human BANs. (for instance, up to 15 Human BAN coordinators)
  The coverage area of the Vehicle BAN should also be considered along with the size of the vehicle.
HC
HC
HC
HC
HC
HC
HC
HC
Vehicle BAN Coordinator
HC: Human BAN Coordinator

## Slide 8: Possible Scenarios of C2C
Vehicle BAN and Human BANs inside the vehicle (n > 5)
  Larger vehicles can be covered by grouping Human BANs.
  Handover may be introduced, considering the similarity with the cellular network.
HC
HC
HC
HC
HC
HC
HC
HC
Vehicle BAN Coordinator #1
HC: Human BAN Coordinator
Vehicle BAN Coordinator #2

## Slide 9: Possible Scenarios of C2C
Multiple Human BANs
  A star topology may be undesirable.
    Unlike the case of Vehicle BAN, it is difficult to determine a super-coordinator, because there is no superiority or inferiority between Human BANs.
    Even if a super-coordinator is selected, it cannot cover the wider area of multiple Human BANs.
Human BAN
Coordinator
Human BAN
Coordinator
Human BAN
Coordinator
Human BAN
Coordinator
Human BAN
Coordinator

## Slide 10: Possible Scenarios of C2C
Multiple Human BANs
  If there is no Vehicle BAN, peer-to-peer (P2P) communication is the only option.
    However, distributed control increases complexity and communication overhead.
    If peer-to-peer communication should be employed, it should be limited to BAN Coordinators, excluding links between BAN Coordinator and BAN Nodes, to reduce overheads.
    Careful considerations are required.

## Slide 11: Possible Scenarios of Handovers
Handover of Human BAN nodes
  Human BAN nodes may be handed over from its Human BAN Coordinator to a Vehicle BAN Coordinator, when its user approaches or boards the vehicle.
VBAN Coordinator
HBAN Coordinator
HBAN Node
HBAN Coordinator
HBAN Node
HBAN Coordinator
HBAN Node
Before: HBAN Node ↔ HBAN Coordinator
After: HBAN Node ↔ VBAN Coordinator

## Slide 12: Possible Scenarios of Handovers
Handover of Human BAN coordinators
  Human BAN coordinators may be handed over from a Vehicle BAN Coordinator to another Vehicle BAN Coordinator, when its user moves on a bus.
HC
HC
HC
Vehicle BAN Coordinator #1
HC: Human BAN Coordinator
Vehicle BAN Coordinator #2
Before: HBAN Coordinator ↔ VBAN Coordinator #1
After: HBAN Coordinator ↔ VBAN Coordinator #2

## Slide 13: Topologies of the Described Scenarios
A dependable network can be built through flexible configuration according to the use cases and QoS control with priority order.
Standalone HBANs
HBAN
Node
1
1..*
HBAN
Coordinator
P2P
Around a user
HBANs inside/around of a vehicle in coordination with a VBAN
P2P
HBAN
Node
HBAN
Coordinator
VBAN
Node
VBAN
Coordinator
1
1..*
0..1
0..*
1
1..*
Inside of a vehicle
HBAN
Node
HBAN
Coordinator
0..1
0..*
1
1..*
HBANs inside/around of a vehicle in deep coordination with a VBAN
(HBAN nodes inside a vehicle are handed over to a VBAN coordinator)
P2P
HBAN
Node
HBAN
Coordinator
VBAN
Node
VBAN
Coordinator
1
1..*
0..1
0..*
0
0..*
Inside of a vehicle
HBAN
Node
HBAN
Coordinator
0..1
0..*
1
1..*

## Slide 14: Detecting other BANs
Special time periods reserved for coordinator-to-coordinator communication may be required in a superframe.
It should be also noted that Vehicle BAN and Human BAN have different mobility characteristics.
  Vehicle BAN coordinators and nodes are fixed on the vehicle, while Human BAN coordinators and nodes are mobile around a vehicle.

## Slide 15: Summary
Coordinator-to-coordinator (C2C) communication is proposed, especially to reduce collisions and interference in situations where BANs are densely located, for instance in a passenger bus.
Both Human BAN and Vehicle BAN are based on the same BAN standard, while Human BAN is mainly for healthcare purpose and in/on/around the human body and Vehicle BAN is for a feedback control loop and in/on/around the vehicle body. Being the same standard also allows interactive sensing and control between the human body and the vehicle.
Scenarios representing several use cases in which multiple Human BANs and/or Vehicle BAN are densely located are presented.
A 2-layer star topology was suggested for a scenario where a Vehicle BAN and Human BANs coexist, and a peer-to-peer topology where only same types of BANs coexist.
We need careful consideration of the mentioned topologies, and how to detect other BANs.

## Slide 16: Thank you for your attention!