## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: UWB channel access aided by pilot narrow band radio
Date Submitted: 11 November, 2021
Source: Huan-Bang Li, Takeshi Matsumura (NICT, Japan)
Address: 3-4 Hikarino-oka, Yokosuka-shi, Kanagawa, 239-0847 Japan
E-Mail: {lee, matsumura}@nict.go.jp
Abstract: Discussion on cooperated UWB and NB radio for enhancing CCA.
Purpose: To improve coexistence between UWB systems.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the authoring individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The authors(s) reserve(s) the right to add, amend or withdraw material contained herein.

## Slide 2
PAR Objective | Proposed Solution (how addressed)
Safeguards so that the high throughput data use cases will not cause significant disruption to low duty-cycle ranging use cases | Effective and efficient CCA reduce disruption between UWB devices
Interference mitigation techniques to support higher density and higher traffic use cases | Use NB radio as pilot to enable effective and efficient CCA to improve coexistence
Other coexistence improvement | 
Backward compatibility with enhanced ranging capable devices (ERDEVs) | 
Improved link budget and/or reduced air-time | 
Additional channels and operating frequencies | 
Improvements to accuracy / precision / reliability and interoperability for high-integrity ranging | 
Reduced complexity and power consumption | 
Hybrid operation with narrowband signaling to assist UWB | Exploiting pilot NB PHY and concurrent operation with UWB to assist UWB channel access
Enhanced native discovery and connection setup mechanisms | 
Sensing capabilities to support presence detection and environment mapping | 
Low-power low-latency streaming | 
Higher data-rate streaming allowing at least 50 Mbit/s of throughput | 
Support for peer-to-peer, peer-to-multi-peer, and station-to-infrastructure protocols | 
Infrastructure synchronization mechanisms | 

## Slide 3: Contents
Background
UWB channel access aided by pilot narrow band radio
  Fully concurrent pilot (FCP)
  Partially concurrent pilot (PCP)
Mapping pilot multiple carriers
Conclusions

## Slide 4: Background
With penetration of portable UWB devices, requirement on coexistence between UWB systems (either same or different UWB PHYs) increases. Effective and efficient channel access control becomes important.
In 802.15.4-2020, a compliant UWB PHY is required to perform CCA when accessing UWB channels with one of six CCA modes*.
However, UWB is of extremely low PSD feature (noise-like). On one hand, energy sense or CSMA sense may play quite limited role. On another hand, preamble sense may increase complexity or be time consuming.
*CCA Mode 1: Energy above threshold.
CCA Mode 2: Carrier sense only.
CCA Mode 3: Carrier sense with energy above threshold.
CCA Mode 4: ALOHA.
CCA Mode 5: HRP UWB preamble sense based on the SHR of a frame.
CCA Mode 6: HRP UWB preamble sense based on the packet with the multiplexed
preamble as specified in 15.6.

## Slide 5: UWB channel access aided by pilot narrow band radio
Assumption:
A compliant device include a UWB PHY (UWB-PHY) and a pilot narrow band PHY (pilot-NB-PHY ) that are operated in cooperative manner, at least, with synchronized clock or same MAC timer.
The UWB-PHY and the pilot-NB-PHY are concurrently controlled by cooperative/unified MAC.

## Slide 6: UWB channel access aided by pilot narrow band radio
Proposals:
Send a pilot-NB signal as an indicator whenever UWB signal is transmitted.
Perform CCA using pilot-NB-PHY against pilot NB signal instead of using UWB-PHY against UWB signal.
The CCA results obtained by pilot-NB-PHY are concurrently shared with UWB-PHY.
UWB-PHY access UWB channel based on the shared pilot-NB-PHY’s CCA results.

## Slide 7: Mode P1: Fully concurrent pilot (FCP)
When accessing channel, the pilot-NB-PHY of a compliant device shall perform CCA at first.
As long as the pilot-NB-PHY senses a busy channel (pilot signal from other compliant pilot-NB-PHYs are sensed), both UWB-PHY and pilot-NB-PHY of the compliant device shall not contend channel.
If the pilot-NB-PHY senses an idle channel, it can contend channel for obtaining access right.
When channel access right is contended, the UWB-PHY and the pilot-NB-PHY execute fully concurrent transmission, i.e., start and stop of transmission from the two PHYs are fully synchronized.

## Slide 8: Illustration of Mode P1
Mode P1 is favorable for UWB transmission with low duty cycle or short UWB task duration.
Different “UWB tasks” may need different time durations for transmission. Duration of transmission can be pre-determined in relation with UWB task.
time
UWB
task
TX
UWB
task
TX
UWB
task
TX
Pilot
TX
Pilot
TX
Pilot
TX
TX signal
CCA
CCA
CCA

## Slide 9: Control flow of Mode P1
CCA Req.
clear channel report
Pilot-NB-PHY MAC UWB-PHY
CCA
Start-send Command
Start-send Command
Task completion report
Pilot-NB-PHY-send*
UWB-PHY-send*
*Transmission duration can be pre-determined in relation with UWB task.

## Slide 10: Mode P2: Partially concurrent pilot (PCP)
When accessing channel, the pilot-NB-PHY of a compliant device shall perform CCA for a time period not smaller than the maximum UWB task duration with additional alpha.
Once the pilot-NB-PHY senses a busy channel, both UWB-PHY and pilot-NB-PHY of the compliant device shall not contend channel for a period of a UWB task duration.
If the pilot-NB-PHY senses an idle channel, it can contend channel to obtain access right.
When channel access right is contended, the UWB-PHY and the pilot-NB-PHY execute transmission simultaneously. However, transmission duration of the pilot-NB-PHY can be shorter than that of the UWB-PHY.

## Slide 11: Illustration of Mode P2
UWB
task x
TX
UWB
task y
TX
UWB
task z
TX
time
Pilot TX Pilot TX Pilot TX
TX signal
CCA
CCA
CCA
Mode P2 is favorable for applications where execution of “UWB tasks” needs long time duration.
The time duration needed by a UWB task can be pre-determined and aware to compliant devices.

## Slide 12: Control flow of Mode P2
CCA Req.
clear channel report
Pilot-NB-PHY MAC UWB-PHY
CCA
Start-send Command
Start-send Command
Task-end report
Pilot-NB-send*
UWB-PHY-send*
*UWB-PHY-send can start simultaneously or with a pre-determined time interval to the pilot-NB-send.

## Slide 13: Illustration of channel access with Mode P2
UWB
task slot
t1
time
Pilot NB
device
D1
device
D2
device
D3
UWB
task slot
Pilot sensed
UWB
Task slot
NB-ref
Pilot NB
Pilot sensed
Pilot sensed
Pilot sensed
t2
t3
keepclear
UWB
task slot
t1
Pilot NB
UWB
task slot
Pilot sensed
t2
Pilot NB
keepclear
keepclear
keepclear
keepclear
no access request
no access request

## Slide 14: Mapping pilot multiple carriers (1)
Assumption:
The pilot-NB-PHY can send a pilot with multiple-carrier signal (MC-pilot) selected from a NB carrier bank of f1, f2, … , fk.
The transmitted multiple carriers of MC-pilot are recognizable through either energy detection or CSMA sensing.
frequency
f1 f2 fk
…
MC-pilot

## Slide 15
frequency
fi fj
Mapping multiple carriers:
Form a multiple carriers group for the purpose of indicating UWB channels (MCG-ch). Each element in the MCG-ch corresponds to a single specified UWB channel.
Form a multiple carriers group for the purpose of indicating UWB task durations (MCG-td). Each element in the MCG-td corresponds to a pre-determined duration to execute a UWB task.
Mapping pilot multiple carriers (2)

## Slide 16: Pros and Cons of using pilot NB radio
Pros:
Avoid the difficulties of sensing UWB signal. No need to touch into preamble.
Unified structure and procedure are available. No matter different UWB systems are involved or not.
Exploit legacy CCA methods (energy detection, CSMA sense, etc.) and benefit from their effectiveness and efficiency .
Cons:
Need additional management of NB PHY.

## Slide 17: Conclusions
Use concurrent pilot NB radio to perform CCA for facilitating UWB channel access.
Fully concurrent pilot or partially concurrent pilot can be used in accordance to UWB frameworks.
Multiple carriers of a pilot can be mapped as indicators corresponding to either UWB channels and/or time duration to execute UWB tasks.
Common CCA procedure for different UWB frameworks.