## Slide 1
Project: IEEE P802.15 Working Group for Wireless Speciality Networks (WSN)
Submission Title: Draft channel plan of 500-GHz fixed wireless system
Date Submitted: 11 March 2022
Source: Atsushi KANNO, NICT, Japan
Nobuhiko SHIBAGAKI and Kenichi KASHIMA, Hitachi Kokusai Electric Inc.
Address 4-2-1 Nukui-kitamachi, Koganei, Tokyo, 184-8795, Japan
Voice:+81423276876, FAX: +81423277938, E-Mail: kanno@nict.go.jp
Re: n/a
Abstract: Draft channel and bandwidth plans of 500-GHz fixed wireless system is proposed.
Purpose: Proposal of 500-GHz fixed wireless access for discussion in future THz standardization.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Draft channel plan of 500-GHz fixed wireless access
Atsushi KANNO, NICT
Nobuhiko SHIBAGAKI, HIKE
Kenichi KITAYAMA, HIKE

## Slide 3: Introduction
Ultra high-definition camera-based surveillance system is highly demanded in smart industry and public transportation.
Typically, the camera and monitor is connected via 100GbE wireline.
When the monitor or camera set in moving vehicle, wireless connection without the beam forming technique is implemented without any spectrum interference in short-distance (<100 m) link.
>450GHz fixed wireless system (FWS) with a capacity greater than 100 Gbps is a possible solution with high-gain antenna.
We propose a draft channel plan of 500-GHz FWS.

## Slide 4: Application use case
Short and secure wireless link as an FWS.
UHD video transmission between station and vehicles in smart factory with low latency.
  Surveillance with tap&pinch feature without optical zoom/swing.
Mobile operation station
8K Camera
Moving crane truck

## Slide 5: Possible block diagram
Oscillator
x9 multiplier
High-speed Switch
Transmitter
High-gain antenna
Bandpass filter
Receiver
IF LNA
Detector
LNA
High-gain antenna
Bandpass filter
Data (OOK, PAM4)
THz link
Data (OOK, PAM4)

## Slide 6: Example link budget of 500-GHz FWS
 | Items | Symbol | Unit | Min. | Typ | Max | Note
Tx | Frequency | Tf | GHz | 475 | 540 | 675 | 
 | Power | Tp | dBm | -2.6 | -2.6 | -2.6 | 
 | Bandwidth | Tb | GHz | 100 | 100 | 100 | 100Gbps in BPSK
 | Noise figure | TNF | dB | 14 | 14 | 14 | Expected
 | Thermal noise | KBTF | dBm | -49.9 | -49.9 | -49.9 | 10Log(Tb)+TNF-114
Link | Distance | d | km | 0.1 | 0.03 | 0.1 | 
 | Antenna gain (Tx/Rx) | TRG | dBi | 48 | 48 | 48 | 
 | Atmospheric attenuation | A | dB | 5.5 | 12.0 | 3.9 | Calculated with d and the values from AMATERASU* model in NICT
 | Propagation loss | L | dB | 125 | 116.7 | 129.1 | 
 | Estimated received power | UR1 | dBm | -38.2 | -27.7 | -39.6 | Tp+TRG+TRG-L
Rx | Required CNR | C/N | dB | 10 | 10 | 10 | Expected (BPSK)
 | Minimum received power | UR2 | dBm | -39.9 | -39.9 | -39.9 | C/N+KBTF
 | Margin | R | dB | 1.7 | 4.6 | 0.2 | UR1-UR2
* P. Baron, J. Mendrok, Y. Kasai,S. Ochiai, T. Seta, K. Sagi, K. Suzuki, H. Sagawa, and J. Urban, “AMATERASU: Model for Atmospheric TeraHertz Radiation Analysis and Simulation, Journal of the National Institute of Information and Communications Technology, 55(1), 109-121 (2008).

## Slide 7: Draft bandwidth plan
462.24GHz
BW=103.68GHz
562.24GHz
BW=51.84GHz
BW=51.84GHz
BW=25.92GHz
BW=25.92GHz
BW=25.92GHz
BW=25.92GHz
8.64GHz (4x2.16-GHz bandwidth, based on IEEE802.15.3d), not used in this configuration

## Slide 8: Draft channel plan
Channel number | 25.92 GHz BW | 51.84 GHz BW | 103.68 GHz BW | Unit
1 | 475.2 |  |  | GHz
9 |  | 488.16 |  | GHz
2 | 501.12 |  |  | GHz
13 |  |  | 514.08 | GHz
3 | 527.04 |  |  | GHz
10 |  | 540 |  | GHz
4 | 552.96 |  |  | GHz
5 | 578.88 |  |  | GHz
11 |  | 591.84 |  | GHz
6 | 604.8 |  |  | GHz
14 |  |  | 617.76 | GHz
7 | 630.72 |  |  | GHz
12 |  | 643.68 |  | GHz
8 | 656.64 |  |  | GHz
475.2
501.12
527.04
552.96
578.88
604.8
630.72
656.64
488.16
514.08
540
591.84
617.76
643.68
462.24
565.92
669.6
These channels may not be available for huge H2O absorption in the air

## Slide 9: Possible modulation formats
Channel BW (GHz) | Modulation format | Expected line rate (Gbps)
25.92 | OOK/BPSK | 25.51
51.84 | OOK/BPSK | 51.43
103.68 | OOK/BPSK | 103.27
25.92 | PAM4/QPSK | 51.02
51.84 | PAM4/QPSK | 102.86
103.68 | PAM4/QPSK | 206.54
Chip rate will be less than 25.51, 51.43, and 103.27 Gchips/s for 25.92, 51.84, and 103.68-GHz channels, respectively.
Coding rate (1/2, 3/4, …) will be discussed later.
ASK-based modulation (OOK, PAM4) is considered for the implementation of IEE802.3-based Ethernet frame format.

## Slide 10: Conclusion
We introduced 500-GHz FWS for wireless connection as a short and secure UHD camera link.
We proposed a draft channel plan of 500-GHz FWS for the realization of 100 Gbps or more.