## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Use Cases of UWB sensing proxy application in 802.15.4ab]
Date Submitted: []
Source: [Kuan Wu, David Xun Yang, Xiaohui Peng, Bin Qian] Company [Huawei Technologies]
Re: [Input to the Working Group]
Abstract: [Sensing Proxy application, Use Cases , UWB in 802.15.4ab]
Purpose: []
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
PAR Objective | Proposed Solution (how addressed)
Safeguards so that the high throughput data use cases will not cause significant disruption to low duty-cycle ranging use cases | 
Interference mitigation techniques to support higher density and higher traffic use cases | 
Other coexistence improvement | 
Backward compatibility with enhanced ranging capable devices (ERDEVs) | 
Improved link budget and/or reduced air-time | 
Additional channels and operating frequencies | 
Improvements to accuracy / precision / reliability and interoperability for high-integrity ranging | 
Reduced complexity and power consumption | 
Hybrid operation with narrowband signaling to assist UWB | 
Enhanced native discovery and connection setup mechanisms | 
Sensing capabilities to support presence detection and environment mapping | Use cases of UWB sensing proxy application in 802.15.4ab
Low-power low-latency streaming | 
Higher data-rate streaming allowing at least 50 Mbit/s of throughput | 
Support for peer-to-peer, peer-to-multi-peer, and station-to-infrastructure protocols | Support of peer-to-peer, peer-to-multi-peer protocols
Infrastructure synchronization mechanisms | 

## Slide 3
Introduction
UWB sensing proxy application is introduced in [1], where the use cases for proxy in 802.15.4ab need further discussion
In this contribution, we discuss potential use cases for UWB sensing proxy application

## Slide 4
Re-cap of UWB sensing proxy application [1]
Requesting
device
Initiator/Rx
Responder/Tx
Sensing request
Sensing packet
OTA CIR measurement report
    Mode A
Object
Initiator/Tx
Responder/Rx
Requesting
device
    Mode B
UWB sensing proxy application: a device can request the OTA CIR measurement report for sensing while not being initiator or responder
  Mode A: Initiator is the sensing receiver, responders are sensing transmitters
  Mode B: Initiator is the sensing transmitter, responders are sensing receivers
Object

## Slide 5
Re-cap of ranging role structure in 802.15.4z [2]
In multi-node ranging, a ranging procedure typically involves the roles of controller, controlee, initiator and responder
The controller may not be necessarily an initiator or a responder
In DL-TDOA [3], full-blown-satellites (FBS) are controllers, battery-powered-satellites (BPS) are initiators, smart tags are responders, respectively
Observation: DL-TDOA scenarios share a similar role structure with sensing proxy. This can be a starting point for discussing UWB sensing proxy use cases. In the following, sensing mode A is used for illustration convenience.

## Slide 6
Use Case 1
    FBS are the sensing requesting devices
    BPS are the sensing initiators/responders
    Directly re-using the DL-TDOA role structure with minimized modifications
Requesting
device
Initiator/Rx
Responder/Tx
FBS
BPS
BPS
Object
Sensing request
Sensing packet
OTA CIR measurement report

## Slide 7
Use Case 2
    Smart tags are the sensing requesting devices
    BPS are the sensing initiators/responders
    Coordination between BPS and smart tags may be needed, e.g. device discovery, synchronization and etc.
Sensing request
Sensing packet
OTA CIR measurement report
Initiator/Rx
Responder/Tx
Object
Smart tag
Requesting
device
BPS
BPS

## Slide 8
Use Case 3
    Smart tags/FBS are the requesting devices
    BPS are the sensing initiators/responders
    A hierarchical proxy structure where FBS serves as primary proxy and BPS serves as secondary proxy, respectively
    Coordination between BPS and smart tags may be needed, e.g. device discovery, synchronization and etc.
Requesting
device
Initiator/Rx
Responder/Tx
FBS
BPS
BPS
Object
Sensing request
Sensing packet
OTA CIR measurement report
Smart tag
Requesting
device

## Slide 9
Use Case 4
    FBS/BPS are the sensing requesting devices
    Smart tags are the sensing initiators/responders
Requesting
device
Initiator/Rx
Responder/Tx
FBS/BPS
Object
Sensing request
Sensing packet
OTA CIR measurement report
Smart tag
Smart tag

## Slide 10
Use Case 5
    Smart tags/FBS are the sensing requesting devices
    Smart tags are the sensing initiators/responders
    A hierarchical proxy structure where FBS serves as primary proxy and BPS serves as secondary proxy, respectively
Requesting
device
FBS/BPS
Object
Sensing request
Sensing packet
OTA CIR measurement report
Smart tag
Requesting
device
Smart tag
Smart tag
Initiator/Rx
Responder/Tx

## Slide 11
March 2022
Use Case 6
    Smart tags can be the sensing requesting devices, sensing initiators/responders
    Infrastructure is not directly involved in sensing measurement processes
    A device-to-device (D2D) sensing application scenario
Initiator/Rx
Responder/Tx
Object
Smart Tag
Smart Tag
Smart Tag
Sensing request
Sensing packet
OTA CIR measurement report
Requesting
device

## Slide 12
March 2022
Summary
Scenarios | Requesting device | Initiator | Responder | Comments
Use Case 1 | FBS | BPS | BPS | Re-use the DL-TDOA role structure with minimized modifications
Use Case 2 | Smart tags | BPS | BPS | Coordination between infrastructure and smart tags
Use Case 3 | Smart tags/FBS | FBS | BPS | 
Use Case 4 | FBS/BPS | Smart tags | Smart tags | Coordination between infrastructure and smart tags Smart tags introduce extra flexibility in extending sensing range Full flexibility regardless of infrastructure deployment in Use Case 6
Use Case 5 | Smart tags | Smart tags | Smart tags | 
Use Case 6 | Smart tags | Smart tags | Smart tags | 
Some proposals may be needed for further study
Support for discovery between smart devices and devices/infrastructure
Infrastructure may provide assistance for smart devices such as channel resource management support, synchronization and etc., especially in Use Case 6 of D2D scenario
Support for efficient signaling designs to allow flexible operations between infrastructure and smart devices
Coexistence designs between sensing proxy and DL-TDOA/UL-TDOA/TWR
Kuan Wu, Huawei

## Slide 13
Conclusion
In this contribution, we identified several potential uses cases for UWB sensing proxy application
Protocol designs on sensing proxy application to address the aforementioned use cases

## Slide 14
References
[1]. Pooria Pakrooh, Bin Tian, Steve Shellhammer, Koorosh Akhavan, UWB Sensing Scenarios for 802.15.4ab, 15-22-0012-02-04ab-uwb-sensing-scenarios-for-802-15-4ab, January 2022
[2]. IEEE Standard for Low-Rate Wireless Networks–Amendment 1: Enhanced Ultra Wideband (UWB) Physical Layers (PHYs) and Associated Ranging Techniques, IEEE Standard 802.15.4z-2020 (Amendment to IEEE Standard 802.15.4-2020), IEEE SA, pp. 1–174, Aug. 25, 2020
[3]. Jean-Marie André, Sven Zeisberg, DL-TDOA positioning TDMA scheme, 15-21-0530-00-04ab-dl-tdoa-positioning-tdma-scheme, October 2021