## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [UWB Channel Usage Coordination for better UWB Coexistence]
Date Submitted: [Sep, 2022]
Source: Lochan Verma, Robert Golshan, Yong Liu [Apple]
Mingyu Lee, Taeyoung Ha, Aniruddh Rao Kabbinale [Samsung]
Wolfgang Kuchler, Riku Pirhonen, Frank Leong [NXP]
E-Mail: [lochan_verma, rgolshan, yong_liu9] @apple.com
[mg0218.lee, ty1115.ha, aniruddh.rao]@samsung.com,
[wolfgang.kuechler, riku.pirhonen, frank.leong]@nxp.com
Abstract: Proposal for UWB channel usage coordination for better UWB coexistence
Purpose:
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
PAR Objective | Proposed Solution (how addressed)
Safeguards so that the high throughput data use cases will not cause significant disruption to low duty-cycle ranging use cases | UWB channel usage coordination
Interference mitigation techniques to support higher density and higher traffic use cases | UWB channel usage coordination
Other coexistence improvement | UWB channel usage coordination
Backward compatibility with enhanced ranging capable devices (ERDEVs) | 
Improved link budget and/or reduced air-time | 
Additional channels and operating frequencies | 
Improvements to accuracy / precision / reliability and interoperability for high-integrity ranging | 
Reduced complexity and power consumption | 
Hybrid operation with narrowband signaling to assist UWB | 
Enhanced native discovery and connection setup mechanisms | 
Sensing capabilities to support presence detection and environment mapping | 
Low-power low-latency streaming | 
Higher data-rate streaming allowing at least 50 Mbit/s of throughput | 
Support for peer-to-peer, peer-to-multi-peer, and station-to-infrastructure protocols | 
Infrastructure synchronization mechanisms | 

## Slide 3: Background
UWB transmitters being good neighbors to each other is very desirable
Coordination of UWB CH (Channel) usage is one method to facilitate better coexistence between UWB transmitters
4ab yields two UWB transceiver types, NBA (Narrow Band Assisted) UWB transceiver and UWB standalone transceiver
Mirror Channel [1] is a good direction to coordinate UWB CH usage amongst NBA UWB transceivers [2]
Here, we describe a UWB CH usage coordination method that is usable by both standalone UWB and NBA UWB transceivers

## Slide 4: Outline
UWB CH Usage Coordination proposal
  Design Principals
  Details
  Key observations

## Slide 5: Design Principals for UWB CH Usage Coordination Method
Method usable by standalone UWB transceivers and NBA UWB transceivers
Coordination method signaling should be decoupled from other UWB sessions on this (standalone / NBA) UWB transceiver
Support of coordination method signaling is optional for (standalone / NBA) UWB transceivers
  Transmission of coordination signaling optional
  Acting on information received from coordination method signaling is optional

## Slide 6: Proposed Approach for UWB CH Usage Coordination (1/2)
Both standalone UWB and NBA UWB Initiator periodically transmit UWB-AP (Acquisition Packet) on a pre-defined UWB Discovery CH
UWB-AP carries information useful to determine all future UWB CH usage of this Initiator
Both standalone UWB and NBA UWB transceivers discover this Initiator by receiving UWB-AP
UWB-AP Interval is configurable (e.g., depending upon use case)

## Slide 7: Proposed Approach for UWB CH Usage Coordination (2/2)
UWB Rx scan for UWB-AP is optimized in NBA UWB transceivers
NBA UWB Initiator periodically transmit NB-AP on a pre-defined NB Discovery CH
NB-AP carries information useful to determine occurrence of the next immediate UWB-AP
NB-AP may carry information useful to determine all future UWB CH usage of this Initiator
NB-AP Interval is related to UWB-AP Interval

## Slide 8: Properties of UWB-AP
Packet type: BPRF Data Packet (STS Packet Config 0, HRP ERDEV PPDU)
Preamble: pre-defined (spec can reserve at least one preamble for UWB-AP)
UWB Discovery CH: pre-defined
MAC HDR UWB-AP: SRC address of transmitter, broadcast DST address, etc.
MAC Payload UWB-AP: ‘UWB CH Usage Info’ such as
  Relative offset to the next ranging round
  Ranging round length
  Ranging round interval
  UWB CH information
  Preamble codes
  Round Usage, etc.
Format of HRP ERDEV PPDU

## Slide 9: Properties of NB-AP
Packet type: O-QPSK packet (e.g., 250 Kbps modulated O-QPSK packet)
NB Discovery CH: pre-defined
MAC Payload NB-AP
  Relative offset to the next immediate UWB-AP
  UWB-AP preamble selection
  UWB-AP CH
  Optional: UWB CH Usage Info (see previous slide)
Format of O-QPSK PPDU

## Slide 10: Coordination Zone Area
Different signaling PHYs have disparate range due to difference in transmit power and minimum receiver sensitivity
UWB-AP (UWB BPRF Data) allows this (standalone / NBA) UWB Initiator to coordinate UWB CH usage with other strong UWB Initiators
Including UWB CH Usage info in the NB-AP (O-QPSK) provides this NBA UWB Initiator an extended coordination zone
Plot using Link budget analysis in [3]
TxPwr O-QPSK = 14 dBm [3]
TxPwr NBA-MMS and UWB BPRF = -7.8 dBm [3]

## Slide 11: Key Observations on Proposed Approach
Item | Observation
1 | Transmit of UWB-AP is mandatory if the UWB CH Usage Coordination method is implemented. This allows UWB standalone transceivers to coordinate UWB CH usage with another UWB standalone transceiver and NBA UWB transceiver.
2 | Transmit of NB-AP is mandatory if UWB CH Usage Coordination method is implemented AND NB is used for NB assisted UWB operation. This allows NBA UWB transceivers to optimize their UWB Rx scan window for UWB-AP acquisition.
3 | UWB-AP Interval value is out of scope of 4ab. It depends upon several factors including application type and device type.

## Slide 12: Summary
UWB CH usage coordination for better UWB coexistence is nice to have
In these slides we presented UWB CH usage coordination method that is usable by both standalone UWB and NBA UWB transceivers

## Slide 13: References
[1] 15-22-0276-02-04ab, Details on Mirroring Channel
[2] 15-22-0262-01-4ab, NBA-UWB Technical Framework Proposal
[3] 15-22-0074-00-04ab, Link Budget Analysis for NBA-UWB