## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Evaluation of IEEE 802.15.6ma Ultra-wideband Physical Layer Utilizing Super Orthogonal Convolutional Code]
Date Submitted: [14 January 2025]
Source: [Kento Takabayashi1, Ryuji Kohno2,3 ] [1;Toyo University, 2;Yokohama National University, 3;YRP International Alliance Institute(YRP-IAI)]
Address [1: 2100 Kujirai, Kawagoe, Saitama, Japan 351-8585, Japan 719-1197,
2; 79-5 Tokiwadai, Hodogaya-ku, Yokohama, Japan 240-8501,
3; YRP1 Blg., 3-4 HikarinoOka, Yokosuka-City, Kanagawa, 239-0847 Japan]
Voice:[1; +81-866-94-2104, 2: +81-90-5408-0611],
Email:[1: takabayashi.kento.xp@gmail.com, 2:kohno@ynu.ac.jp]
Re: []
Abstract: [The performance of an IEEE 802.15.6ma ultra-wideband physical layer utilizing super orthogonal convolutional codes is evaluated. These slides may offer opportunity to discuss on revision for a dependable physical layer technology of a new standard IEEE802.15.6ma.] Purpose: [The discussion will lead definition and requirement of current ongoing research and development on dependable wireless networks.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein. Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
Notes: doc.: IEEE 802.15-09-0117-00-0007
<month year>

## Slide 2
Evaluation of IEEE 802.15.6ma Ultra-wideband Physical Layer Utilizing Super Orthogonal Convolutional Code
January 2025,
Hybrid Session ,
Kobe Covention Center - Kobe, Japan
Kento Takabayashi1, Ryuji Kohno2,3
1. Toyo University, Japan
2. Yokohama National University, Japan
3. YRP International Alliance Institute, Japan

## Slide 3: Motivation and Aim of study
UWB is a promising technology that may satisfy the requirements of IoMT
IEEE 802.15.6 UWB PHY has limited transmission output and requires to ensure dependability
New consideration is given to the application of Super Orthogonal Convolutional Codes (SOCC) as a technique for improving dependability for higher priority case
We perform evaluation when SOCC is applied at the IEEE 802.15.6 UWB PHY, and confirm the effectiveness of these combinations
Notes: SOCCs have attracted attention as error correction codes for code division multiple access (CDMA) using the spread spectrum
Therefore, SOCCs are considered to be compatible with the UWB, as they use a very wide bandwidth

## Slide 4: SOCC
Fig. SOCC encoder
SOCC is a kind of orthogonal convolutional code of very low coding rate
The encoder is composed of K length shift registers (constraint length) and a block orthogonal (Hadamard) encoder
The coding rate is given by
The decoder uses the Viterbi algorithm
Notes: The inner (K- 2) bit memories are mapped into one Walsh sequence of length (two to the power of K-2)
The two outer bits are added to each binary number of the selected Walsh sequence by exclusive OR
One divided by two to the power of K-2
Therefore, SOCCs are considered to be compatible with the UWB, as they use a very wide bandwidth
The inner (K- 2) bit memories are mapped into one Walsh sequence of length 2^(𝐾−2) (two to the power of K-2)
The two outer bits are added to each binary number of the selected Walsh sequence by exclusive OR
One divided by two to the power of K-2

## Slide 5: Bit erasure channel
0 1 1 0 0 1 0 0 1・・・0 1 1 1 ✕ ✕ ✕ ✕ ✕ ✕ ・・・0 1 1 0 0 0 1 1
Consecutive bit erasures,
Bit erasure channel is assumed, which simulate asynchronous interference from another system
It is assumed that consecutive bit erasures of up to % of the length of PSDU occur
is uniformly distributed in the interval [0 ]

## Slide 6: Evaluation
Channel model | AWGN, Bit erasure
Bandwidth () | 499.2 MHz
Center Frequency | 3993.6 MHz
Modulation | BPSK
Transmission power () | 0 dBm
Thermal noise density () | -174 dBm/Hz
Implementation losses () | 3 dB
Receiver noise figure () | 5 dB
FEC | IEEE802.15.4ab BCC, LDPC (R=1/2) SOCC (K=3~6)
Decoding algorism | SOVA (BCC, SOCC), Belief propagation (LDPC)
PSDU data rate | 125 Mbps
Maximum number of retransmissions () | 3
PSDU length () | 1296 bits
Maximum erasure ratio () | 80%
Slot length | 1.0 ms
Channel model | AWGN, Bit erasure
 | 499.2 MHz
Center Frequency | 3993.6 MHz
Modulation | BPSK
 | -174 dBm/Hz
 | 3 dB
 | 5 dB
FEC | IEEE802.15.4ab BCC, LDPC (R=1/2) SOCC (K=3~6)
Decoding algorism | SOVA (BCC, SOCC), Belief propagation (LDPC)
PSDU data rate | 125 Mbps
 | 3
 | 1296 bits
 | 80%
Slot length | 1.0 ms
4. Evaluation
Table. Simulation Parameters

## Slide 7: Results
Packet error ratio as a function of in the case of 15.4ab BCC, LDPC, and SOCC with random inter-leaver, %
Notes: SOCC with random inter-leaver had a very good performance.
Especially, low-rate case had better in low EsN0 area.

## Slide 8: Results
PSDU throughput as a function of in the case of 15.4ab BCC, LDPC, and SOCC with random inter-leaver, %
Notes: Low-rate SOCCs had a less performance than other case, but at least 7.8Mbps or more can be achieved.
SOCC with random inter-leaver also had a good performance in low 𝐸_𝑏/𝑁_0 areas.

## Slide 9: Results
Average delay as a function of in the case of 15.4ab BCC, LDPC, and SOCC with random inter-leaver, %
Notes: In addition, low-rate SOCCs also achieves low delay and retransmission count even in low areas.
This is an advantage over HARQ with BCC.
In addition, low-rate SOCCs also achieves low delay and retransmission count even in low 𝐸_𝑏/𝑁_0 areas.
This is an advantage over HARQ with BCC.

## Slide 10: Conclusion
Numerical results showed that SOCC with random inter-leaver had a very good performance
Low-rate SOCCs had a less performance than other case, but at least 7.8Mbps or more can be achieved
In addition, low-rate SOCCs also achieves low delay (several ms) and retransmission count even in low areas
  This is an advantage over HARQ with BCC
  SOCC may be effective in applications that require low latency and dependability

## Slide 11: Reference
Kento Takabayashi, Hirokazu Tanaka, Katsumi Sakakibara, "Evaluation of Wireless Body Area Network Utilizing Super Orthogonal Convolutional Code," in Proceedings of 2019 International Symposium on Intelligent Signal Processing and Communication Systems (ISPACS 2019), Beitou, Taipei, Taiwan, pp.1-2, Dec. 2019.
Kento Takabayashi, Hirokazu Tanaka, Katsumi Sakakibara, "Toward Dependable Internet of Medical Things: IEEE 802.15.6 Ultra-Wideband Physical Layer Utilizing Superorthogonal Convolutional Code," Sensors, 2022, vol. 22, no. 6, 2172, Mar. 2022.

## Slide 12
12
Thank you for your attention ! ! !
* This research was funded by JSPS Grant-in-Aid for Early-Career Scientists Grant Number JP20K14737

## Slide 13: Results
Packet error ratio as a function of in the case of 15.4ab BCC, LDPC, and SOCC with random inter-leaver, %
Notes: SOCC with random inter-leaver had a very good performance.
Especially, low-rate case had better in low EsN0 area.

## Slide 14: Results
PSDU throughput as a function of in the case of 15.4ab BCC, LDPC, and SOCC with random inter-leaver, %
Notes: Low-rate SOCCs had a less performance than other case, but at least 7.8Mbps or more can be achieved.
SOCC with random inter-leaver also had a good performance in low 𝐸_𝑏/𝑁_0 areas.

## Slide 15: Results
Average delay as a function of in the case of 15.4ab BCC, LDPC, and SOCC with random inter-leaver, %
Notes: In addition, low-rate SOCCs also achieves low delay and retransmission count even in low areas.
This is an advantage over HARQ with BCC.
In addition, low-rate SOCCs also achieves low delay and retransmission count even in low 𝐸_𝑏/𝑁_0 areas.
This is an advantage over HARQ with BCC.